## Slide 1
FRC ROBOT SOFTWARE
The finished command-based
robot implementation
Four passes: physical robot, software structure, runtime behavior, and code traces
PASS 1
↓
PASS 2
↓
PASS 3
↓
PASS 4
WPILib 2026.2.1
2020 FRC robot | command-based implementation
01
Notes: The presentation revisits the complete robot four times. Pass 1 introduces the physical robot and operator controls. Pass 2 maps that robot to RobotContainer, commands, subsystems, and Trigger bindings. Pass 3 explains the TimedRobot loop and CommandScheduler behavior. Pass 4 traces real inputs through the checked-in code to physical outputs.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/docs/final-implementation-presentation-architecture.md
- C:/Users/dmona/.codex/attachments/9b367a0a-b3b8-45c0-a3fa-dc3de4f5d67b/pasted-text.txt
[/Sources]

## Slide 2
PASS 1: PHYSICAL ROBOT
Four subsystems share the CommandScheduler
Each subsystem encapsulates separate hardware, so commands for different subsystems can run concurrently.
Drive
4 Talon motor controllers
Default command
Ball belt
1 Talon motor controller
Trigger.whileTrue bindings
Scoring roller
1 Talon motor controller
Trigger.whileTrue binding
Climber
2 double solenoids
Trigger.onTrue binding
RobotContainer constructs the subsystems. CommandScheduler schedules their commands.
2020 FRC robot | command-based implementation
02
Notes: The four subsystems are DriveSubsystem, BeltSubsystem, RollerSubsystem, and ClimberSubsystem. Each encapsulates its hardware objects and exposes methods used by commands.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/Subsystem.html
[/Sources]

## Slide 3
PASS 1: PHYSICAL ROBOT
The software map follows the robot's actuator wiring
PWM connects the motor controllers. The roboRIO communicates with CTRE PCM 0 over CAN.
Mechanism
Actuator
Connection / channel
Left drivetrain
2 PWM Talons
PWM 0 and 1
Right drivetrain
2 PWM Talons
PWM 3 and 2
Ball belt
1 PWM Talon
PWM 5
Scoring roller
1 PWM Talon
PWM 4
Climber
2 DoubleSolenoid objects
CAN ID 0; solenoid channels 0/1 and 2/3
2020 FRC robot | command-based implementation
03
PWM outputs 0-9
NI roboRIO | WPILib documentation
Notes: The roboRIO sends PWM signals directly to the Talon motor controllers. It communicates with CTRE PCM module 0 over the CAN bus; the two DoubleSolenoid objects use PCM channel pairs 0/1 and 2/3. The right drivetrain motor pair is inverted once inside DriveSubsystem.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
- https://docs.wpilib.org/en/2020/docs/getting-started/getting-started-frc-control-system/control-system-hardware.html
[/Sources]

## Slide 4
PASS 1: PHYSICAL ROBOT
Two Xbox controllers separate driving from mechanism control
The driver owns tank drive; the operator owns the belt, roller, and climber.
USB 0
Driver Xbox
Left stick Y
Left drive output
Right stick Y
Right drive output
MODE
Slow drive
Right bumper
Hold for 0.4 scale
Release for 0.8 scale
Driver control only
USB 1
Operator Xbox
A Belt in
B Belt out
X Roller
Y Climber
Two CommandXboxController instances keep driver and operator bindings distinct.
2020 FRC robot | command-based implementation
04
Notes: The driver CommandXboxController is on USB 0 and supplies both tank-drive Y axes plus the right-bumper slow mode. The operator CommandXboxController is on USB 1: A runs the belt inward, B runs it outward, X runs the roller, and Y schedules the climber command.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 5
PASS 2: SOFTWARE STRUCTURE
Subsystems define how; commands define when
RobotContainer connects operator input to commands, and the scheduler controls when those commands run.
1
Controllers
Axes and buttons
2
RobotContainer
Objects and bindings
3
Commands
Scheduled behavior
4
Subsystems
Hardware ownership
5
WPILib hardware classes
Talon and DoubleSolenoid
CommandScheduler polls triggers, runs scheduled commands, and enforces subsystem requirements.
2020 FRC robot | command-based implementation
05
Notes: - RobotContainer creates the Xbox controllers, subsystems, default drive command, and controller bindings.
- The controllers provide driver axes and button states. RobotContainer connects those inputs to commands.
- CommandScheduler polls the Trigger bindings, schedules or cancels commands, and enforces subsystem requirements.
- Commands define when an action runs. They call methods on the subsystem they require.
- Subsystems encapsulate the robot hardware and define how each mechanism operates.
- WPILib hardware classes produce the final outputs: Talon objects use roboRIO PWM channels, while DoubleSolenoid objects communicate through the CAN-connected PCM.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/CommandScheduler.html
[/Sources]

## Slide 6
PASS 2: SOFTWARE STRUCTURE
RobotContainer assembles the live robot once
robotInit() constructs the container, which creates controllers, subsystems, camera capture, default commands, and Trigger bindings.
STARTUP PATH
public void robotInit() {
robotContainer = new RobotContainer();
}
public RobotContainer() {
driverController = new CommandXboxController(
Constants.Operator.DRIVER_CONTROLLER);
operatorController = new CommandXboxController(
Constants.Operator.OPERATOR_CONTROLLER);
driveSubsystem = new DriveSubsystem();
climberSubsystem = new ClimberSubsystem();
beltSubsystem = new BeltSubsystem();
rollerSubsystem = new RollerSubsystem();
CameraServer.startAutomaticCapture(0);
configureDefaultCommands();
configureBindings();
}
After construction
Each hardware object is encapsulated by one subsystem.
The drive default command is ready.
Trigger bindings are configured.
The USB camera is streaming.
2020 FRC robot | command-based implementation
06
Notes: - robotInit() runs once when the robot program starts and creates the single RobotContainer.
- RobotContainer creates the two CommandXboxController objects, four subsystem objects, drive-speed state, and camera connection.
- Each subsystem constructor creates the WPILib objects that represent the physical hardware, using the PWM channels, PCM module, and solenoid channels defined in Constants.
- The subsystem keeps those hardware objects private. Commands operate the robot by calling subsystem methods rather than accessing motors or solenoids directly.
- configureDefaultCommands() creates the continuous drive command and connects it to the driver-controller axis suppliers.
- configureBindings() creates the remaining command objects and connects them to the appropriate Xbox controller Trigger bindings.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Robot.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/
[/Sources]

## Slide 7
PASS 2: SOFTWARE STRUCTURE
Commands turn subsystem capabilities into robot actions
Subsystems define how hardware operates; commands define when each action runs.
1
Subsystem method
Defines a capability
2
Command
Packages one action
3
Requirements
Declare subsystem use
4
Trigger or sequence
Schedules the command
5
Scheduler
CommandScheduler runs it
A command calls subsystem methods; it does not access motors or solenoids directly.
2020 FRC robot | command-based implementation
07
Notes: - Slide 5 established that each subsystem encapsulates hardware and provides methods for operating one mechanism.
- A command packages calls to those subsystem methods into a schedulable robot action.
- This project creates commands for driving, moving the belt, running the roller, toggling the climber, and selecting slow-drive mode.
- Commands keep controller bindings separate from hardware-control details.
- Each command declares the subsystem it requires, allowing CommandScheduler to prevent conflicting actions.
- The same command can be scheduled by a controller Trigger or used later as part of an autonomous routine.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/Command.html
[/Sources]

## Slide 8
PASS 2: SOFTWARE STRUCTURE
RobotContainer states the operator interface in one place
Each Trigger binding method matches the behavior: whileTrue for held actions and onTrue for one-time actions.
RobotContainer.configureBindings()
operatorController.y()
.onTrue(new ToggleClimberArmsCommand(climberSubsystem));
operatorController.a()
.whileTrue(new BeltInCommand(beltSubsystem));
operatorController.b()
.whileTrue(new BeltOutCommand(beltSubsystem));
operatorController.x()
.whileTrue(new RollerCommand(rollerSubsystem));
driverController.rightBumper()
.whileTrue(new SlowDriveCommand(driveSpeedMode));
Read a binding as a sentence
Which controller?
Which button?
Which Trigger binding method?
Which command?
Which subsystem does it require?
2020 FRC robot | command-based implementation
08
Notes: CommandXboxController button methods return Trigger objects. RobotContainer binds operator A, B, X, and Y and driver rightBumper() directly to commands with Trigger.whileTrue or Trigger.onTrue.
[Sources]
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/button/Trigger.html
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
[/Sources]

## Slide 9
PASS 3: RUNTIME BEHAVIOR
robotPeriodic() calls CommandScheduler.run() once per robot loop
The default TimedRobot period is 20 ms, producing about 50 scheduler iterations per second.
Robot.java
@Override
public void robotPeriodic() {
CommandScheduler.getInstance().run();
}
1
Run subsystem periodic methods
2
Poll Trigger bindings; schedule or cancel commands
3
Execute scheduled commands
4
Check completion and call end(...)
5
Schedule default commands
Commands must return promptly so CommandScheduler.run() can finish each iteration.
2020 FRC robot | command-based implementation
09
Notes: - This project follows the standard WPILib Java structure: Robot extends TimedRobot, which provides the robot's periodic execution loop.
- By default, the WPILib robot library calls robotPeriodic() every 20 milliseconds, or about 50 times per second.
- Each call to robotPeriodic() calls CommandScheduler.run(), producing one scheduler iteration.
- During an iteration, the scheduler runs subsystem periodic methods, polls Trigger bindings, and schedules or cancels commands.
- It then executes scheduled commands, ends commands that have finished or were canceled, and schedules default commands for available subsystems.
- Command methods must return promptly. A blocking method prevents the scheduler from completing that robot-loop iteration.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Robot.java
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj/TimedRobot.html
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/CommandScheduler.html
[/Sources]

## Slide 10
PASS 3: RUNTIME BEHAVIOR
Commands run one step per scheduler iteration
The lifecycle separates setup, repeated work, completion, and cleanup.
initialize()
Once when scheduled
↓
execute()
Once per scheduler iteration
↓
isFinished()
Checked after execution
↓
end(interrupted)
Once on finish or cancellation
false
Remain scheduled; execute again.
finished or canceled
Call end(false) or end(true).
A loop that never returns blocks CommandScheduler.
2020 FRC robot | command-based implementation
10
Notes: - initialize() runs once when the scheduler starts the command.
- execute() runs once during each scheduler iteration and calls the required subsystem methods.
- isFinished() tells the scheduler whether the command has completed.
- If isFinished() returns false, the command remains scheduled and executes again during the next iteration.
- end(false) runs after normal completion, while end(true) runs after cancellation or interruption.
- Cleanup belongs in end(). The belt and roller commands stop their motors there.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/Command.html
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/button/Trigger.html
[/Sources]

## Slide 11
PASS 3: RUNTIME BEHAVIOR
Requirements keep competing commands off the same hardware
Commands requiring different subsystems may run concurrently.
Subsystem
Commands that require it
Scheduler result
DriveSubsystem
DriveTeleopCommand
Scheduled by default when DriveSubsystem is available
BeltSubsystem
BeltInCommand, BeltOutCommand
Only one command requiring BeltSubsystem can be scheduled
RollerSubsystem
RollerCommand
Can run concurrently with belt commands
ClimberSubsystem
ToggleClimberArmsCommand
No other command requiring ClimberSubsystem can run concurrently
addRequirements(subsystem) adds a subsystem requirement. A field reference does not add that requirement.
2020 FRC robot | command-based implementation
11
Notes: Belt commands require BeltSubsystem. RollerCommand requires RollerSubsystem, so the scheduler may run a belt command and RollerCommand concurrently. It will not schedule two commands that require BeltSubsystem at the same time.
[Sources]
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/Command.html
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/
[/Sources]

## Slide 12
PASS 3: RUNTIME BEHAVIOR
The default command turns two Xbox stick axes into tank-drive outputs
A 0.08 deadband filters stick drift; holding the right bumper changes the scale from 0.8 to 0.4.
DriveTeleopCommand.java
public void execute() {
driveSubsystem.drive(
scale(leftDriveSupplier.getAsDouble()),
scale(rightDriveSupplier.getAsDouble()));
}
private double scale(double joystickValue) {
double driveScale = driveSpeedMode.isSlow()
? Constants.Tuning.SLOW_DRIVE_SCALE
: Constants.Tuning.NORMAL_DRIVE_SCALE;
return joystickValue * driveScale;
}
USB 0 left Y
Left output
USB 0 right Y
Right output
Right bumper
0.4 scale while held
2020 FRC robot | command-based implementation
12
Notes: DriveTeleopCommand requires DriveSubsystem and does not finish on its own. CommandScheduler schedules it as the subsystem's default command whenever no other scheduled command requires DriveSubsystem.
[Sources]
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/Subsystem.html
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/DriveTeleopCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/SlowDriveCommand.java
[/Sources]

## Slide 13
PASS 3: RUNTIME BEHAVIOR
Trigger.whileTrue starts a command on true and cancels it on false
The command continues because isFinished() returns false; cancellation calls end(true).
Button
Command
Output while held
Release behavior
Operator A
BeltInCommand
BeltSubsystem.run(+1.0)
Cancel command, then stop PWM 5
Operator B
BeltOutCommand
BeltSubsystem.run(-1.0)
Cancel command, then stop PWM 5
Operator X
RollerCommand
RollerSubsystem.run(+1.0)
Cancel command, then stop PWM 4
SHARED COMMAND PATTERN
execute() -> subsystem.run(speed)
isFinished() -> false
end(true) -> subsystem.stop()
2020 FRC robot | command-based implementation
13
Notes: BeltInCommand and BeltOutCommand compete for BeltSubsystem. RollerCommand uses RollerSubsystem, so it can run with either belt command.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltOutCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/RollerCommand.java
[/Sources]

## Slide 14
PASS 3: RUNTIME BEHAVIOR
Trigger.onTrue schedules once when Y becomes active
initialize() toggles both DoubleSolenoid objects; isFinished() then returns true.
ToggleClimberArmsCommand.java
@Override
public void initialize() {
climberSubsystem.toggleArms();
}
@Override
public boolean isFinished() {
return true;
}
State transition
Retracted
⇄
Extended
Startup assumption
The code starts with armsExtended = false. The physical arms must begin retracted.
2020 FRC robot | command-based implementation
14
Notes: The operator controller's Y method returns a Trigger. Trigger.onTrue schedules ToggleClimberArmsCommand when the condition changes from false to true, so holding Y does not repeatedly schedule it.
[Sources]
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/button/Trigger.html
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/ToggleClimberArmsCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
[/Sources]

## Slide 15
PASS 4: CODE TRACES
Driver stick input reaches the drivetrain through six steps
The default command repeats this path on every scheduler iteration.
1
Driver Xbox
Left Y and right Y
2
Default command
Scheduled when drive is free
3
Scheduler
Executes every iteration
4
Drive command
Reads axes and scales
5
Drive subsystem
drive(left, right)
6
Four Talons
PWM 0-3 drive motors
Continuous
No requirement conflict -> default command stays scheduled -> execute() repeats next iteration
2020 FRC robot | command-based implementation
15
Notes: - The driver Xbox controller supplies the left-stick and right-stick Y-axis values.
- DriveTeleopCommand is the default command for DriveSubsystem, so CommandScheduler schedules it whenever the subsystem is available.
- On each scheduler iteration, execute() reads both axis suppliers and applies the active normal or slow scale.
- DriveTeleopCommand calls DriveSubsystem.drive(left, right).
- DriveSubsystem sends the two values to four Talon objects on PWM channels 0 through 3.
- The right motor pair is inverted once inside DriveSubsystem so positive input drives both sides forward.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/DriveTeleopCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
[/Sources]

## Slide 16
PASS 4: CODE TRACES
Operator A reaches the belt motor through six explicit steps
Every step can be located in the checked-in Java source.
1
Operator Xbox
A becomes true
2
Trigger
whileTrue schedules
3
Scheduler
Checks requirements
4
Command
execute() runs
5
Subsystem
run(+1.0)
6
Talon
PWM 5 drives belt
Release
A false -> cancel -> end(true) -> beltSubsystem.stop() -> PWM 5 output becomes zero
2020 FRC robot | command-based implementation
16
Notes: The operator A Trigger schedules BeltInCommand through whileTrue. BeltInCommand remains scheduled because isFinished() returns false. When A becomes false, the Trigger cancels the command and CommandScheduler calls end(true), which stops BeltSubsystem.
[Sources]
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/button/Trigger.html
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
[/Sources]

## Slide 17
PASS 4: CODE TRACES
Operator Y reaches both climber solenoids through six steps
The command completes after one state change.
1
Operator Xbox
Y becomes true
2
Trigger
onTrue schedules
3
Scheduler
Checks requirements
4
Command
initialize() toggles
5
Climber subsystem
toggleArms()
6
Solenoids
PCM channels 0/1 and 2/3
Completion
isFinished() returns true -> end(false) -> command is removed; the PCM holds the selected state
2020 FRC robot | command-based implementation
17
Notes: - Operator Y becomes active on the operator Xbox controller.
- The onTrue binding schedules ToggleClimberArmsCommand once on the false-to-true transition.
- CommandScheduler checks the ClimberSubsystem requirement before scheduling the command.
- initialize() calls ClimberSubsystem.toggleArms() once.
- ClimberSubsystem changes both DoubleSolenoid objects between forward and reverse states.
- The DoubleSolenoid objects address CTRE PCM module 0 on channel pairs 0/1 and 2/3; the PCM communicates with the roboRIO over CAN.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/ToggleClimberArmsCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
[/Sources]

## Slide 18
PASS 4: CODE TRACES
Each responsibility has one clear home
Follow the same path when reading, testing, or debugging any robot action.
1
Start with the hardware
Identify the hardware object and the subsystem that encapsulates it.
2
Find the binding
Locate the controller input and Trigger binding method.
3
Read the command
Check requirements, lifecycle methods, and completion.
4
Trace the output
Follow the subsystem method to the WPILib hardware object.
CommandScheduler coordinates commands; each subsystem encapsulates its own hardware.
2020 FRC robot | command-based implementation
18
Notes: Close by repeating the concrete reading path rather than summarizing the development process.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/
[/Sources]