## Slide 1
FRC ROBOT SOFTWARE
The finished command-based
robot implementation
Hardware, operator controls, subsystem ownership, commands, and the scheduler loop
INPUT
↓
COMMANDS
↓
SUBSYSTEMS
↓
HARDWARE
WPILib 2026.2.1
2020 FRC robot | command-based implementation
01
Notes: This deck describes the checked-in implementation as a working system. It does not cover the history of how the code reached this structure.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/
- C:/Users/dmona/Downloads/Blueprint_to_Codebase.pdf
[/Sources]

## Slide 2
SYSTEM OVERVIEW
Four control domains share one command scheduler
Each domain owns separate hardware, so the driver can operate several mechanisms at once.
Drive
4 Talon motor controllers
Default command
Ball belt
1 Talon motor controller
Held commands
Scoring roller
1 Talon motor controller
Held command
Climber
2 double solenoids
One-shot command
RobotContainer constructs the domains. CommandScheduler coordinates them.
2020 FRC robot | command-based implementation
02
Notes: The four domains align with DriveSubsystem, BeltSubsystem, RollerSubsystem, and ClimberSubsystem.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 3
HARDWARE
The software map follows the robot's actuator wiring
PWM channels drive the motors. PCM module 0 controls both climber cylinders.
Mechanism
Actuator
Channel
Implementation detail
Left drivetrain
2 PWM Talons
PWM 0 and 1
One output is sent to both motors
Right drivetrain
2 PWM Talons
PWM 3 and 2
The right pair is inverted in software
Ball belt
1 PWM Talon
PWM 5
Positive output moves the belt inward
Scoring roller
1 PWM Talon
PWM 4
Runs independently from the belt
Climber
2 DoubleSolenoids
PCM 0, ports 0/1 and 2/3
Both cylinders change position together
2020 FRC robot | command-based implementation
03
Notes: The right drivetrain motor pair is inverted once inside DriveSubsystem. Belt and roller use distinct PWM channels and distinct subsystems.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
[/Sources]

## Slide 4
OPERATOR CONTROLS
Two Xbox controllers separate driving from mechanism control
The driver owns tank drive; the operator owns the belt, roller, and climber.
USB 0
Driver Xbox
Left stick Y
Left drive output
Right stick Y
Right drive output
MODE
Slow drive
Right bumper
Hold for 0.4 scale
Release for 0.8 scale
Driver control only
USB 1
Operator Xbox
A Belt in
B Belt out
X Roller
Y Climber
Two named controller objects keep driver and operator bindings distinct.
2020 FRC robot | command-based implementation
04
Notes: The revised operator mapping is roller 2, climber 3, belt in 4, and belt out 5. Slow drive remains button 2 on USB port 0.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
[/Sources]

## Slide 5
SOFTWARE ARCHITECTURE
Subsystems define how; commands define when
RobotContainer connects operator input to commands, and the scheduler controls when those commands run.
1
Controllers
Axes and buttons
2
RobotContainer
Objects and bindings
3
Commands
Scheduled behavior
4
Subsystems
Hardware ownership
5
WPILib HAL
PWM and pneumatics
CommandScheduler controls timing and subsystem access between the middle layers.
2020 FRC robot | command-based implementation
05
Notes: RobotContainer is the composition root. Commands depend on subsystems, while subsystems depend on WPILib hardware classes.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 6
STARTUP
RobotContainer assembles the live robot once
robotInit() constructs the container, which then creates controls, subsystems, camera capture, defaults, and bindings.
STARTUP PATH
public void robotInit() {
robotContainer = new RobotContainer();
}
public RobotContainer() {
driverController = new CommandXboxController(
Constants.Operator.DRIVER_CONTROLLER);
operatorController = new CommandXboxController(
Constants.Operator.OPERATOR_CONTROLLER);
driveSubsystem = new DriveSubsystem();
climberSubsystem = new ClimberSubsystem();
beltSubsystem = new BeltSubsystem();
rollerSubsystem = new RollerSubsystem();
CameraServer.startAutomaticCapture(0);
configureDefaultCommands();
configureBindings();
}
After construction
Every actuator has exactly one subsystem owner.
The drive default command is ready.
Button triggers are registered.
The USB camera is streaming.
2020 FRC robot | command-based implementation
06
Notes: Construction happens once during robot initialization. The scheduler later uses the registered defaults and triggers.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Robot.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 7
SCHEDULER
robotPeriodic() advances the command system once per robot packet
The normal TimedRobot period is 20 ms, which produces about 50 scheduler passes per second.
Robot.java
@Override
public void robotPeriodic() {
CommandScheduler.getInstance().run();
}
1
Run subsystem periodic methods
2
Poll buttons and triggers
3
Schedule and cancel commands
4
Execute active commands
5
Check completion and call end
6
Start defaults on free subsystems
Every command must return promptly so the scheduler can run the rest of the robot.
2020 FRC robot | command-based implementation
07
Notes: The scheduler runs on the robot thread. A blocking loop inside execute prevents later scheduler work from running.
[Sources]
- https://docs.wpilib.org/en/latest/docs/software/commandbased/command-scheduler.html
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Robot.java
[/Sources]

## Slide 8
COMMAND LIFECYCLE
Commands run one small step on each scheduler pass
The lifecycle separates setup, repeated work, completion, and cleanup.
initialize()
Once when scheduled
↓
execute()
Once per scheduler pass
↓
isFinished()
Checked after execution
↓
end(interrupted)
Once on finish or cancellation
false
Stay scheduled and execute again.
true or canceled
Call end(interrupted) once.
A loop that never returns stops the scheduler.
2020 FRC robot | command-based implementation
08
Notes: Held commands return false from isFinished and rely on trigger cancellation. The one-shot climber command returns true after initialize.
[Sources]
- https://docs.wpilib.org/en/latest/docs/software/commandbased/commands.html
[/Sources]

## Slide 9
SUBSYSTEM OWNERSHIP
Requirements keep competing commands off the same hardware
Commands on different subsystems may run together because they do not compete for the same resource.
Subsystem
Commands that require it
Scheduler result
DriveSubsystem
DriveTeleopCommand
Runs as the default whenever drive is free
BeltSubsystem
BeltInCommand, BeltOutCommand
Only one belt direction can own the motor
RollerSubsystem
RollerCommand
May run at the same time as the belt
ClimberSubsystem
ToggleClimberArmsCommand
The toggle has exclusive access while it runs
addRequirements(subsystem) declares ownership. Saving a subsystem in a field only gives the command access to it.
2020 FRC robot | command-based implementation
09
Notes: The belt and roller are separate scheduler resources, so intake and scoring mechanisms may operate concurrently.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/
[/Sources]

## Slide 10
DRIVING
The default command turns two Xbox stick axes into tank-drive outputs
A 0.08 deadband filters stick drift; holding the right bumper changes the scale from 0.8 to 0.4.
DriveTeleopCommand.java
public void execute() {
driveSubsystem.drive(
scale(leftDriveSupplier.getAsDouble()),
scale(rightDriveSupplier.getAsDouble()));
}
private double scale(double joystickValue) {
double driveScale = driveSpeedMode.isSlow()
? Constants.Tuning.SLOW_DRIVE_SCALE
: Constants.Tuning.NORMAL_DRIVE_SCALE;
return joystickValue * driveScale;
}
USB 0 left Y
Left output
USB 0 right Y
Right output
Right bumper
0.4 scale while held
2020 FRC robot | command-based implementation
10
Notes: DriveTeleopCommand requires DriveSubsystem and never finishes on its own. WPILib schedules it whenever the drive subsystem is unclaimed.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/DriveTeleopCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/SlowDriveCommand.java
[/Sources]

## Slide 11
BELT AND ROLLER
whileTrue converts a held button into continuous motor output
Press schedules the command. Release cancels it, and end() stops the motor.
Button
Command
Output while held
Release behavior
Operator A
BeltInCommand
BeltSubsystem.run(+1.0)
Cancel command, then stop PWM 5
Operator B
BeltOutCommand
BeltSubsystem.run(-1.0)
Cancel command, then stop PWM 5
Operator X
RollerCommand
RollerSubsystem.run(+1.0)
Cancel command, then stop PWM 4
SHARED COMMAND PATTERN
execute() -> subsystem.run(speed)
isFinished() -> false
end(...) -> subsystem.stop()
2020 FRC robot | command-based implementation
11
Notes: BeltInCommand and BeltOutCommand compete for BeltSubsystem. RollerCommand uses RollerSubsystem, so it can run with either belt command.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltOutCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/RollerCommand.java
[/Sources]

## Slide 12
CLIMBER
onTrue performs one pneumatic state change per button press
Operator Y schedules the command once; initialize() toggles both cylinders and then finishes.
ToggleClimberArmsCommand.java
@Override
public void initialize() {
climberSubsystem.toggleArms();
}
@Override
public boolean isFinished() {
return true;
}
State transition
Retracted
⇄
Extended
Startup assumption
The code starts with armsExtended = false. The physical arms must begin retracted.
2020 FRC robot | command-based implementation
12
Notes: Button 3 uses onTrue, so holding the button does not toggle repeatedly. Each new press changes the stored arm state once.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/ToggleClimberArmsCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
[/Sources]

## Slide 13
BINDINGS
RobotContainer states the operator interface in one place
The binding type matches the behavior: held motor action or one-time pneumatic action.
RobotContainer.configureBindings()
operatorController.y()
.onTrue(new ToggleClimberArmsCommand(climberSubsystem));
operatorController.a()
.whileTrue(new BeltInCommand(beltSubsystem));
operatorController.b()
.whileTrue(new BeltOutCommand(beltSubsystem));
operatorController.x()
.whileTrue(new RollerCommand(rollerSubsystem));
driverController.rightBumper()
.whileTrue(new SlowDriveCommand(driveSpeedMode));
Read a binding as a sentence
Which controller?
Which button?
Which trigger rule?
Which command?
Which subsystem does it require?
2020 FRC robot | command-based implementation
13
Notes: The numeric button values live in Constants.Operator. RobotContainer uses their names, so the intent remains readable after remapping.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
[/Sources]

## Slide 14
END-TO-END TRACE
Operator A reaches the belt motor through six explicit steps
Every step can be located in the checked-in Java source.
1
Operator Xbox
A becomes true
2
Trigger
whileTrue schedules
3
Scheduler
Claims BeltSubsystem
4
Command
execute() runs
5
Subsystem
run(+1.0)
6
Talon
PWM 5 drives belt
Release
A false -> cancel -> end(true) -> beltSubsystem.stop() -> PWM 5 output becomes zero
2020 FRC robot | command-based implementation
14
Notes: The input uses the revised operator button 4 mapping. BeltInCommand remains active until whileTrue cancels it on release.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
[/Sources]

## Slide 15
OPERATING MODEL
Each responsibility has one clear home
Follow the same path when reading, testing, or debugging any robot action.
1
Start with the hardware
Identify the actuator and its subsystem owner.
2
Find the binding
Locate the controller, button, and trigger rule.
3
Read the command
Check requirements, lifecycle methods, and completion.
4
Trace the output
Follow the subsystem method to the WPILib hardware object.
One scheduler coordinates the robot, but each subsystem remains responsible for its own hardware.
2020 FRC robot | command-based implementation
15
Notes: Close by repeating the concrete reading path rather than summarizing the development process.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/
[/Sources]