## Slide 1
FRC Command-Based Robot Controls
How an Xbox button becomes robot motion
1
Physical robot parts
2
Command-based rules
3
Java source files
FRC Team 2126 robot source, 2026 command-based migration
Notes: This presentation uses the current 2026 robot source as the authority. The repeated example is Operator A, which runs the belt inward.

## Slide 2
The Robot's Jobs
Start with the mechanisms students can see
02
Robot job | Mechanism | Student description
Drive | Left and right drivetrain | Moves and turns the robot with tank drive
Move game pieces | Belt | Moves balls inward or outward
Score game pieces | Roller | Runs the outtake roller
Climb | Pneumatic climber arms | Extends or retracts arms with air pressure
Robot job
Mechanism
Student description

## Slide 3
Hardware Map
Hardware IDs identify robot control points
03
Mechanism | Source object | Hardware ID | Physical function
Left drive | Talon frontLeft, follower backLeft | PWM 0, PWM 1 | Drives left side
Right drive | Talon frontRight, follower backRight | PWM 3, PWM 2 | Drives right side
Belt | Talon beltMotor | PWM 5 | Moves balls inward or outward
Roller | Talon rollerMotor | PWM 4 | Runs outtake roller
Climber arms | Two DoubleSolenoid objects | PCM CAN ID 0, channels 0/1 and 2/3 | Moves climber arms
Mechanism
Source object
Hardware ID
Physical function
Current source uses WPILib Talon PWM controllers. Newer CAN devices also use numeric IDs.

## Slide 4
Hardware Map Diagram
The roboRIO sends outputs to motor controllers and pneumatics
04
roboRIO
Left drive Talons
PWM 0 and 1
Right drive Talons
PWM 3 and 2
Belt Talon
PWM 5
Roller Talon
PWM 4
CTRE PCM CAN ID 0
Solenoid channels 0/1 and 2/3
Climber arms

## Slide 5
Two Xbox Controllers
The Driver Station USB order matters
05
USB port | Controller | Main responsibility
0 | Driver Xbox controller | Tank drive and precision drive
1 | Operator Xbox controller | Belt, roller, and climber
USB port
Controller
Main responsibility
Check the Driver Station USB tab before enabling
Driver controller must appear before operator controller

## Slide 6
Controller Map
Every active input has one job
06
Port | Controller | Input | Code path | Robot action
0 | Driver Xbox | Left stick Y | getLeftY() | Left drivetrain speed
0 | Driver Xbox | Right stick Y | getRightY() | Right drivetrain speed
0 | Driver Xbox | Right bumper | rightBumper().whileTrue(...) | Precision drive
1 | Operator Xbox | A | a().whileTrue(...) | Belt inward
1 | Operator Xbox | B | b().whileTrue(...) | Belt outward
1 | Operator Xbox | X | x().whileTrue(...) | Roller
1 | Operator Xbox | Y | y().onTrue(...) | Toggle climber arms
Port
Controller
Input
Code path
Robot action

## Slide 7
Controller Layout Diagram
Driver controls movement; operator controls mechanisms
07
Driver Xbox
USB 0
Operator Xbox
USB 1
Left stick Y
left drive
Right stick Y
right drive
Right bumper
precision drive
A
belt in
B
belt out
X
roller
Y
toggle climber

## Slide 8
Golden Trace Preview
One example connects the whole system
08
Operator presses A
Driver Station input
CommandScheduler
RobotContainer binding
BeltInCommand
BeltSubsystem -> Talon PWM 5 -> belt
The next slides unpack each step.

## Slide 9
Subsystems and Commands
Commands decide when; subsystems know how
09
Concept | What it represents | Example
Subsystem | Physical part plus hardware owner code | BeltSubsystem owns beltMotor
Command | Action that tells a subsystem what to do | BeltInCommand runs belt inward
Requirement | Lock on a subsystem while a command uses it | BeltInCommand requires BeltSubsystem
Concept
What it represents
Example
Commands decide when to act
Subsystems know how to act

## Slide 10
Why Requirements Exist
Only one command can own a subsystem at a time
10
A button
BeltInCommand
B button
BeltOutCommand
Requires
BeltSubsystem
CommandScheduler
allows one owner
Old command ends
new command runs

## Slide 11
Command Types
Button bindings use different command patterns
11
Control pattern | Code pattern | Robot example | Behavior
Hold to run | whileTrue(command) | A, B, X | Runs while held
Tap once | onTrue(command) | Y | Runs once when pressed
Always available | setDefaultCommand(command) | Drive command | Runs when subsystem is idle
State modifier | whileTrue(command) | Right bumper | Changes drive speed mode
Control pattern
Code pattern
Robot example
Behavior

## Slide 12
Command Lifecycle
The scheduler calls these methods at different times
12
Method | When it runs | Example use
initialize() | When command starts | Toggle climber arms once
execute() | Repeated while command runs | Keep belt motor running
end(interrupted) | When command stops | Stop belt motor
isFinished() | Scheduler asks if command is done | Belt returns false; climber toggle returns true
Method
When it runs
Example use

## Slide 13
The 20 ms Scheduler Loop
robotPeriodic runs the scheduler about 50 times per second
13
Poll controller inputs
Check bindings
Schedule commands
Handle conflicts
Run active commands
Stop finished commands
CommandScheduler.getInstance().run();

## Slide 14
What Happens When A Is Held
whileTrue keeps BeltInCommand scheduled
14
A button held
a().whileTrue(...)
is active
Scheduler starts
BeltInCommand
execute()
repeats
beltSubsystem.run
(BELT_SPEED)
beltMotor.set
(speed)

## Slide 15
What Happens When A Is Released
end stops the belt output
15
A button released
whileTrue no
longer active
Scheduler cancels
BeltInCommand
end(true)
runs
beltSubsystem.stop()
beltMotor.set(0)

## Slide 16
What Happens If A and B Are Pressed
The framework controls the belt conflict
16
Step | What the scheduler sees | Result
1 | A asks for BeltInCommand | BeltSubsystem gets claimed
2 | B asks for BeltOutCommand | Scheduler sees the same requirement
3 | Both require BeltSubsystem | Only one belt command can own it
4 | Scheduler interrupts previous command | Previous end(...) stops output
5 | New command runs | Belt follows the active command
Step
What the scheduler sees
Result

## Slide 17
Source File Map
Each file has a specific job
17
File | Role in the robot
Constants.java | Stores hardware IDs, controller ports, and tuning values
RobotContainer.java | Creates controllers, subsystems, default commands, and button bindings
DriveSubsystem.java | Owns drive Talons
BeltSubsystem.java | Owns belt Talon
RollerSubsystem.java | Owns roller Talon
ClimberSubsystem.java | Owns climber solenoids
commands/*.java | Defines robot actions
File
Role in the robot

## Slide 18
Constants.java
Numeric robot settings live in one place
18
Constant group | Examples | Use
Hardware | PWM_BELT = 5, PWM_ROLLER = 4 | Hardware ports and channels
Operator | DRIVER_CONTROLLER = 0, OPERATOR_CONTROLLER = 1 | Driver Station USB ports
Tuning | BELT_SPEED = 1.0, SLOW_DRIVE_SCALE = 0.20 | Speeds, scaling, deadband
Constant group
Examples
Use

## Slide 19
BeltSubsystem.java
Our helper method calls the WPILib motor API
19
private final Talon beltMotor;
public void run(double speed) {
beltMotor.set(speed);
}
public void stop() {
run(0);
}
Takeaway
Our run(...) helper calls WPILib Talon.set(...), which sends output to PWM 5.

## Slide 20
BeltInCommand.java
The command claims the belt, runs it, then stops it
20
public BeltInCommand(BeltSubsystem beltSubsystem) {
this.beltSubsystem = beltSubsystem;
addRequirements(beltSubsystem);
}
public void execute() {
beltSubsystem.run(Constants.Tuning.BELT_SPEED);
}
public void end(boolean interrupted) {
beltSubsystem.stop();
}
Method | Job
constructor | Stores subsystem and calls addRequirements
execute | Runs belt inward
end | Stops belt when released or interrupted
Method
Job

## Slide 21
RobotContainer.java
RobotContainer connects controller inputs to commands
21
driverController = new CommandXboxController(Constants.Operator.DRIVER_CONTROLLER);
operatorController = new CommandXboxController(Constants.Operator.OPERATOR_CONTROLLER);
operatorController.a()
.whileTrue(new BeltInCommand(beltSubsystem));
RobotContainer is the wiring hub
It creates controllers, creates subsystems, installs default commands, and maps buttons to commands.

## Slide 22
Full Operator A Code Trace
The same trace, now at source-code level
22
RobotContainer
configureBindings()
A button bound
to BeltInCommand
CommandScheduler
run() repeats
Scheduler calls
BeltInCommand
Our method
BeltSubsystem.run(...)
WPILib Talon.set(...)
PWM 5 belt motor

## Slide 23
Operator A Lookup Trace
Use this table while reading the code
23
Stage | File | Code item | Meaning
Binding | RobotContainer.java | operatorController.a().whileTrue(...) | A schedules command while held
Requirement | BeltInCommand.java | addRequirements(beltSubsystem) | Needs exclusive control of the belt subsystem
Motor request | BeltInCommand.java | beltSubsystem.run(...) | Calls our belt helper method
WPILib motor call | BeltSubsystem.java | beltMotor.set(speed) | Calls WPILib Talon API
Physical result | Robot wiring | PWM 5 | roboRIO sends output to belt motor
Stage
File
Code item
Meaning

## Slide 24
Other Control Traces
The same pattern repeats for the rest of the robot
24
Input | Binding | Command or read path | Result
Driver left stick Y | Default drive command | getLeftDriveValue() | Left drive output
Driver right stick Y | Default drive command | getRightDriveValue() | Right drive output
Driver right bumper | whileTrue | SlowDriveCommand | Precision drive scale
Operator B | whileTrue | BeltOutCommand | Belt runs outward
Operator X | whileTrue | RollerCommand | Roller runs
Operator Y | onTrue | ToggleClimberArmsCommand | Climber arms toggle
Input
Binding
Command or read path
Result

## Slide 25
Student Practice
Trace the code instead of guessing
25
Exercise | Prompt
1 | Trace Operator A from button press to belt motion
2 | Explain why A and B cannot both own BeltSubsystem
3 | Explain why A uses whileTrue() and Y uses onTrue()
4 | Find where belt speed is stored
5 | Find where the operator controller USB port is stored
Exercise
Prompt

## Slide 26
Extension Discussion
Small code changes start from known files
26
Question | Where to look first
How would you make belt speed slower? | Constants.Tuning.BELT_SPEED
How would you change the operator controller port? | Constants.Operator.OPERATOR_CONTROLLER
How would you add a new button command? | RobotContainer.configureBindings()
How would you make a new mechanism safe? | Create a subsystem, then require it from commands
Question
Where to look first
The command-based pattern scales because each new action has a clear owner, command, and binding.