## Slide 1
FRC ROBOT SOFTWARE
The finished command-based
robot implementation
Four questions connect the robot's jobs, subsystems, hardware, and software
ROBOT JOBS
↓
SUBSYSTEMS
↓
HARDWARE
↓
SOFTWARE
WPILib 2026.2.1
2020 FRC robot | command-based implementation
01
Notes: This presentation answers four questions in order. First, what does the robot do? Second, what are its major subsystems? Third, how does the hardware work? Fourth, how does the software identify and control each piece? The last section includes the WPILib runtime and two complete code traces because they show the software control path in operation.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/docs/final-implementation-presentation-architecture.md
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 2
1 · ROBOT JOBS
The robot drives, moves game pieces, scores, and climbs
The finished robot gives its two operators four physical functions.
Drive
Move and steer the robot
Two-stick tank drive
Ball belt
Move balls through the robot
Runs forward or backward
Scoring roller
Push balls into the goal
Runs while X is held
Climber
Raise or lower the arms
Y toggles the position
The driver controls motion. The operator controls the belt, roller, and climber.
2020 FRC robot | command-based implementation
02
Notes: - The drivetrain moves and steers the robot with tank drive.
- The ball belt moves game pieces forward or backward inside the robot.
- The scoring roller pushes game pieces out toward the goal.
- The climber changes the position of two pneumatic arms.
- The driver owns robot motion; the operator owns the three mechanisms.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/RollerSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
[/Sources]

## Slide 3
1 · ROBOT JOBS
Two Xbox controllers separate driving from mechanism control
The driver owns tank drive; the operator owns the belt, roller, and climber.
USB 0
Driver Xbox
Left stick Y
Left drive output
Right stick Y
Right drive output
MODE
Slow drive
Right bumper
Hold for 0.4 scale
Release for 0.8 scale
Driver control only
USB 1
Operator Xbox
A Belt in
B Belt out
X Roller
Y Climber
Two CommandXboxController instances keep driver and operator bindings distinct.
2020 FRC robot | command-based implementation
03
Notes: The driver CommandXboxController is on USB 0 and supplies both tank-drive Y axes plus the right-bumper slow mode. The operator CommandXboxController is on USB 1: A runs the belt inward, B runs it outward, X runs the roller, and Y schedules the climber command.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 4
2 · MAJOR SUBSYSTEMS
Four subsystems divide the robot by mechanism
Each subsystem owns the hardware objects and methods for one physical function.
Drive
4 motor controllers
drive(left, right)
Ball belt
1 motor controller
run(speed), stop()
Scoring roller
1 motor controller
run(speed), stop()
Climber
CAN module and 2 valves
toggleArms()
DriveSubsystem, BeltSubsystem, RollerSubsystem, and ClimberSubsystem each own one mechanism.
2020 FRC robot | command-based implementation
04
Notes: - The four subsystem boundaries come from physical mechanisms, not the communication bus.
- DriveSubsystem owns four motor-controller objects.
- BeltSubsystem and RollerSubsystem each own one motor-controller object.
- ClimberSubsystem owns the pneumatic device objects used by the climber.
- The 2020 implementations use PWM motor controllers and a CAN-connected PCM; current implementations can use CAN devices without changing these subsystem boundaries.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/RollerSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
[/Sources]

## Slide 5
3 · HARDWARE OPERATION
This 2020 robot uses PWM for motors and CAN for pneumatics
These connections describe this robot's installed hardware, not the command-based architecture.
Mechanism
Owned device
2020 connection
Left drivetrain
2 motor controllers
PWM
Right drivetrain
2 motor controllers
PWM
Ball belt
1 motor controller
PWM
Scoring roller
1 motor controller
PWM
Climber
CAN module and 2 valves
CAN to module
2020 FRC robot | command-based implementation
05
2020 PWM outputs
NI roboRIO | WPILib documentation
Notes: - This slide is a case study of the hardware installed on the 2020 robot.
- The drivetrain motor controllers use PWM channels 0 through 3.
- The belt uses PWM 5, and the scoring roller uses PWM 4.
- The climber uses CTRE PCM module 0 over the CAN bus, with solenoid channel pairs 0/1 and 2/3.
- The team's current motor controllers and pneumatics modules use CAN rather than PWM.
- The software lesson is device ownership inside subsystems, not the particular channel numbers.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/RollerSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
- User-provided project context about the team's current CAN-connected hardware
[/Sources]

## Slide 6
3 · HARDWARE OPERATION
A PWM channel becomes a CAN ID; the subsystem boundary stays
The identifier and device construction change. The subsystem methods and commands do not.
What changes inside the subsystem
2020 robot
identifier -> PWM channel
connection -> dedicated PWM signal
object -> PWM motor controller
Current robot
identifier -> CAN ID
connection -> shared CAN bus
object -> CAN motor controller
2020 robot
PWM channel
Current robot
CAN ID
Unchanged
drive(left, right)
2020 FRC robot | command-based implementation
06
Notes: - A PWM motor controller is identified by the roboRIO PWM channel connected to it.
- A CAN motor controller is identified by its CAN ID on the shared CAN bus.
- Moving to CAN changes the device object, construction, configuration, and identifier stored in Constants.
- The subsystem still exposes mechanism-level methods such as drive(left, right).
- Commands and controller bindings continue calling those subsystem methods.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
- User-provided project context about the team's current CAN-connected hardware
[/Sources]

## Slide 7
3 · HARDWARE OPERATION
Commands do not need to know which bus the controller uses
The command and subsystem method stay the same when a PWM device is replaced by a CAN device.
Layer
2020 robot
Current robot
What changes
Command
BeltInCommand
Same command
Nothing
Subsystem call
run(+1.0)
Same method
Nothing
Device object
PWM controller
CAN controller
Construction and setup
DURABLE CONTROL PATH
controller input -> command -> subsystem method -> device API
2020 FRC robot | command-based implementation
07
Notes: - BeltInCommand represents the task regardless of the installed motor controller.
- The command still calls BeltSubsystem.run(+1.0).
- BeltSubsystem still owns the motor-controller object and translates run(speed) into a device API call.
- Replacing PWM with CAN changes the construction and device API inside BeltSubsystem.
- The controller binding, command lifecycle, subsystem requirement, and stop behavior do not need to change.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
[/Sources]

## Slide 8
3 · HARDWARE OPERATION
The climber already demonstrates the CAN module pattern
The roboRIO addresses one module over CAN; that module controls the two pneumatic valves.
2020 climber connection
roboRIO -> CAN bus -> CTRE PCM
PCM -> left pneumatic valve
PCM -> right pneumatic valve
The solenoids are controlled by the module;
they are not individual CAN devices.
State transition
Retracted
⇄
Extended
Startup assumption
The code starts with armsExtended = false. The physical arms must begin retracted.
2020 FRC robot | command-based implementation
08
Notes: - The 2020 climber already uses a CAN-connected control module.
- The roboRIO addresses CTRE PCM module 0 over the CAN bus.
- The PCM then controls the left and right pneumatic valves through its local solenoid channels.
- The DoubleSolenoid objects represent those channel pairs in ClimberSubsystem.
- The individual solenoids are not CAN devices; the PCM is the CAN device.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
[/Sources]

## Slide 9
4 · SOFTWARE CONTROL
Software gives each hardware piece one owner and one control path
RobotContainer creates subsystems and command instances, then connects controller inputs to commands.
1
Controllers
Axes and buttons
2
RobotContainer
Objects and bindings
3
Commands
Scheduled behavior
4
Subsystems
Hardware ownership
5
Device APIs
PWM or CAN devices
CommandScheduler polls triggers, runs scheduled commands, and enforces subsystem requirements.
2020 FRC robot | command-based implementation
09
Notes: - Robot creates one RobotContainer during robotInit().
- RobotContainer creates the controllers and the four subsystem objects.
- Each subsystem constructor creates the device objects that represent its installed hardware.
- RobotContainer creates command instances, passes them the required subsystem objects, and binds controller inputs to them.
- When CommandScheduler runs a command, the command calls subsystem methods; the subsystem methods call the device APIs.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Robot.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 10
4 · SOFTWARE CONTROL
RobotContainer creates subsystems, commands, and bindings
Subsystem constructors create hardware objects; RobotContainer then configures commands and controller bindings.
STARTUP PATH
public void robotInit() {
robotContainer = new RobotContainer();
}
public RobotContainer() {
driverController = new CommandXboxController(
Constants.Operator.DRIVER_CONTROLLER);
operatorController = new CommandXboxController(
Constants.Operator.OPERATOR_CONTROLLER);
driveSubsystem = new DriveSubsystem();
climberSubsystem = new ClimberSubsystem();
beltSubsystem = new BeltSubsystem();
rollerSubsystem = new RollerSubsystem();
CameraServer.startAutomaticCapture(0);
configureDefaultCommands();
configureBindings();
}
What RobotContainer establishes
Each subsystem constructor creates and owns its device objects.
The drive command is installed as the default command.
Bindings create command instances and pass subsystem references.
Hardware-specific construction stays inside each subsystem.
2020 FRC robot | command-based implementation
10
Notes: - Robot.robotInit() creates RobotContainer once.
- RobotContainer's constructor creates the two CommandXboxController objects and four subsystem objects.
- Each subsystem constructor creates and owns its motor-controller or solenoid objects.
- configureDefaultCommands() creates DriveTeleopCommand and installs it on DriveSubsystem.
- configureBindings() creates the button-controlled command instances and passes the appropriate subsystem object into each constructor.
- The camera is also started here, but it is separate from the command and subsystem relationships shown in this presentation.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Robot.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 11
4 · SOFTWARE CONTROL
RobotContainer creates instances of the command classes we write
Each command instance receives the subsystem object it needs to perform one specific task.
1
Command class
Written for one task
2
RobotContainer
Creates an instance
3
Subsystem reference
Passed to constructor
4
Binding or default
Determines when it runs
5
Command Scheduler
Runs its lifecycle
The command calls subsystem methods; the subsystem controls its device objects.
2020 FRC robot | command-based implementation
11
Notes: - The programmer writes a command class for a specific task, such as BeltInCommand.
- RobotContainer creates a command instance with new BeltInCommand(beltSubsystem).
- Passing beltSubsystem gives that command access to the subsystem methods it needs.
- The command constructor calls addRequirements(beltSubsystem), which declares exclusive use of the mechanism while the command runs.
- A Trigger binding or default-command assignment determines when CommandScheduler schedules that instance.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
[/Sources]

## Slide 12
4 · SOFTWARE CONTROL
Trigger bindings identify which command each input schedules
new BeltInCommand(beltSubsystem) creates the instance; whileTrue binds it to operator button A.
RobotContainer.configureBindings()
operatorController.y()
.onTrue(new ToggleClimberArmsCommand(climberSubsystem));
operatorController.a()
.whileTrue(new BeltInCommand(beltSubsystem));
operatorController.b()
.whileTrue(new BeltOutCommand(beltSubsystem));
operatorController.x()
.whileTrue(new RollerCommand(rollerSubsystem));
driverController.rightBumper()
.whileTrue(new SlowDriveCommand(driveSpeedMode));
Read a binding as a sentence
Which controller?
Which button?
Which Trigger binding method?
Which command?
Which subsystem does it require?
2020 FRC robot | command-based implementation
12
Notes: - Start by reading operatorController.a() as the operator's A button.
- new BeltInCommand(beltSubsystem) creates one command instance and passes it the existing BeltSubsystem object.
- whileTrue binds that command to the button's active state.
- When A becomes active, CommandScheduler schedules the command after checking its BeltSubsystem requirement.
- When A becomes inactive, WPILib cancels the command and calls end(true), which stops the belt.
- DriveTeleopCommand is different because RobotContainer installs it as DriveSubsystem's default command instead of binding it to a button.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
[/Sources]

## Slide 13
4 · SOFTWARE CONTROL
CommandScheduler moves each request through the control path
robotPeriodic() calls CommandScheduler.run() every 20 ms, about 50 times per second.
Robot.java
@Override
public void robotPeriodic() {
CommandScheduler.getInstance().run();
}
1
Run subsystem periodic methods
2
Poll Trigger bindings; schedule or cancel commands
3
Execute scheduled commands
4
Check completion and call end(...)
5
Schedule default commands
Commands must return promptly so CommandScheduler.run() can finish each iteration.
2020 FRC robot | command-based implementation
13
Notes: - This project follows the standard WPILib Java structure: Robot extends TimedRobot, which provides the robot's periodic execution loop.
- By default, the WPILib robot library calls robotPeriodic() every 20 milliseconds, or about 50 times per second.
- Each call to robotPeriodic() calls CommandScheduler.run(), producing one scheduler iteration.
- During an iteration, the scheduler runs subsystem periodic methods, polls Trigger bindings, and schedules or cancels commands.
- It then executes scheduled commands, ends commands that have finished or were canceled, and schedules default commands for available subsystems.
- Command methods must return promptly. A blocking method prevents the scheduler from completing that robot-loop iteration.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Robot.java
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj/TimedRobot.html
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/CommandScheduler.html
[/Sources]

## Slide 14
4 · SOFTWARE CONTROL
The command lifecycle controls setup, repeated work, and shutdown
The lifecycle separates setup, repeated work, completion, and cleanup.
initialize()
Once when scheduled
↓
execute()
Once per scheduler iteration
↓
isFinished()
Checked after execution
↓
end(interrupted)
Once on finish or cancellation
false
Remain scheduled; execute again.
finished or canceled
Call end(false) or end(true).
A loop that never returns blocks CommandScheduler.
2020 FRC robot | command-based implementation
14
Notes: - initialize() runs once when the scheduler starts the command.
- execute() runs once during each scheduler iteration and calls the required subsystem methods.
- isFinished() tells the scheduler whether the command has completed.
- If isFinished() returns false, the command remains scheduled and executes again during the next iteration.
- end(false) runs after normal completion, while end(true) runs after cancellation or interruption.
- Cleanup belongs in end(). The belt and roller commands stop their motors there.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/Command.html
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/button/Trigger.html
[/Sources]

## Slide 15
4 · SOFTWARE CONTROL
Requirements keep two commands from owning one mechanism
Commands requiring different subsystems may run concurrently.
Subsystem
Commands that require it
Scheduler result
DriveSubsystem
DriveTeleopCommand
Scheduled by default when DriveSubsystem is available
BeltSubsystem
BeltInCommand, BeltOutCommand
Only one command requiring BeltSubsystem can be scheduled
RollerSubsystem
RollerCommand
Can run concurrently with belt commands
ClimberSubsystem
ToggleClimberArmsCommand
No other command requiring ClimberSubsystem can run concurrently
addRequirements(subsystem) adds a subsystem requirement. A field reference does not add that requirement.
2020 FRC robot | command-based implementation
15
Notes: Belt commands require BeltSubsystem. RollerCommand requires RollerSubsystem, so the scheduler may run a belt command and RollerCommand concurrently. It will not schedule two commands that require BeltSubsystem at the same time.
[Sources]
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/Command.html
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/
[/Sources]

## Slide 16
4 · SOFTWARE CONTROL
Driver stick input reaches the drivetrain through six steps
The same path works whether the subsystem owns PWM or CAN motor-controller objects.
1
Driver Xbox
Left Y and right Y
2
Default command
Scheduled when drive is free
3
Scheduler
Executes every iteration
4
Drive command
Reads axes and scales
5
Drive subsystem
drive(left, right)
6
Motor controllers
Drive motors turn
Continuous
No requirement conflict -> default command stays scheduled -> execute() repeats next iteration
2020 FRC robot | command-based implementation
16
Notes: - The driver Xbox controller supplies the left-stick and right-stick Y values.
- CommandScheduler runs DriveTeleopCommand as DriveSubsystem's default command.
- The command scales both values and calls DriveSubsystem.drive(left, right).
- DriveSubsystem sends those values through its owned motor-controller objects.
- On this 2020 robot those objects use PWM; the current robot can use CAN devices without changing the earlier steps.
- The physical result is the same: the left and right drivetrain motors turn.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/DriveTeleopCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
[/Sources]

## Slide 17
4 · SOFTWARE CONTROL
Operator A reaches the belt motor through six explicit steps
The software path stays the same when the motor-controller connection changes.
1
Operator Xbox
A becomes true
2
Trigger
whileTrue schedules
3
Scheduler
Checks requirements
4
Command
execute() runs
5
Subsystem
run(+1.0)
6
Motor controller
Belt motor turns
Release
A false -> cancel -> end(true) -> beltSubsystem.stop() -> motor output becomes zero
2020 FRC robot | command-based implementation
17
Notes: - Operator A activates a Trigger binding in RobotContainer.
- The binding schedules a BeltInCommand instance that holds a reference to BeltSubsystem.
- execute() calls BeltSubsystem.run(+1.0).
- BeltSubsystem sends that value through its owned motor-controller object.
- Releasing A cancels the command; end(true) calls BeltSubsystem.stop(), which commands zero output.
- PWM or CAN changes the device implementation inside BeltSubsystem, not this control path.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
[/Sources]

## Slide 18
4 · SOFTWARE CONTROL
Every robot action follows the same ownership path
Start with the mechanism, then follow its subsystem, command, binding, and hardware object.
1
Start with the hardware
Identify the hardware object and the subsystem that encapsulates it.
2
Find the binding
Locate the controller input and Trigger binding method.
3
Read the command
Check requirements, lifecycle methods, and completion.
4
Trace the output
Follow the subsystem method to the WPILib hardware object.
CommandScheduler coordinates commands; each subsystem encapsulates its own hardware.
2020 FRC robot | command-based implementation
18
Notes: Close by repeating the concrete reading path rather than summarizing the development process.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/
[/Sources]