## Slide 1
FRC ROBOT SOFTWARE
The finished command-based
robot implementation
Four questions connect the robot's jobs, subsystems, hardware, and software
ROBOT JOBS
↓
SUBSYSTEMS
↓
HARDWARE
↓
SOFTWARE
WPILib 2026.2.1
2020 FRC robot | command-based implementation
01
Notes: This presentation answers four questions in order. First, what does the robot do? Second, what are its major subsystems? Third, how does the hardware work? Fourth, how does the software identify and control each piece? The last section includes the WPILib runtime and two complete code traces because they show the software control path in operation.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/docs/final-implementation-presentation-architecture.md
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 2
1 · ROBOT JOBS
The robot drives, moves game pieces, scores, and climbs
The finished robot gives its two operators four physical functions.
Drive
Move and steer the robot
Two-stick tank drive
Ball belt
Move balls through the robot
Runs forward or backward
Scoring roller
Push balls into the goal
Runs while X is held
Climber
Raise or lower the arms
Y toggles the position
The driver controls motion. The operator controls the belt, roller, and climber.
2020 FRC robot | command-based implementation
02
Notes: - The drivetrain moves and steers the robot with tank drive.
- The ball belt moves game pieces forward or backward inside the robot.
- The scoring roller pushes game pieces out toward the goal.
- The climber changes the position of two pneumatic arms.
- The driver owns robot motion; the operator owns the three mechanisms.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/RollerSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
[/Sources]

## Slide 3
1 · ROBOT JOBS
Two Xbox controllers separate driving from mechanism control
The driver owns tank drive; the operator owns the belt, roller, and climber.
USB 0
Driver Xbox
Left stick Y
Left drive output
Right stick Y
Right drive output
MODE
Slow drive
Right bumper
Hold for 0.4 scale
Release for 0.8 scale
Driver control only
USB 1
Operator Xbox
A Belt in
B Belt out
X Roller
Y Climber
Two CommandXboxController instances keep driver and operator bindings distinct.
2020 FRC robot | command-based implementation
03
Notes: The driver CommandXboxController is on USB 0 and supplies both tank-drive Y axes plus the right-bumper slow mode. The operator CommandXboxController is on USB 1: A runs the belt inward, B runs it outward, X runs the roller, and Y schedules the climber command.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 4
2 · MAJOR SUBSYSTEMS
Four subsystems divide the robot by mechanism
Each subsystem owns the hardware objects and methods for one physical function.
Drive
4 motor controllers
drive(left, right)
Ball belt
1 motor controller
run(speed), stop()
Scoring roller
1 motor controller
run(speed), stop()
Climber
CAN module and 2 valves
toggleArms()
DriveSubsystem, BeltSubsystem, RollerSubsystem, and ClimberSubsystem each own one mechanism.
2020 FRC robot | command-based implementation
04
Notes: - The four subsystem boundaries come from physical mechanisms, not the communication bus.
- DriveSubsystem owns four motor-controller objects.
- BeltSubsystem and RollerSubsystem each own one motor-controller object.
- ClimberSubsystem owns the pneumatic device objects used by the climber.
- The 2020 implementations use PWM motor controllers and a CAN-connected PCM; current implementations can use CAN devices without changing these subsystem boundaries.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/RollerSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
[/Sources]

## Slide 5
3 · HARDWARE OPERATION
A hardware ID tells the software which control point to use
The ID passed to a device object selects the physical interface or device it controls.
Mechanism
Device object
Control point ID
Left drivetrain
2 motor controllers
0 and 1
Right drivetrain
2 motor controllers
3 and 2
Ball belt
1 motor controller
5
Scoring roller
1 motor controller
4
Climber
CAN module and 2 valves
module 0; channels 0/1, 2/3
2020 FRC robot | command-based implementation
05
2020 example: PWM ports
NI roboRIO | WPILib documentation
Notes: - Every hardware object needs an identifier that tells the library which control point it represents.
- The code passes that ID into the device object's constructor.
- The subsystem stores the resulting device object and uses it whenever a command requests an action.
- On this 2020 robot, the motor-controller IDs are the roboRIO PWM port numbers shown in the table.
- The climber uses a module ID for the PCM and channel IDs for the module outputs.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/RollerSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
[/Sources]

## Slide 6
3 · HARDWARE OPERATION
Constants give each control point ID a useful name
Named constants tell a reader what each number controls and prevent unexplained numeric literals.
Named hardware IDs in Constants
PWM_FRONT_LEFT_DRIVE = 0
PWM_BACK_LEFT_DRIVE = 1
PWM_FRONT_RIGHT_DRIVE = 3
PWM_BACK_RIGHT_DRIVE = 2
PWM_BELT = 5
PWM_ROLLER = 4
Constants
Names each ID
Subsystem constructor
Creates device objects
Subsystem method
Uses owned objects
2020 FRC robot | command-based implementation
06
Notes: - Constants gives each numeric hardware ID a name that describes the control point.
- PWM_FRONT_LEFT_DRIVE identifies control point 0; PWM_BELT identifies control point 5.
- The names keep raw hardware numbers out of the subsystem code.
- Changing a wiring assignment requires changing the named constant instead of searching for repeated numeric literals.
- These names also make the subsystem constructors readable without hiding the actual ID values.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
[/Sources]

## Slide 7
3 · HARDWARE OPERATION
A subsystem uses each ID when it creates a device object
After construction, commands call subsystem methods. They do not need the hardware ID.
Step
Drive example
Belt example
What the ID does
Named ID
PWM_FRONT_LEFT_ DRIVE
PWM_BELT
Selects control point
Create object
new Talon(ID)
new Talon(ID)
Connects software object
Run mechanism
drive(left, right)
run(speed)
Uses stored object
ID TO ACTION
named ID -> constructor -> device object -> subsystem method -> hardware output
2020 FRC robot | command-based implementation
07
Notes: - A subsystem constructor creates each hardware device object once.
- The constructor passes the named hardware ID to the WPILib device class, such as new Talon(Constants.Hardware.PWM_BELT).
- That call connects the software object to the specified control point.
- The subsystem stores the object in a field and later calls set() through its mechanism methods.
- Commands call drive(), run(), or stop(); they do not work with hardware IDs directly.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/RollerSubsystem.java
[/Sources]

## Slide 8
3 · HARDWARE OPERATION
The climber uses IDs for its pneumatic module and output channels
Module ID 0 selects the PCM; channel IDs select the left and right valve outputs.
Climber control point IDs
PCM module ID 0
channel IDs 0/1 -> left valve
channel IDs 2/3 -> right valve
The module ID selects the PCM.
The channel IDs select its outputs.
State transition
Retracted
⇄
Extended
Startup assumption
The code starts with armsExtended = false. The physical arms must begin retracted.
2020 FRC robot | command-based implementation
08
Notes: - The climber uses the same identification idea at two levels.
- PCM module ID 0 tells WPILib which pneumatics module to address over CAN.
- Channel IDs 0/1 select the left valve outputs; channel IDs 2/3 select the right valve outputs.
- The PCM receives the CAN message and switches the requested module channels.
- The individual solenoids are controlled by the PCM; they are not separate CAN devices.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Constants.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/ClimberSubsystem.java
[/Sources]

## Slide 9
4 · SOFTWARE CONTROL
Software gives each hardware piece one owner and one control path
RobotContainer creates subsystems and command instances, then connects controller inputs to commands.
1
Controllers
Axes and buttons
2
RobotContainer
Objects and bindings
3
Commands
Scheduled behavior
4
Subsystems
Hardware ownership
5
Device APIs
Hardware device objects
CommandScheduler polls triggers, runs scheduled commands, and enforces subsystem requirements.
2020 FRC robot | command-based implementation
09
Notes: - Robot creates one RobotContainer during robotInit().
- RobotContainer creates the controllers and the four subsystem objects.
- Each subsystem constructor creates the device objects that represent its installed hardware.
- RobotContainer creates command instances, passes them the required subsystem objects, and binds controller inputs to them.
- When CommandScheduler runs a command, the command calls subsystem methods; the subsystem methods call the device APIs.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Robot.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 10
4 · SOFTWARE CONTROL
RobotContainer creates subsystems, commands, and bindings
Subsystem constructors create hardware objects; RobotContainer then configures commands and controller bindings.
STARTUP PATH
public void robotInit() {
robotContainer = new RobotContainer();
}
public RobotContainer() {
driverController = new CommandXboxController(
Constants.Operator.DRIVER_CONTROLLER);
operatorController = new CommandXboxController(
Constants.Operator.OPERATOR_CONTROLLER);
driveSubsystem = new DriveSubsystem();
climberSubsystem = new ClimberSubsystem();
beltSubsystem = new BeltSubsystem();
rollerSubsystem = new RollerSubsystem();
CameraServer.startAutomaticCapture(0);
configureDefaultCommands();
configureBindings();
}
What RobotContainer establishes
Each subsystem constructor creates and owns its device objects.
The drive command is installed as the default command.
Bindings create command instances and pass subsystem references.
Hardware-specific construction stays inside each subsystem.
2020 FRC robot | command-based implementation
10
Notes: - Robot.robotInit() creates RobotContainer once.
- RobotContainer's constructor creates the two CommandXboxController objects and four subsystem objects.
- Each subsystem constructor creates and owns its motor-controller or solenoid objects.
- configureDefaultCommands() creates DriveTeleopCommand and installs it on DriveSubsystem.
- configureBindings() creates the button-controlled command instances and passes the appropriate subsystem object into each constructor.
- The camera is also started here, but it is separate from the command and subsystem relationships shown in this presentation.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Robot.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
[/Sources]

## Slide 11
4 · SOFTWARE CONTROL
RobotContainer creates instances of the command classes we write
Each command instance receives the subsystem object it needs to perform one specific task.
1
Command class
Written for one task
2
RobotContainer
Creates an instance
3
Subsystem reference
Passed to constructor
4
Binding or default
Determines when it runs
5
Command Scheduler
Runs its lifecycle
The command calls subsystem methods; the subsystem controls its device objects.
2020 FRC robot | command-based implementation
11
Notes: - The programmer writes a command class for a specific task, such as BeltInCommand.
- RobotContainer creates a command instance with new BeltInCommand(beltSubsystem).
- Passing beltSubsystem gives that command access to the subsystem methods it needs.
- The command constructor calls addRequirements(beltSubsystem), which declares exclusive use of the mechanism while the command runs.
- A Trigger binding or default-command assignment determines when CommandScheduler schedules that instance.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
[/Sources]

## Slide 12
4 · SOFTWARE CONTROL
Trigger bindings identify which command each input schedules
new BeltInCommand(beltSubsystem) creates the instance; whileTrue binds it to operator button A.
RobotContainer.configureBindings()
operatorController.y()
.onTrue(new ToggleClimberArmsCommand(climberSubsystem));
operatorController.a()
.whileTrue(new BeltInCommand(beltSubsystem));
operatorController.b()
.whileTrue(new BeltOutCommand(beltSubsystem));
operatorController.x()
.whileTrue(new RollerCommand(rollerSubsystem));
driverController.rightBumper()
.whileTrue(new SlowDriveCommand(driveSpeedMode));
Read a binding as a sentence
Which controller?
Which button?
Which Trigger binding method?
Which command?
Which subsystem does it require?
2020 FRC robot | command-based implementation
12
Notes: - Start by reading operatorController.a() as the operator's A button.
- new BeltInCommand(beltSubsystem) creates one command instance and passes it the existing BeltSubsystem object.
- whileTrue binds that command to the button's active state.
- When A becomes active, CommandScheduler schedules the command after checking its BeltSubsystem requirement.
- When A becomes inactive, WPILib cancels the command and calls end(true), which stops the belt.
- DriveTeleopCommand is different because RobotContainer installs it as DriveSubsystem's default command instead of binding it to a button.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
[/Sources]

## Slide 13
4 · SOFTWARE CONTROL
CommandScheduler moves each request through the control path
robotPeriodic() calls CommandScheduler.run() every 20 ms, about 50 times per second.
Robot.java
@Override
public void robotPeriodic() {
CommandScheduler.getInstance().run();
}
1
Run subsystem periodic methods
2
Poll Trigger bindings; schedule or cancel commands
3
Execute scheduled commands
4
Check completion and call end(...)
5
Schedule default commands
Commands must return promptly so CommandScheduler.run() can finish each iteration.
2020 FRC robot | command-based implementation
13
Notes: - This project follows the standard WPILib Java structure: Robot extends TimedRobot, which provides the robot's periodic execution loop.
- By default, the WPILib robot library calls robotPeriodic() every 20 milliseconds, or about 50 times per second.
- Each call to robotPeriodic() calls CommandScheduler.run(), producing one scheduler iteration.
- During an iteration, the scheduler runs subsystem periodic methods, polls Trigger bindings, and schedules or cancels commands.
- It then executes scheduled commands, ends commands that have finished or were canceled, and schedules default commands for available subsystems.
- Command methods must return promptly. A blocking method prevents the scheduler from completing that robot-loop iteration.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/Robot.java
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj/TimedRobot.html
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/CommandScheduler.html
[/Sources]

## Slide 14
4 · SOFTWARE CONTROL
The command lifecycle controls setup, repeated work, and shutdown
The lifecycle separates setup, repeated work, completion, and cleanup.
initialize()
Once when scheduled
↓
execute()
Once per scheduler iteration
↓
isFinished()
Checked after execution
↓
end(interrupted)
Once on finish or cancellation
false
Remain scheduled; execute again.
finished or canceled
Call end(false) or end(true).
A loop that never returns blocks CommandScheduler.
2020 FRC robot | command-based implementation
14
Notes: - initialize() runs once when the scheduler starts the command.
- execute() runs once during each scheduler iteration and calls the required subsystem methods.
- isFinished() tells the scheduler whether the command has completed.
- If isFinished() returns false, the command remains scheduled and executes again during the next iteration.
- end(false) runs after normal completion, while end(true) runs after cancellation or interruption.
- Cleanup belongs in end(). The belt and roller commands stop their motors there.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/Command.html
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/button/Trigger.html
[/Sources]

## Slide 15
4 · SOFTWARE CONTROL
Requirements keep two commands from owning one mechanism
Commands requiring different subsystems may run concurrently.
Subsystem
Commands that require it
Scheduler result
DriveSubsystem
DriveTeleopCommand
Scheduled by default when DriveSubsystem is available
BeltSubsystem
BeltInCommand, BeltOutCommand
Only one command requiring BeltSubsystem can be scheduled
RollerSubsystem
RollerCommand
Can run concurrently with belt commands
ClimberSubsystem
ToggleClimberArmsCommand
No other command requiring ClimberSubsystem can run concurrently
addRequirements(subsystem) adds a subsystem requirement. A field reference does not add that requirement.
2020 FRC robot | command-based implementation
15
Notes: Belt commands require BeltSubsystem. RollerCommand requires RollerSubsystem, so the scheduler may run a belt command and RollerCommand concurrently. It will not schedule two commands that require BeltSubsystem at the same time.
[Sources]
- https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/Command.html
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/
[/Sources]

## Slide 16
4 · SOFTWARE CONTROL
Driver stick input reaches the drivetrain through six steps
DriveSubsystem already owns the motor-controller objects selected by their hardware IDs.
1
Driver Xbox
Left Y and right Y
2
Default command
Scheduled when drive is free
3
Scheduler
Executes every iteration
4
Drive command
Reads axes and scales
5
Drive subsystem
drive(left, right)
6
Motor controllers
Drive motors turn
Continuous
No requirement conflict -> default command stays scheduled -> execute() repeats next iteration
2020 FRC robot | command-based implementation
16
Notes: - The driver Xbox controller supplies the left-stick and right-stick Y values.
- CommandScheduler runs DriveTeleopCommand as DriveSubsystem's default command.
- The command scales both values and calls DriveSubsystem.drive(left, right).
- DriveSubsystem sends those values through the motor-controller objects it created from the named hardware IDs.
- The physical result is that the left and right drivetrain motors turn.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/DriveTeleopCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/DriveSubsystem.java
[/Sources]

## Slide 17
4 · SOFTWARE CONTROL
Operator A reaches the belt motor through six explicit steps
BeltSubsystem already owns the motor-controller object selected by its hardware ID.
1
Operator Xbox
A becomes true
2
Trigger
whileTrue schedules
3
Scheduler
Checks requirements
4
Command
execute() runs
5
Subsystem
run(+1.0)
6
Motor controller
Belt motor turns
Release
A false -> cancel -> end(true) -> beltSubsystem.stop() -> motor output becomes zero
2020 FRC robot | command-based implementation
17
Notes: - Operator A activates a Trigger binding in RobotContainer.
- The binding schedules a BeltInCommand instance that holds a reference to BeltSubsystem.
- execute() calls BeltSubsystem.run(+1.0).
- BeltSubsystem sends that value through the motor-controller object created from the belt hardware ID.
- Releasing A cancels the command; end(true) calls BeltSubsystem.stop(), which commands zero output.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/RobotContainer.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/commands/BeltInCommand.java
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
[/Sources]

## Slide 18
4 · SOFTWARE CONTROL
Every robot action follows the same ownership path
Start with the mechanism, then follow its subsystem, command, binding, and hardware object.
1
Start with the hardware
Identify the hardware object and the subsystem that encapsulates it.
2
Find the binding
Locate the controller input and Trigger binding method.
3
Read the command
Check requirements, lifecycle methods, and completion.
4
Trace the output
Follow the subsystem method to the WPILib hardware object.
CommandScheduler coordinates commands; each subsystem encapsulates its own hardware.
2020 FRC robot | command-based implementation
18
Notes: Close by repeating the concrete reading path rather than summarizing the development process.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/
[/Sources]

## Slide 19
CLOSING EXAMPLE
Modern CAN devices use the same control-point ID idea
The ID now selects a device on the shared CAN bus instead of a roboRIO PWM port.
One concept, two interfaces
2020 motor controller
ID -> roboRIO PWM port
connection -> dedicated signal
Modern motor controller
ID -> CAN device ID
connection -> shared CAN bus
The subsystem still owns the device object.
2020 example
ID 5 selects PWM port 5
Modern example
ID 5 selects CAN device 5
Unchanged call
beltSubsystem.run(speed)
2020 FRC robot | command-based implementation
19
Notes: - The control-point ID concept remains useful when the hardware interface changes.
- On the 2020 robot, motor-controller IDs select dedicated PWM ports on the roboRIO.
- On the team's modern hardware, a motor-controller ID selects a device on the shared CAN bus.
- For example, the number 5 can identify PWM port 5 in the older design or CAN device 5 in a modern design.
- The subsystem still creates and owns the device object, and commands still call the same subsystem methods.
- Only the device class, identifier meaning, and device configuration change inside the subsystem.
[Sources]
- C:/Users/dmona/2020FrcRobotCode/2020v2/2020/src/main/java/frc/robot/subsystems/BeltSubsystem.java
- User-provided current team hardware context
[/Sources]