## Slide 1
2020 FRC Robot Code Architecture & Implementation Guide
A Technical Guide to Robot Hardware, WPILib Command-Based Architecture, and Java Code Case Study: 4-Talon Drivetrain, Belt/Roller Transport, CTRE PCM Climber, and Dual CommandXboxControllers
Notes: Talking points - Introduce the robot as one connected system: hardware channels, operator controls, command scheduling, and Java files. - Explain that the presentation starts with direct hardware control, then adds the command framework, then traces the same behavior through the repository. Ask the room - Which part feels less familiar right now: wiring, WPILib, or Java? Watch out for - This is a guide to this robot. Other teams may use different ports, motor controllers, or pneumatic modules.

## Slide 2
SECTION 1
Robot hardware
Exploring physical mechanisms, PWM motor channels, pneumatics, and direct hardware control.
Notes: Talking points - The first section answers two questions: what mechanisms exist, and which roboRIO or PCM channels reach them? - Tell students that every software object shown later must eventually produce a physical electrical or pneumatic output. Ask the room - Before looking at code, what information would you need to make one motor move safely? Watch out for - Keep this transition short. The mechanism slides carry the technical detail.

## Slide 3
ROBOT HARDWARE
Physical Hardware Inventory & Actuator Channel Map
Mechanism | Hardware Device | Bus / Channel | Configuration Notes
Drivetrain (4 Motors) | 4x Talon SRX | PWM 0, 1 (Left) PWM 2, 3 (Right) | Tank Drive. Left-side motors inverted due to mechanical mounting.
Ball Transport Belt | 1x Talon SRX | PWM Port 5 | Feeds balls inward/outward through indexer.
Outtake Roller | 1x Talon SRX | PWM Port 4 | High-speed ball ejection roller.
Climber Arms | 1x Double Solenoid Valve | CTRE PCM ID 0 Channels 0/1 | One valve feeds both cylinders through split air lines.
Hardware Inversion Note:
Because the left and right drive gearboxes are mounted symmetrically facing opposite directions, positive voltage on both sides drives left forward and right backward. The left-side motors must be inverted in software (leftDriveMotors.setInverted(true)) so positive speed drives both sides forward.
Notes: Talking points - Walk across the table one mechanism at a time. - The drivetrain uses PWM ports 0 through 3. The roller uses port 4. The belt uses port 5. - The climber uses one double-solenoid valve on PCM channels 0 and 1. Pneumatic tees let that valve control both cylinders. - Explain why the left drivetrain side needs inversion. Ask the room - If the belt does not move, which single channel would you inspect first? Watch out for - A channel number identifies an electrical connection. It does not identify the mechanism unless the wiring and constants agree.

## Slide 4
ROBOT HARDWARE
PWM wiring from the roboRIO to the motors
roboRIO PWM outputs Ports 0 through 5
PWM 0 and 1 Left drive Talons
PWM 2 and 3 Right drive Talons
PWM 4 Roller Talon
PWM 5 Belt Talon
Talon SRX motor controllers translate PWM commands into motor voltage
Separate CAN connection roboRIO CAN bus to PCM ID 0
This robot controls its Talon SRXs through PWM. The PCM uses CAN.
Notes: Talking points - Follow each colored line from a roboRIO PWM output to its Talon SRX. - The Talon SRXs in this project receive motor commands through PWM. - The PCM has a separate CAN connection. The presence of CAN-capable Talon SRXs does not mean this project controls them through CAN. Ask the room - Which port would you inspect for a roller problem? Which ports belong to the right drive? Watch out for - Do not describe PWM as motor power. PWM is the control signal. The motor controller switches battery power to the motor.

## Slide 5
ROBOT HARDWARE
Running the belt motor
Bare-Minimum Belt Control Program:
• Direct Hardware Actuation: Uses WPILib's Talon class on PWM Port 5 directly inside a TimedRobot program.
• Continuous Teleop Execution: teleopPeriodic() runs continuously every 20ms while teleop is enabled.
• Constant Power Output: Calls beltMotor.set(0.25) to run the belt at 25% power.
• Automatic Safety Shutdown: Disabling the robot instantly cuts the roboRIO PWM signal to 0V, stopping the motor.
package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; public class Robot extends TimedRobot { // Talon motor controller on PWM Port 5 private final Talon beltMotor = new Talon(5); @Override public void teleopPeriodic() { // Runs belt at 25% output continuously beltMotor.set(0.25); } }
Notes: Talking points - This TimedRobot example removes controllers and commands. Enabling teleop repeatedly calls teleopPeriodic(). - The Talon object maps directly to PWM port 5. - A value of 0.25 requests 25 percent output. Ask the room - What line would you change to reverse the belt? Watch out for - Driver Station disable prevents motor output. Avoid describing the disabled PWM signal as a guaranteed literal zero-volt waveform. VS Code - Open the small belt demonstration project if available, then compare it with BeltSubsystem.java later.

## Slide 6
ROBOT HARDWARE
Roller Challenge: Running the Roller Motor
What Changes From the Belt Program?
• Identical Pattern, Different Channel: Operating the roller requires only changing the PWM channel and instance name.
• PWM Port 4: The outtake roller is wired to PWM Port 4 (Talon rollerMotor = new Talon(4)).
• Direct Actuation: rollerMotor.set(0.25) runs the outtake roller at 25% speed.
• Key Observation: Every motor controller in WPILib uses the exact same set(double speed) API call.
package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; public class Robot extends TimedRobot { // Roller motor controller on PWM Port 4 private final Talon rollerMotor = new Talon(4); @Override public void teleopPeriodic() { // Runs roller at 25% output continuously rollerMotor.set(0.25); } }
Notes: Talking points - The roller example repeats the same motor-control pattern on PWM port 4. - Point out that learning one motor API transfers directly to the next mechanism. Ask the room - Which two code tokens changed from the belt example? Watch out for - The repeated pattern is the lesson here. Move quickly once students identify the port and variable-name changes.

## Slide 7
ROBOT HARDWARE
Pneumatic Climber Arms
One Valve Controls Both Arms • One DoubleSolenoid: A single valve on CTRE PCM ID 0 controls the climber. • PCM Channels 0 and 1: The forward and reverse coils use one channel pair. • Split Air Lines: Each valve output splits to the matching port on both cylinders, so both pistons receive the same command. • Shared Motion: kForward extends both arms. kReverse retracts both arms.
package frc.robot; import edu.wpi.first.wpilibj.DoubleSolenoid; import edu.wpi.first.wpilibj.PneumaticsModuleType; import edu.wpi.first.wpilibj.TimedRobot; /** * NAME * Robot - extends both climber arms through one valve. * * DESCRIPTION * One double-solenoid valve feeds both cylinders. */ public class Robot extends TimedRobot { private final DoubleSolenoid climberSolenoid = new DoubleSolenoid( 0, PneumaticsModuleType.CTREPCM, 0, 1); @Override public void teleopPeriodic() { climberSolenoid.set( DoubleSolenoid.Value.kForward); } }
Notes: Talking points - One DoubleSolenoid object represents one physical valve with forward and reverse coils. - PCM channels 0 and 1 energize those coils. - The pneumatic plumbing splits both valve outputs so the two cylinders receive the same command. - The detailed code header documents that shared-valve assumption. Ask the room - Why does the Java program need only one DoubleSolenoid even though the robot has two cylinders? Watch out for - The software reports the commanded valve state, not measured arm position. Without sensors, it cannot prove that both cylinders moved.

## Slide 8
ROBOT HARDWARE
One valve moves both climber cylinders
ELECTRICAL CONTROL
roboRIO CAN bus
PCM ID 0 channels 0 and 1
One DoubleSolenoid valve forward and reverse coils
PNEUMATIC AIRFLOW
Compressor, tank, and regulator
The same valve routes air to both cylinder ports
Left cylinder
Right cylinder
A tee in each valve output sends the same extend or retract pressure to both cylinders.
Notes: Talking points - Read the top row as electrical control and the bottom row as airflow. - The roboRIO sends CAN messages to PCM ID 0. PCM channels 0 and 1 energize the valve coils. - Air comes from the compressor, storage tank, and regulator. The valve routes that air through tees to both cylinders. Ask the room - Which path still exists if the robot has air pressure but loses the electrical command? Watch out for - The PCM does not create compressed air. It controls the compressor and valve coils.

## Slide 9
ROBOT HARDWARE
4-Motor Drivetrain Control
SAFETY WARNING: Place the robot securely on blocks off the floor before enabling this test program.
• 4 Motors Across PWM 0..3: Front-left (PWM 0), Back-left (PWM 1), Back-right (PWM 2), Front-right (PWM 3).
• Sign Inversion (-0.15 vs +0.15): Drives left side at -0.15 and right side at +0.15 to account for left-side motor inversion.
package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; public class Robot extends TimedRobot { private final Talon frontLeft = new Talon(0); private final Talon backLeft = new Talon(1); private final Talon backRight = new Talon(2); private final Talon frontRight = new Talon(3); @Override public void teleopPeriodic() { // Left side inverted in software frontLeft.set(-0.15); backLeft.set(-0.15); frontRight.set(0.15); backRight.set(0.15); } }
Notes: Talking points - Put the robot securely on blocks before enabling this direct drivetrain test. - Four Talon objects map to PWM ports 0 through 3. - Opposite signs compensate for mirrored drivetrain mechanics. Ask the room - What physical behavior would tell you that one side needs inversion? Watch out for - Start with low output. Verify wheel direction before placing the robot on the floor.

## Slide 10
ROBOT HARDWARE
Controlling several mechanisms
Direct Control Strengths:
• 1-to-1 Hardware Verification: Simple TimedRobot code proves electrical wiring, PWM ports, and PCM channels function.
• Zero Framework Overhead: Directly invokes motor.set() without configuring commands or scheduling rules.
• Isolated Testing: Validates direction and motor response on blocks prior to driving.
System Coordination Bottlenecks:
• Monolithic teleopPeriodic(): Mixing joysticks, buttons, and 4 mechanisms into one huge loop leads to chaotic nested if-else logic.
• Hardware Conflicts: What happens if two buttons try to command the same belt motor at once?
• No Clean State Cleanup: Button releases, interruptions, and automated scoring sequences require complex state tracking flags.
Notes: Talking points - Direct hardware examples are excellent for verifying wiring and direction. - A complete robot needs coordination when several controls can request the same hardware. - Use the belt-in and belt-out conflict as the concrete reason for subsystem ownership. Ask the room - What happens in a large teleopPeriodic() method when two independent if statements set opposite belt speeds? Watch out for - Avoid claiming direct TimedRobot code is inherently unsafe. The issue is that coordination becomes harder to reason about as behavior grows.

## Slide 11
ROBOT HARDWARE
Human Controls & Dual CommandXboxController Mapping
DRIVER CONTROLLER (USB Port 0)
• Left Stick Y: Commands left-side drivetrain speed (-1.0 to +1.0).
• Right Stick Y: Commands right-side drivetrain speed (-1.0 to +1.0).
• Right Bumper (Held): Activates Precision Slow Drive Mode (scales speed from 40% down to 20%).
• Deadband: Applies 0.08 deadband to eliminate stick drift near center.
OPERATOR CONTROLLER (USB Port 1) • Button A (Held): Runs Ball Transport Belt Inward (+1.0 speed). • Button B (Held): Runs Ball Transport Belt Outward (-1.0 speed). • Button X (Held): Runs Outtake Roller (+1.0 speed). • Button Y (Pressed): Toggles the shared climber valve, extending or retracting both arms.
Notes: Talking points - The driver controller occupies USB slot 0. The operator controller occupies USB slot 1. - The driver uses two stick axes and the right bumper. - The operator controls the belt, roller, and shared climber valve. Ask the room - Which controls should continue while held, and which control should act once per press? Watch out for - Button labels describe intent only after RobotContainer binds them to commands.

## Slide 12
ROBOT HARDWARE
Driver Station USB Setup & Live Telemetry Diagnostics
Driver Station USB Slot Rules:
• Index Matching: The Driver Station USB tab assigns numeric port slots (0, 1, 2...). Software constants DRIVER_CONTROLLER = 0 and OPERATOR_CONTROLLER = 1 must match physical USB slots.
• Port Swap Misconfigurations: If controllers are plugged in backwards (Operator in Slot 0, Driver in Slot 1), stick inputs drive the wrong mechanisms.
• Live Diagnostic Grid: Pressing physical buttons on the Xbox controller lights up indicators in the live Driver Station telemetry grid to confirm mapping before enabling.
Notes: Talking points - Driver Station USB slot order must match Constants.Operator. - Use the live button grid before enabling the robot. - A working controller in the wrong slot can look like a software failure. Ask the room - If Button X lights up under USB slot 0, what configuration problem do you have? Watch out for - Diagnose input first. Do not enable mechanisms merely to discover which controller object is reading a button.

## Slide 13
ROBOT HARDWARE
Button A reaches PWM port 5
1. Controller
Button A Press
2. Driver Station
USB HID Packet
3. RobotContainer
Trigger Binding
4. BeltInCommand
Lifecycle Hooks
5. BeltSubsystem
PWM 5 Motor Output
PHYSICAL SIGNAL ORIGIN
• 1. Human Press: Thumb depresses Button A on Operator Xbox Controller (USB Port 1).
• 2. USB HID Packet: Controller micro-ASIC encodes button state and sends USB packet to Driver Station laptop.
• 3. UDP Network Packet: Driver Station software packages HID state into a 20ms UDP packet sent over Ethernet/Wi-Fi to roboRIO.
ACTUATOR OUTPUT DESTINATION
• 4. roboRIO HAL/FPGA: DriverStation HAL updates internal button array during 20ms periodic pass.
• 5. PWM 5 Signal: Software commands beltMotor.set(1.0). roboRIO FPGA generates 1.0ms to 2.0ms pulse-width signal on PWM Port 5.
• 6. Motor Motion: Talon SRX reads PWM signal and meters +12V from Power Distribution Panel to drive belt motor inward.
Notes: Talking points - Trace Button A from the operator's hand to PWM port 5. - Separate physical transport from Java routing: USB and Driver Station carry the state, then RobotContainer and the scheduler select the command. - BeltSubsystem owns the final Talon call. Ask the room - At which step does Button A become a BeltInCommand rather than a generic controller value? Watch out for - The numbered labels summarize layers, not separate threads or separate 20 ms loops.

## Slide 14
SECTION 2
Command-based robot code
Managing hardware exclusivity, trigger bindings, lifecycle hooks, and the 20ms execution loop.
Notes: Talking points - The command section adds ownership, lifecycle, and trigger semantics to the hardware knowledge from Section 1. - Tell students that the belt conflict will anchor the next several slides. Ask the room - What should decide which command controls the belt motor? Watch out for - Do not introduce commands as background threads. WPILib runs normal commands synchronously from the robot loop.

## Slide 15
COMMAND-BASED ROBOT CODE
Two commands request the belt
A Concrete Engineering Conflict:
1. Button A Request: Operator holds Button A -> Triggers BeltInCommand -> Commands belt motor +1.0 (Inward).
2. Button B Request: Simultaneously, Operator holds Button B -> Triggers BeltOutCommand -> Commands belt motor -1.0 (Outward).
3. The Conflict: Both commands target the exact same physical hardware (Talon SRX on PWM Port 5).
4. The Core Question: Which command owns the motor? What prevents the code from sending contradictory signals to the motor controller in the same 20ms loop pass?
The Architectural Solution: Subsystem Requirements (addRequirements)
WPILib solves this through subsystem requirements. Commands must declare which hardware resources they require. The CommandScheduler enforces hardware exclusivity, cancelling the older command before starting the new one.
Notes: Talking points - BeltInCommand requests positive output. BeltOutCommand requests negative output. - Both commands target one physical Talon on PWM port 5. - The scheduler needs explicit ownership information to resolve that conflict. Ask the room - If both commands start, should their outputs be averaged, should the first command win, or should one interrupt the other? Watch out for - The result depends on scheduling order and interruption behavior. The core guarantee is that two scheduled commands cannot own the same required subsystem simultaneously.

## Slide 16
COMMAND-BASED ROBOT CODE
Subsystem Requirements & Hardware Exclusivity
How addRequirements(subsystem) Works:
• Resource Registration: Inside a Command's constructor, calling addRequirements(beltSubsystem) registers the subsystem as a required resource.
• Scheduler Exclusivity Referee: The CommandScheduler tracks which command currently owns each subsystem.
• Automatic Interrupt & Cleanup: When Button B schedules BeltOutCommand, the scheduler sees that beltSubsystem is currently owned by BeltInCommand. It interrupts BeltInCommand, calls its end(true) method to safely stop the motor, and grants ownership to BeltOutCommand.
• Scheduler Ownership Scope: Enforces ownership within the CommandScheduler list—it is a logical referee, not an OS thread mutex.
public class BeltInCommand extends Command { private final BeltSubsystem beltSubsystem; public BeltInCommand(BeltSubsystem beltSubsystem) { this.beltSubsystem = beltSubsystem; // Declares exclusive hardware ownership addRequirements(beltSubsystem); } @Override public void execute() { beltSubsystem.run(Constants.Tuning.BELT_SPEED); } @Override public void end(boolean interrupted) { // Invoked automatically when cancelled beltSubsystem.stop(); } }
1
This line tells the scheduler that the command needs exclusive use of BeltSubsystem.
Notes: Talking points - Point directly to addRequirements(beltSubsystem). - The line does not lock an operating-system mutex. It declares ownership to CommandScheduler. - When another command needs BeltSubsystem, the scheduler interrupts the current owner before starting the new owner. Ask the room - What failure becomes possible if BeltOutCommand forgets this line? Watch out for - addRequirements protects scheduler-managed command ownership only. Code outside the subsystem can still create bad behavior if it accesses the same hardware directly. VS Code - Open BeltInCommand.java and BeltOutCommand.java. Compare their constructors.

## Slide 17
COMMAND-BASED ROBOT CODE
Architectural Separation: Subsystems (HOW) vs. Commands (WHEN)
SUBSYSTEMS (SubsystemBase)
• Hardware Ownership: Owns raw motor controllers (Talon), sensors, and solenoids in private fields.
• Encapsulation (HOW): Defines public API methods for mechanism actions (run(speed), stop(), extendArms()).
• Passive Capability: Knows HOW to move the hardware, but never decides WHEN to move.
• Examples: DriveSubsystem, BeltSubsystem, RollerSubsystem, ClimberSubsystem.
COMMANDS (Command)
• Execution Logic: Contains state machine rules and lifecycle methods (initialize, execute, end).
• Action Sequencing (WHEN): Dictates WHEN hardware actions occur in response to triggers or autonomous schedules.
• Resource Locks: Declares required subsystems via addRequirements().
• Examples: BeltInCommand, BeltOutCommand, ToggleClimberArmsCommand, DriveTeleopCommand.
Notes: Talking points - A subsystem owns hardware objects and exposes mechanism operations. - A command decides when to call those operations. - RobotContainer connects human inputs to command objects. Ask the room - Where should a raw Talon object live? Where should the decision to run it on Button A live? Watch out for - "Subsystems know how, commands know when" is a useful rule, not a ban on all state inside subsystems. Sensors and mechanism state often belong there.

## Slide 18
COMMAND-BASED ROBOT CODE
Trigger Bindings: whileTrue, onTrue, and setDefaultCommand
whileTrue(command)
• Momentary Active Control: Schedules command when button is pressed; keeps running while held.
• Release Cancellation: Button release cancels command and invokes end(true) cleanup.
• Used for: BeltInCommand, BeltOutCommand, RollerCommand, SlowDriveCommand.
onTrue(command) • Schedules the command once when the trigger changes from false to true. • The command decides when it finishes. onTrue does not make a command instant. • This climber command ends immediately because isFinished() returns true.
setDefaultCommand(...)
• Fallback Subsystem Command: Runs automatically whenever no other command is requiring the subsystem.
• Continuous Active Control: Re-schedules every pass unreserved.
• Used for: DriveTeleopCommand on DriveSubsystem.
Notes: Talking points - whileTrue schedules on the press and cancels on the release. - onTrue schedules once when the trigger changes from false to true. - onTrue does not make a command instant. ToggleClimberArmsCommand finishes quickly because its own isFinished() returns true. - A default command runs whenever its subsystem has no other scheduled owner. Ask the room - What would happen if a long-running command were bound with onTrue? Watch out for - Do not teach binding type and command duration as the same concept.

## Slide 19
COMMAND-BASED ROBOT CODE
Polymorphic Command Lifecycle Method Hooks
Lifecycle Method | When Invoked by CommandScheduler | Implementation Responsibility
initialize() | Runs ONCE when the command is scheduled. | Set up initial state, reset timers, toggle solenoids.
execute() | Runs REPEATEDLY every 20ms while command is active. | Pass motor speed setpoints to subsystem API methods.
isFinished() | Evaluated REPEATEDLY every 20ms after execute(). | Return true when complete (instant) or false to keep running.
end(boolean interrupted) | Runs ONCE when command finishes or is cancelled. | Safely shut off outputs (beltSubsystem.stop()).
Notes: Talking points - initialize() runs once when scheduling succeeds. - execute() runs during scheduler passes while the command remains scheduled. - isFinished() decides normal completion. - end(false) follows normal completion. end(true) follows cancellation or interruption. Ask the room - Which method should stop a motor so both completion paths are safe? Watch out for - A command can be interrupted before its next execute() call. Cleanup belongs in end(), not after a blocking loop.

## Slide 20
COMMAND-BASED ROBOT CODE
The 20 ms CommandScheduler cycle
1 Subsystem periodic() Each registered subsystem runs periodic().
2 Poll button bindings Triggers detect button changes and schedule commands.
3 Execute commands Scheduled commands run execute() on the main robot thread.
4 Finish and clean up The scheduler checks isFinished(), calls end(), and removes finished commands.
5 Start default commands Unused subsystems receive their default commands.
The sequence repeats about every 20 ms. WPILib does not reserve a fixed number of milliseconds for each stage.
Notes: Talking points - Read the boxes in the documented scheduler order. - Subsystem periodic methods run first, then button bindings, command execution, finish checks, and default-command scheduling. - The cycle repeats at the TimedRobot period, normally about 20 ms. Ask the room - If execute() calls Thread.sleep(500), which later stages must wait? Watch out for - The five stages do not own fixed 4 ms time slices. Their duration depends on the code executed during that cycle. Source - WPILib 2026 CommandScheduler API: https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj2/command/CommandScheduler

## Slide 21
COMMAND-BASED ROBOT CODE
Releasing Button A stops the belt
1. Controller
Button A Press
2. Driver Station
USB HID Packet
3. RobotContainer
Trigger Binding
4. BeltInCommand
Lifecycle Hooks
5. BeltSubsystem
PWM 5 Motor Output
STATE MACHINE CLEANUP TRACE ON BUTTON RELEASE:
1. Trigger State Transition: Operator releases Button A -> CommandXboxController detects state change from TRUE to FALSE.
2. Command Cancellation: whileTrue() trigger condition becomes false -> CommandScheduler cancels BeltInCommand.
3. end(true) Lifecycle Hook: CommandScheduler invokes BeltInCommand.end(true) with interrupted = true.
4. Subsystem Shutdown Method: BeltInCommand.end() calls beltSubsystem.stop().
5. Motor Voltage Cutoff: BeltSubsystem.stop() executes run(0.0) -> beltMotor.set(0.0), bringing PWM Port 5 output voltage back to zero.
Notes: Talking points - Releasing Button A changes the trigger from true to false. - whileTrue cancels BeltInCommand. - The scheduler calls end(true), and end() calls beltSubsystem.stop(). - BeltSubsystem sends zero output to the Talon on PWM port 5. Ask the room - Which method provides the safety behavior on release: execute(), isFinished(), or end()? Watch out for - The release does not wait for isFinished() to return true. The trigger cancels the command.

## Slide 22
SECTION 3
Project source code
Examining exact Java repository files: Constants.java, Subsystems, Commands, and RobotContainer.java.
Notes: Talking points - The repository section maps the runtime behavior onto actual Java files. - Keep VS Code open beside the slides and jump to the named file when a slide shows an excerpt. Ask the room - Which file would you open first to find a Button A binding? Watch out for - The slides show excerpts. Treat the repository as the source of truth for complete comments and current code.

## Slide 23
PROJECT SOURCE CODE
Project Directory Tree & Repository Structure
src/main/java/frc/robot/ ├── Main.java <- Entry point (starts Robot) ├── Robot.java <- 20ms CommandScheduler loop ├── RobotContainer.java <- Wiring hub & button bindings ├── Constants.java <- Hardware ports & tuning ├── subsystems/ │ ├── DriveSubsystem.java <- 4-motor tank drive │ ├── BeltSubsystem.java <- Ball transport belt │ ├── RollerSubsystem.java <- Outtake roller │ └── ClimberSubsystem.java <- One valve, two cylinders └── commands/ ├── DriveTeleopCommand.java ├── BeltInCommand.java ├── BeltOutCommand.java ├── RollerCommand.java ├── SlowDriveCommand.java └── ToggleClimberArmsCommand.java
Repository Class Roles:
• package frc.robot: Root package housing all robot Java source files.
• Constants.java: Central configuration hub containing static inner classes for hardware ports and tuning values.
• RobotContainer.java: Master wiring hub; instantiates hardware subsystems and connects controller triggers to commands.
• subsystems/: Folder containing SubsystemBase classes that encapsulate motor controllers and solenoids.
• commands/: Folder containing Command classes implementing action logic and lifecycle hooks.
Notes: Talking points - Main.java launches the program. Robot.java owns the TimedRobot lifecycle. - RobotContainer creates and connects controllers, subsystems, and commands. - Constants names hardware channels and tuning values. - ClimberSubsystem now owns one valve that controls two cylinders. Ask the room - Which folders contain hardware ownership? Which folder contains actions? VS Code - Expand src/main/java/frc/robot and match the Explorer tree to this slide.

## Slide 24
PROJECT SOURCE CODE
Centralized Configuration: Constants.java
Constants.java Structure • Hardware ports: Stores every PWM channel and the PCM module ID. • Climber valve: CLIMBER_SOLENOID_FORWARD and CLIMBER_SOLENOID_REVERSE identify PCM channels 0 and 1. • Climber commands: CLIMBER_ARMS_OUT and CLIMBER_ARMS_IN name the two valve states. • Operator and tuning groups: Store controller ports, motor speeds, drive scaling, and deadband values.
package frc.robot; import edu.wpi.first.wpilibj.DoubleSolenoid.Value; public final class Constants { private Constants() { } public static final class Hardware { public static final int PWM_FRONT_LEFT_DRIVE = 0; public static final int PWM_BACK_LEFT_DRIVE = 1; public static final int PWM_BACK_RIGHT_DRIVE = 2; public static final int PWM_FRONT_RIGHT_DRIVE = 3; public static final int PWM_ROLLER = 4; public static final int PWM_BELT = 5; public static final int PCM = 0; public static final int CLIMBER_SOLENOID_FORWARD = 0; public static final int CLIMBER_SOLENOID_REVERSE = 1; public static final Value CLIMBER_ARMS_OUT = Value.kForward; public static final Value CLIMBER_ARMS_IN = Value.kReverse; } }
Notes: Talking points - Constants replaces unexplained numbers with names that express hardware intent. - The climber uses one forward channel, one reverse channel, and two named valve states. - A channel constant describes wiring. A Value constant describes the requested valve direction. Ask the room - Why is CLIMBER_ARMS_OUT clearer than placing Value.kForward throughout the subsystem? Watch out for - Changing a constant cannot repair incorrect physical wiring. Software and wiring must describe the same robot. VS Code - Open Constants.java and show the additional hardware and tuning values omitted from the slide excerpt.

## Slide 25
PROJECT SOURCE CODE
Hardware Encapsulation: BeltSubsystem.java
BeltSubsystem Class Anatomy:
• Extends SubsystemBase: Inherits subsystem capabilities and automatic periodic() registration with the scheduler.
• Private Hardware Object: Private final Talon beltMotor hides raw PWM handle from external classes.
• run(double speed) API: Public method allowing commands to set motor output speed.
• stop() Method: Convenience API executing run(0.0) to command zero output.
package frc.robot.subsystems; import edu.wpi.first.wpilibj.motorcontrol.Talon; import edu.wpi.first.wpilibj2.command.SubsystemBase; import frc.robot.Constants; public class BeltSubsystem extends SubsystemBase { private final Talon beltMotor; public BeltSubsystem() { beltMotor = new Talon(Constants.Hardware.PWM_BELT); } public void run(double speed) { beltMotor.set(speed); } public void stop() { run(0.0); } }
Notes: Talking points - BeltSubsystem is the only class that owns the belt Talon. - Commands call run(speed) and stop() instead of touching PWM hardware. - stop() delegates to run(0), keeping motor output in one code path. Ask the room - What new test or safety rule becomes easier when all belt output passes through this subsystem? Watch out for - Encapsulation depends on keeping beltMotor private and avoiding a second Talon object for PWM port 5. VS Code - Open BeltSubsystem.java and compare the slide excerpt with the full NAME and DESCRIPTION comments.

## Slide 26
PROJECT SOURCE CODE
Action Execution Logic: BeltInCommand.java
BeltInCommand Class Anatomy:
• Constructor Requirement: Calls addRequirements(beltSubsystem) to declare exclusive hardware ownership.
• execute() Pass: Calls beltSubsystem.run(Constants.Tuning.BELT_SPEED) every 20ms.
• isFinished() = false: Returns false so the command continues running while Button A is held.
• end(boolean interrupted): Calls beltSubsystem.stop() when button is released or command is cancelled.
package frc.robot.commands; import edu.wpi.first.wpilibj2.command.Command; import frc.robot.Constants; import frc.robot.subsystems.BeltSubsystem; public class BeltInCommand extends Command { private final BeltSubsystem beltSubsystem; public BeltInCommand(BeltSubsystem beltSubsystem) { this.beltSubsystem = beltSubsystem; addRequirements(beltSubsystem); } @Override public void execute() { beltSubsystem.run(Constants.Tuning.BELT_SPEED); } @Override public void end(boolean interrupted) { beltSubsystem.stop(); } @Override public boolean isFinished() { return false; } }
2
end() returns the belt motor to zero output after release or interruption.
Notes: Talking points - The constructor stores the subsystem and declares its requirement. - execute() sends the configured inward speed. - isFinished() remains false, so the trigger controls cancellation. - The highlighted stop call handles release and interruption. Ask the room - Which two lines distinguish BeltInCommand from BeltOutCommand? Watch out for - A false isFinished() does not create an infinite blocking loop. It tells the scheduler to keep the command scheduled across normal cycles. VS Code - Open BeltInCommand.java and identify each lifecycle method.

## Slide 27
PROJECT SOURCE CODE
Robot Wiring & Event Bindings: RobotContainer.java
Central Event Wiring Hub:
• Instantiates Controllers & Subsystems: Instantiates driverController (Port 0), operatorController (Port 1), and all 4 hardware subsystems.
• configureBindings(): Connects Xbox triggers to commands (a().whileTrue(BeltIn), b().whileTrue(BeltOut), x().whileTrue(Roller), y().onTrue(ToggleClimber)).
• configureDefaultCommands(): Binds DriveTeleopCommand as default command on DriveSubsystem.
• Note: Code simplified for slide display.
// Note: Simplified code example for slide presentation public class RobotContainer { private final CommandXboxController driverController = new CommandXboxController(Constants.Operator.DRIVER_CONTROLLER); private final CommandXboxController operatorController = new CommandXboxController(Constants.Operator.OPERATOR_CONTROLLER); private final DriveSubsystem driveSubsystem = new DriveSubsystem(); private final BeltSubsystem beltSubsystem = new BeltSubsystem(); private void configureBindings() { // Operator Xbox Bindings operatorController.a().whileTrue(new BeltInCommand(beltSubsystem)); operatorController.b().whileTrue(new BeltOutCommand(beltSubsystem)); operatorController.x().whileTrue(new RollerCommand(rollerSubsystem)); operatorController.y().onTrue(new ToggleClimberArmsCommand(climberSubsystem)); // Driver Xbox Binding driverController.rightBumper().whileTrue(new SlowDriveCommand(driveSpeedMode)); } }
3
whileTrue starts on the press and cancels on the release.
Notes: Talking points - RobotContainer creates the controller objects and mechanism subsystems once. - configureBindings maps buttons to command instances. - The highlighted whileTrue calls encode press and release behavior. - The right bumper controls DriveSpeedMode rather than requiring DriveSubsystem directly. Ask the room - Why do the belt and roller use whileTrue while the climber uses onTrue? Watch out for - The slide is an excerpt. Use the live file to show constructor initialization and the default drive command. VS Code - Open RobotContainer.java and trace operatorController.a() through its command constructor.

## Slide 28
PROJECT SOURCE CODE
Button A across the Java files
1. Controller
Button A Press
2. Driver Station
USB HID Packet
3. RobotContainer
Trigger Binding
4. BeltInCommand
Lifecycle Hooks
5. BeltSubsystem
PWM 5 Motor Output
Repository File | Code Line / Method | Action Execution Responsibility
RobotContainer.java | operatorController.a().whileTrue(...) | Registers whileTrue trigger condition for Operator Button A.
BeltInCommand.java | public BeltInCommand(BeltSubsystem...) addRequirements(beltSubsystem); | Declares exclusive hardware requirement on BeltSubsystem.
BeltInCommand.java | execute() -> beltSubsystem.run(...) end() -> beltSubsystem.stop() | Commands belt speed in execute(); stops belt in end() on button release.
BeltSubsystem.java | run(double speed) -> beltMotor.set(speed) stop() -> run(0.0) | Sends speed setpoint directly to Talon motor controller on PWM Port 5.
Notes: Talking points - This is the third Button A visit. Students now know the hardware path and scheduler lifecycle, so trace the exact files. - RobotContainer creates the trigger, BeltInCommand expresses the action, and BeltSubsystem owns PWM port 5. Ask the room - If the belt runs but does not stop on release, which file and method would you inspect first? Watch out for - Keep the trace directional. Do not read every line of every file.

## Slide 29
SECTION 4
Practice and reference
Student code-tracing exercises, technical investigation questions, and hardware protocols.
Notes: Talking points - The final section asks students to apply the model instead of repeating definitions. - Explain that the next slide contains intentionally broken code. Ask the room - Which failure would you rather diagnose first: ownership, cleanup, or controller mapping? Watch out for - Give students time to predict behavior before revealing the fixes.

## Slide 30
PRACTICE AND REFERENCE
Spot the bug
BUG 1
class BeltOutCommand extends Command { BeltOutCommand(BeltSubsystem belt) { this.belt = belt; } }
Two belt commands can fight over the same motor.
BUG 2
@Override public void end(boolean interrupted) { // Nothing here }
What happens when the operator releases Button A?
BUG 3
DRIVER_CONTROLLER = 0; OPERATOR_CONTROLLER = 0;
Which physical controller will both objects read?
Pause here. Ask students to predict the robot behavior before advancing.
Notes: Talking points - Bug 1 omits addRequirements(), so the scheduler does not know the command claims BeltSubsystem. - Bug 2 omits motor cleanup from end(). - Bug 3 assigns both controller objects to USB slot 0. - Pause after each card and ask for a predicted robot symptom. Ask the room - Name the visible symptom, then name the missing or incorrect line. Watch out for - Do not reveal the answers while presenting this slide. Advance only after students commit to a diagnosis.

## Slide 31
PRACTICE AND REFERENCE
Bug fixes
FIX 1
addRequirements(belt);
The scheduler can now interrupt the current belt command before another belt command starts.
FIX 2
@Override public void end(boolean interrupted) { beltSubsystem.stop(); }
Releasing or interrupting the command returns the motor output to zero.
FIX 3
DRIVER_CONTROLLER = 0; OPERATOR_CONTROLLER = 1;
The driver and operator objects now read different Driver Station USB slots.
Notes: Talking points - Match each fix to the symptom students predicted. - addRequirements restores scheduler ownership. - beltSubsystem.stop() returns the motor to zero output. - Separate USB constants restore the intended driver and operator mappings. Ask the room - Which fix prevents a dangerous physical behavior, and which fix repairs input routing? Watch out for - The corrected lines work because the surrounding classes follow the same subsystem and command design shown earlier.

## Slide 32
PRACTICE AND REFERENCE
Hardware Protocol Appendix: PWM vs. CAN Bus
Feature | PWM Protocol (Current Robot Setup) | CAN Bus Protocol (Advanced Hardware)
Wiring Topology | Point-to-point 3-wire cable from roboRIO PWM port to each Talon SRX. | Daisy-chained 2-wire differential bus (CAN High / CAN Low) linking all motor controllers.
Signal Direction | One-way control signal (roboRIO -> Talon). No telemetry feedback. | Bi-directional data bus allowing real-time motor telemetry.
Telemetry Capabilities | Open-loop voltage control only. Cannot read motor temperature, current draw, or encoder position. | Full closed-loop telemetry (current, voltage, temperature, position, velocity).
Notes: Talking points - PWM sends a control pulse through individual roboRIO ports. - CAN carries addressed messages across a shared bus. - This project controls the Talon SRXs through PWM and connects the PCM through CAN. - Use the table as a comparison, not as a claim that the current motor code uses both protocols. Ask the room - What would need to change in the software and wiring to move a Talon SRX from PWM control to CAN control? Watch out for - CAN capability in the hardware does not prove that CAN control is configured in this repository.