## Slide 1
2020 FRC Robot Code Architecture & Implementation Guide
A Student's Technical Guide to Robot Hardware, WPILib Command-Based Architecture, and Java Code
Case Study: 4-Talon Drivetrain, Belt/Roller Transport, CTRE PCM Climber, and Dual CommandXboxControllers
Notes: Welcome students. This presentation breaks down how human operator inputs on an Xbox controller move physical hardware on our robot. We examine raw low-level control first, then build up to WPILib's pure Command-Based architecture.

## Slide 2
ROBOT HARDWARE
Physical Hardware Inventory & Actuator Channel Map
Actuator Channel Allocation
• Drivetrain: 4x Talon SRX Motor Controllers
- Left: PWM 0 (Front) & PWM 1 (Back)
- Right: PWM 3 (Front) & PWM 2 (Back)
• Ball Transport Belt: 1x Talon SRX on PWM 5
• Outtake Roller: 1x Talon SRX on PWM 4
• Climber Arms: 1x CTRE PCM (ID 0), Solenoid 0 & 1
• Power Distribution Board: PDB ID 1
Hardware Inversion & Wiring
• Symmetrical Mechanical Mounting:
Left and right drivetrain gearboxes are mounted facing opposite directions on the chassis.
• Software Sign Inversion:
leftDriveMotors.setInverted(true) aligns forward velocity vectors so positive values drive straight ahead.
• Open-Loop PWM Control:
roboRIO generates 1.0ms–2.0ms pulse-width signals to command output voltage.
Notes: Note the exact PWM port mappings: Front Left is PWM 0, Back Left is PWM 1, Front Right is PWM 3, Back Right is PWM 2. Because the gearboxes face opposite directions, inverting leftDriveMotors in software aligns forward motion.

## Slide 3
ROBOT HARDWARE
Running the Belt Motor in TimedRobot
// Direct Belt Test Program
package frc.robot;
import edu.wpi.first.wpilibj.TimedRobot;
import edu.wpi.first.wpilibj.motorcontrol.Talon;
public class Robot extends TimedRobot {
private final Talon beltMotor = new Talon(5);
@Override
public void teleopPeriodic() {
// Direct hardware actuation on PWM Port 5
beltMotor.set(0.25); // Runs belt inward at 25% power
}
}
Direct Control Mechanics
• Direct Hardware Handle:
Instantiates a raw Talon object directly tied to PWM Port 5.
• 50 Hz Synchronous Loop:
teleopPeriodic() executes every 20ms while teleop is active.
• Continuous Voltage Output:
Repeatedly sends +3.0V (25% of 12V bus) to the belt controller.
• Hardware Isolation:
Great for quick bench testing single mechanisms without framework overhead.
Notes: This bare-minimum TimedRobot program proves the belt motor and Talon controller on PWM 5 are wired correctly. Notice how teleopPeriodic executes continuously every 20 ms.

## Slide 4
ROBOT HARDWARE
Roller Challenge: Running the Roller Motor
// Direct Roller Test Program
package frc.robot;
import edu.wpi.first.wpilibj.TimedRobot;
import edu.wpi.first.wpilibj.motorcontrol.Talon;
public class Robot extends TimedRobot {
private final Talon rollerMotor = new Talon(4);
@Override
public void teleopPeriodic() {
// Identical pattern, targeting PWM Port 4
rollerMotor.set(0.25); // Spins ejection roller at 25%
}
}
What Changes From the Belt?
• Same Architectural Pattern:
Instantiates a Talon motor controller inside TimedRobot.
• Channel Target Change:
Constructed with PWM Port 4 instead of PWM Port 5.
• Independent Actuation Domain:
The outtake roller is a physically separate mechanism from the intake belt.
• Reusable Control Pattern:
Demonstrates how every open-loop PWM motor is initialized.
Notes: The roller program follows the exact same pattern as the belt demo, changing only the PWM port handle from 5 to 4.

## Slide 5
ROBOT HARDWARE
Pneumatic Climber Arms Control
// Direct Pneumatic Test Program
package frc.robot;
import edu.wpi.first.wpilibj.DoubleSolenoid;
import edu.wpi.first.wpilibj.PneumaticsModuleType;
import edu.wpi.first.wpilibj.TimedRobot;
public class Robot extends TimedRobot {
private final DoubleSolenoid climberSolenoid =
new DoubleSolenoid(0, PneumaticsModuleType.CTREPCM, 0, 1);
@Override
public void teleopPeriodic() {
// Extends climber solenoids on CTRE PCM ID 0
climberSolenoid.set(DoubleSolenoid.Value.kForward);
}
}
Pneumatic Control Mechanics
• Single CTRE PCM Valve:
Constructed on CAN PCM ID 0, Forward Channel 0, Reverse Channel 1.
• Split Air Lines:
One double-solenoid valve splits airflow via tee-fittings to both physical climber cylinders.
• Latching State:
Pneumatic solenoids maintain state once shifted until commanded otherwise.
Notes: Pneumatics use a DoubleSolenoid valve on CTRE PCM ID 0. A single valve controls both left and right climber arms together through split air lines.

## Slide 6
ROBOT HARDWARE
4-Motor Drivetrain Control & Safety Shutdown
// 4-Motor Drivetrain Test package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; public class Robot extends TimedRobot { private final Talon frontLeft = new Talon(0); private final Talon backLeft = new Talon(1); private final Talon frontRight = new Talon(3); private final Talon backRight = new Talon(2); @Override public void robotInit() { frontLeft.addFollower(backLeft); frontRight.addFollower(backRight); frontLeft.setInverted(true); } @Override public void teleopPeriodic() { frontLeft.set(0.15); frontRight.set(0.15); } }
Safety & Motor Limits
⚠️ SAFETY WARNING:
Elevate chassis on blocks off the floor before enabling test code!
• Correct PWM Mapping:
Front-Right is PWM 3, Back-Right is PWM 2. Left is PWM 0 & 1.
• Positive Voltages Drive Forward:
Because left is setInverted(true), passing +0.15 to both sides drives the robot forward.
• Automatic Safety Shutdown:
Disabling the robot commands the motor outputs to a safe disabled state.
Notes: Front-right uses PWM 3 and back-right uses PWM 2. robotInit() configures the followers and left-side inversion once. Commanding +0.15 to both leaders then drives both sides forward. Keep the chassis elevated on blocks during this test.

## Slide 7
ROBOT HARDWARE
Electrical Wiring & Pneumatic Routing Schematic
Point-to-Point Electrical Signals
• roboRIO PWM Header Distribution:
- PWM 0 -> Front Left Drive Talon SRX
- PWM 1 -> Back Left Drive Talon SRX
- PWM 2 -> Back Right Drive Talon SRX
- PWM 3 -> Front Right Drive Talon SRX
- PWM 4 -> Outtake Roller Talon SRX
- PWM 5 -> Ball Transport Belt Talon SRX
• CAN Bus Topology:
roboRIO CAN -> CTRE PCM (ID 0) -> PDP (ID 1)
Pneumatic Air Line Distribution
• Compressor & Main Pressure Regulator:
Main system pressure regulated to 60 PSI max.
• CTRE PCM Solenoid Module (ID 0):
- Channel 0: Forward Solenoid Line (Extend)
- Channel 1: Reverse Solenoid Line (Retract)
• Dual-Cylinder Split Tee Fittings:
Channel 0 splits to Left & Right Extend ports.
Channel 1 splits to Left & Right Retract ports.
Notes: This schematic illustrates physical signal distribution. Notice how PWM channels 0-5 wire point-to-point from the roboRIO, while the CAN bus links the PCM and PDP. A single PCM valve splits air to both climber cylinders.

## Slide 8
ROBOT HARDWARE
Human Controls & Dual CommandXboxController Mapping
DRIVER CONTROLLER (USB Port 0)
• Driving Responsibilities:
- Left Stick Y: Left-side tank drive speed
- Right Stick Y: Right-side tank drive speed
- Right Bumper (Held): Precision Slow Drive Mode (scales speed from 40% down to 20%)
• Axis Deadband Tuning:
- 0.08 deadband applied to suppress stick drift
OPERATOR CONTROLLER (USB Port 1)
• Mechanism Manipulation:
- Button A (Held): Runs Ball Transport Belt Inward (+1.0)
- Button B (Held): Runs Ball Transport Belt Outward (-1.0)
- Button X (Held): Runs Outtake Roller (+1.0)
- Button Y (Pressed): Toggles Pneumatic Climber Arms once
Notes: Driver commands chassis movement on USB Port 0 while Operator commands mechanisms on USB Port 1. Before enabling teleop during live tests, physically confirm the chassis is on blocks!

## Slide 9
ROBOT HARDWARE
Driver Station USB Setup & Live Telemetry Diagnostics
Driver Station USB Slot Index Rules
• USB Slot 0: Driver Xbox Controller
• USB Slot 1: Operator Xbox Controller
• Port-Swap Diagnostic Warning:
Plugging the Operator controller into USB Slot 0 swaps driver and mechanism controls on the physical robot!
• USB Order Lock:
Always verify USB slot index order in Driver Station before enabling.
Live Telemetry Diagnostics
• USB Input Indicator Grid:
Driver Station UI highlights active buttons in real time when physically depressed.
• Diagnostic Workflow:
1. Press Operator Button A -> Verify Button 1 illuminates on USB Slot 1.
2. Press Driver Right Bumper -> Verify Bumper illuminates on USB Slot 0.
Notes: Always check the Driver Station USB tab before enabling. USB indexes must match Driver = 0, Operator = 1.

## Slide 10
ROBOT HARDWARE
Reading Controller Inputs in TimedRobot
// Raw Controller Polling
package frc.robot;
import edu.wpi.first.wpilibj.TimedRobot;
import edu.wpi.first.wpilibj.XboxController;
import edu.wpi.first.wpilibj.motorcontrol.Talon;
public class Robot extends TimedRobot {
private final XboxController operator = new XboxController(1);
private final Talon beltMotor = new Talon(5);
@Override
public void teleopPeriodic() {
if (operator.getAButton()) {
beltMotor.set(0.25); // Button held
} else {
beltMotor.set(0.0); // Mandatory release cutoff
}
}
}
Manual Polling Mechanics
• Output Persistence Rule:
A motor controller retains its last commanded output until a new value is written or the robot is disabled.
• Mandatory Release Cutoff:
Without the else { set(0.0); } block, the previous motor output remains active until code writes a new value or the robot is disabled.
• Polling Scalability Bottleneck:
Manual if/else ladders grow unmaintainable across 10+ buttons.
Notes: A motor controller keeps its last command until code overwrites it or the robot is disabled. Manual polling therefore needs the else block to stop the belt when the operator releases Button A.

## Slide 11
ROBOT HARDWARE
Button A reaches PWM port 5
1. Controller (Button A)
2. Driver Station (USB Packet)
3. RobotContainer (Event Binding)
4. BeltInCommand (Lifecycle Hooks)
5. BeltSubsystem (PWM 5 Output)
Physical Signal Trace — Pass 1 Checkpoint
1. Physical Human Press: Operator's thumb depresses Button A on Xbox Controller (USB Port 1).
2. USB HID Packet: Windows Driver Station packages raw digital state into USB HID data frame.
3. Driver Station UDP Broadcast: Transmits 20ms UDP control packet across Wi-Fi / Ethernet to roboRIO.
4. roboRIO HAL / FPGA: NetComm daemon parses packet and updates DriverStation HAL state buffer.
5. Actuator Power Output: roboRIO FPGA emits 1.0ms–2.0ms PWM pulse on PWM Port 5, driving Talon SRX to +12V.
Notes: This is Checkpoint 1 of our Button A signal trace. Here we focus on the physical ends: human thumb press on the Xbox controller on USB 1, through the Driver Station UDP packet, to PWM Port 5 hardware output.

## Slide 12
COMMAND-BASED ROBOT CODE
Two Commands Request the Belt
A Concrete Engineering Conflict
• Operator Action 1:
Operator presses Button A -> Requests BeltInCommand (+1.0 speed).
• Operator Action 2 (Simultaneous):
Operator presses Button B -> Requests BeltOutCommand (-1.0 speed).
• Hardware Contention:
Both commands target the exact same Talon SRX motor controller on PWM Port 5.
• Unsafe 'Last Write Wins':
Without framework management, motor output depends on execution order. The result is deterministic, but brittle and unsafe.
The Architectural Solution
• Subsystem Resource Ownership:
Commands must declare which physical hardware mechanisms they require.
• CommandScheduler as Referee:
When a new command requests a busy subsystem, the scheduler interrupts the older command safely.
• Explicit Conflict Resolution:
Makes command ownership explicit and resolves the conflict safely.
Notes: Without subsystem requirements, both commands may write to the same motor during one scheduler pass. The later write wins. That behavior follows execution order, but it is brittle and unsafe.

## Slide 13
COMMAND-BASED ROBOT CODE
Subsystem Requirements & Hardware Exclusivity
// Declaring Requirements
public class BeltInCommand extends Command {
private final BeltSubsystem beltSubsystem;
public BeltInCommand(BeltSubsystem beltSubsystem) {
this.beltSubsystem = beltSubsystem;
// Registers resource requirement with scheduler referee
addRequirements(beltSubsystem);
}
}
Scheduler Ownership Rules
• Resource Registration:
addRequirements() registers the subsystem inside the CommandScheduler list.
• Logical Referee (Main Thread):
It acts as a scheduler referee on the single main loop thread—it is NOT an OS thread mutex.
• Interrupt Preemption:
If Button B schedules BeltOutCommand, the scheduler automatically cancels BeltInCommand and calls its end(true) method.
Notes: Emphasize to students: addRequirements() registers resource ownership inside the CommandScheduler list. It acts as a logical referee on the single main thread, not an OS thread mutex!

## Slide 14
COMMAND-BASED ROBOT CODE
Architectural Separation: Subsystems (HOW) vs. Commands (WHEN)
SUBSYSTEMS (SubsystemBase)
• Hardware Encapsulation (HOW):
Owns raw motor controllers, solenoids, and sensors in private fields.
• Public Mechanism API:
Exposes state-manipulation methods (e.g. run(speed), stop()).
• Decoupled Mechanisms:
BeltSubsystem, RollerSubsystem, DriveSubsystem, and ClimberSubsystem operate as independent domains.
COMMANDS (Command)
• Action Execution Rules (WHEN):
Dictates when, for how long, and under what conditions an action occurs.
• Resource Declarations:
Declares requirements via addRequirements() to lock hardware.
• Lifecycle Management:
Contains state machine logic across initialize(), execute(), isFinished(), and end().
Notes: Remember the core rule: Subsystems own the hardware and define HOW it moves. Commands contain the execution rules and dictate WHEN it moves.

## Slide 15
COMMAND-BASED ROBOT CODE
Trigger Bindings: whileTrue, onTrue, and setDefaultCommand
whileTrue(command)
• Momentary Control:
Schedules command when button is pressed; cancels it when released.
• Active Motor Actions:
Used for BeltInCommand, BeltOutCommand, RollerCommand.
• Automatic Cancellation:
Button release invokes end(true) to shut down motor.
onTrue(command)
• Rising-Edge Trigger:
Schedules command ONCE on button press transition.
• Instant State Actions:
Used for ToggleClimberArmsCommand.
• Self-Terminating:
Command ends immediately because its isFinished() returns true.
setDefaultCommand(...)
• Fallback Subsystem Action:
Runs automatically when no other command requires the subsystem.
• Continuous Control:
Used for DriveTeleopCommand on DriveSubsystem.
Notes: Note the distinction: onTrue schedules the command on the rising edge. ToggleClimberArmsCommand ends immediately because its own isFinished() method returns true!

## Slide 16
COMMAND-BASED ROBOT CODE
Polymorphic Command Lifecycle Method Hooks
initialize()
• Executed ONCE when command is first scheduled.
• Used to set up initial state, reset timers, or shift pneumatic valves.
execute()
• Executed repeatedly every 20ms pass while active.
• Sends continuous setpoints to motor controllers.
isFinished()
• Evaluated every 20ms pass to check for completion.
• Returns true to signal normal completion; false to keep running.
end(boolean interrupted)
• Executed ONCE when command finishes or is cancelled.
• Crucial for safety: shuts down motors (e.g. beltSubsystem.stop()).
Notes: These four lifecycle hooks govern every command. initialize runs once at start; execute and isFinished run every 20 ms pass; end runs when finished or cancelled.

## Slide 17
COMMAND-BASED ROBOT CODE
The Fixed 20ms Single-Threaded CommandScheduler Loop
WPILib 2026 Discrete 50 Hz Loop Pass Sequence
1. Subsystem periodic() -> Calls periodic() on all registered SubsystemBase objects to update telemetry/sensors.
2. Poll Triggers & Bindings -> Reads HID button state arrays and evaluates trigger conditions (whileTrue, onTrue).
3. Execute Active Commands -> Calls execute() on all active commands sequentially on the main thread.
4. Check Completion & Clean Up -> Evaluates isFinished() and calls end() on finished or interrupted commands.
5. Schedule Default Commands -> Schedules default commands for any unreserved subsystems.
⚠️ SINGLE-THREADED EXECUTION RULE:
Scheduler callbacks run serially on the main robot thread. Calling Thread.sleep() delays every other callback, causing loop-overrun warnings and watchdog timeouts!
Notes: Ask students: What happens if you call Thread.sleep(1000) inside execute()? Because the scheduler loop is single-threaded, sleep() delays all other callbacks, triggering loop overruns and watchdog timeouts!

## Slide 18
COMMAND-BASED ROBOT CODE
Releasing Button A stops the belt
1. Controller (Button A)
2. Driver Station (USB Packet)
3. RobotContainer (Event Binding)
4. BeltInCommand (Lifecycle Hooks)
5. BeltSubsystem (PWM 5 Output)
State Machine Cleanup Trace — Pass 2 Checkpoint
1. Trigger State Transition: Operator releases Button A -> whileTrue condition evaluates to false.
2. Scheduler Cancellation: The whileTrue binding cancels BeltInCommand when its condition becomes false.
3. Lifecycle Cleanup Hook: Scheduler invokes BeltInCommand.end(true) with interrupted = true.
4. Subsystem Shutdown Method: end() calls beltSubsystem.stop(), executing beltMotor.set(0.0).
5. Actuator Output Cutoff: Talon SRX cuts motor voltage output to zero.
Notes: This is Checkpoint 2. Releasing Button A makes the whileTrue condition false, so the scheduler cancels BeltInCommand. end(true) then calls beltSubsystem.stop().

## Slide 19
PROJECT SOURCE CODE
Project Directory Tree & Repository Structure
// Repository Package Layout
src/main/java/frc/robot/
├── Main.java <- Entry point
├── Robot.java <- 20ms scheduler loop
├── RobotContainer.java <- Wiring hub & button bindings
├── Constants.java <- Hardware channels & tuning
├── DriveSpeedMode.java <- Shared drive state
├── subsystems/
│ ├── DriveSubsystem.java <- 4-motor tank drive
│ ├── BeltSubsystem.java <- Transport belt motor
│ ├── RollerSubsystem.java <- Ejection roller motor
│ └── ClimberSubsystem.java <- Pneumatic climber valve
└── commands/
├── DriveTeleopCommand.java
├── BeltInCommand.java
├── BeltOutCommand.java
├── RollerCommand.java
├── SlowDriveCommand.java
└── ToggleClimberArmsCommand.java
Repository Class Roles
• package frc.robot:
Root package housing all robot source code.
• Constants.java:
Central read-only configuration hub for ports, IDs, and speeds.
• RobotContainer.java:
Master wiring hub; instantiates hardware and binds triggers.
• subsystems/:
Contains SubsystemBase classes encapsulating raw hardware.
• commands/:
Contains Command classes implementing lifecycle hooks.
Notes: Here is our actual repository directory tree. Notice how code is organized into root package, subsystems, and commands folders.

## Slide 20
PROJECT SOURCE CODE
Centralized Configuration: Constants.java
// Selected Constants.java fields // Hardware public static final int PWM_FRONT_LEFT_DRIVE = 0; public static final int PWM_BACK_LEFT_DRIVE = 1; public static final int PWM_BACK_RIGHT_DRIVE = 2; public static final int PWM_FRONT_RIGHT_DRIVE = 3; public static final int PWM_ROLLER = 4; public static final int PWM_BELT = 5; public static final int PCM = 0; public static final int PDB = 1; public static final int CLIMBER_SOLENOID_FORWARD = 0; public static final int CLIMBER_SOLENOID_REVERSE = 1; public static final Value CLIMBER_ARMS_OUT = Value.kForward; public static final Value CLIMBER_ARMS_IN = Value.kReverse; // Operator public static final int DRIVER_CONTROLLER = 0; public static final int OPERATOR_CONTROLLER = 1; // Tuning public static final double ROLLER_SPEED = 1.0; public static final double BELT_SPEED = 1.0; public static final double NORMAL_DRIVE_SCALE = 0.40; public static final double SLOW_DRIVE_SCALE = 0.20; public static final double DRIVE_DEADBAND = 0.08; public static final double DRIVE_SLEW_RATE_LIMIT = 0.8;
Notes: This focused excerpt shows the constants used by the hardware, controller, and tuning examples. Open the complete Constants.java file in VS Code to show its documentation and private constructors.

## Slide 21
PROJECT SOURCE CODE
Hardware Encapsulation: BeltSubsystem.java
// BeltSubsystem.java
package frc.robot.subsystems;
import edu.wpi.first.wpilibj.motorcontrol.Talon;
import edu.wpi.first.wpilibj2.command.SubsystemBase;
import frc.robot.Constants;
/**
* NAME: BeltSubsystem - owns the ball-transport belt motor.
*/
public class BeltSubsystem extends SubsystemBase {
private final Talon beltMotor;
public BeltSubsystem() {
beltMotor = new Talon(Constants.Hardware.PWM_BELT);
}
public void run(double speed) {
beltMotor.set(speed);
}
public void stop() {
run(0.0); // Safe motor output cutoff
}
}
Notes: BeltSubsystem encapsulates the Talon motor controller on PWM 5 in a private field. Its public API provides run(speed) and stop().

## Slide 22
PROJECT SOURCE CODE
Action Execution Logic: BeltInCommand.java
// BeltInCommand.java (key methods) public class BeltInCommand extends Command { private final BeltSubsystem beltSubsystem; public BeltInCommand(BeltSubsystem beltSubsystem) { this.beltSubsystem = beltSubsystem; addRequirements(beltSubsystem); } @Override public void execute() { beltSubsystem.run(Constants.Tuning.BELT_SPEED); } @Override public void end(boolean interrupted) { beltSubsystem.stop(); } @Override public boolean isFinished() { return false; } }
Notes: This slide keeps the three methods that explain the command. The constructor claims BeltSubsystem, execute() runs the motor, and end() stops it. Show the complete file in VS Code if students need the package, imports, and documentation header.

## Slide 23
PROJECT SOURCE CODE
Robot Wiring & Event Bindings: RobotContainer.java
// RobotContainer.java (focused excerpt) public RobotContainer() { driverController = new CommandXboxController(Constants.Operator.DRIVER_CONTROLLER); operatorController = new CommandXboxController(Constants.Operator.OPERATOR_CONTROLLER); driveSubsystem = new DriveSubsystem(); climberSubsystem = new ClimberSubsystem(); beltSubsystem = new BeltSubsystem(); rollerSubsystem = new RollerSubsystem(); driveSpeedMode = new DriveSpeedMode(); configureDefaultCommands(); configureBindings(); } private void configureBindings() { operatorController.y().onTrue(new ToggleClimberArmsCommand(climberSubsystem)); operatorController.a().whileTrue(new BeltInCommand(beltSubsystem)); operatorController.b().whileTrue(new BeltOutCommand(beltSubsystem)); operatorController.x().whileTrue(new RollerCommand(rollerSubsystem)); driverController.rightBumper().whileTrue(new SlowDriveCommand(driveSpeedMode)); }
Notes: This focused excerpt matches the repository constructor and configureBindings() method. RobotContainer creates the controllers, subsystems, and drive-speed state before installing defaults and button bindings. Show the complete file in VS Code.

## Slide 24
PROJECT SOURCE CODE
Button A across the Java files
1. Controller (Button A)
2. Driver Station (USB Packet)
3. RobotContainer (Event Binding)
4. BeltInCommand (Lifecycle Hooks)
5. BeltSubsystem (PWM 5 Output)
Java Execution Path — Pass 3 Checkpoint
1. RobotContainer.java: operatorController.a().whileTrue(new BeltInCommand(beltSubsystem));
2. WPILib CommandScheduler: Evaluates the Button A trigger during the 20ms scheduler pass.
3. BeltInCommand.java: Constructor executes addRequirements(beltSubsystem); execute() runs every 20ms.
4. BeltSubsystem.java: run(Constants.Tuning.BELT_SPEED) executes beltMotor.set(1.0);
5. Constants.java: Hardware.PWM_BELT = 5 and Tuning.BELT_SPEED = 1.0 supply static channel & speed parameters.
Notes: This is Checkpoint 3. The path begins in the repository binding, passes through WPILib CommandScheduler, and returns to BeltInCommand, BeltSubsystem, and Constants. CommandScheduler belongs to WPILib, not this repository.

## Slide 25
PRACTICE AND REFERENCE
Spot the Bug: Classroom Debugging Challenges
BUG 1: Missing addRequirements
Code Snippet:
public BeltInCommand(BeltSubsystem belt) {
this.belt = belt;
// addRequirements(belt); OMITTED!
}
Question:
What happens when the operator presses Button A and Button B simultaneously?
BUG 2: Empty end() Method
Code Snippet:
public void end(boolean interrupted) {
// Left empty!
}
Question:
When the operator releases Button A, what happens to the physical belt motor?
BUG 3: Duplicate USB Slots
Code Snippet:
public static final class Operator {
public static final int DRIVER_CONTROLLER = 0;
public static final int OPERATOR_CONTROLLER = 0;
}
Question:
What happens when the robot is enabled on the field?
Notes: Present these three bugs to the class. Have students analyze what goes wrong in each case before advancing to the fix slide!

## Slide 26
PRACTICE AND REFERENCE
Spot the Bug: Solutions & Exact Code Fixes
FIX 1: Add addRequirements
Symptom: Last write wins, causing unsafe motor fighting.
Exact Fix:
public BeltInCommand(BeltSubsystem belt) {
this.belt = belt;
addRequirements(belt); // Solved!
}
FIX 2: Call stop() in end()
Symptom: Motor keeps its last output after release until code writes a new value or the robot is disabled.
Exact Fix:
public void end(boolean interrupted) {
beltSubsystem.stop(); // Solved!
}
FIX 3: Assign Unique USB Ports
Symptom: Driver & Operator controls clash on USB Slot 0.
Exact Fix:
public static final class Operator {
public static final int DRIVER_CONTROLLER = 0;
public static final int OPERATOR_CONTROLLER = 1; // Solved!
}
Notes: Fix 1 gives the scheduler exclusive ownership information. Fix 2 writes zero when the command ends. Fix 3 assigns distinct USB slots to the driver and operator controllers.