## Slide 1
2020 FRC Robot Code Architecture & Implementation Guide
A Student's Technical Guide to Robot Hardware, WPILib Command-Based Architecture, and Java Code
Case Study: 4-Talon Drivetrain, Belt/Roller Transport, CTRE PCM Climber, and Dual CommandXboxControllers
Notes: Welcome students. This presentation breaks down how human operator inputs on an Xbox controller move physical hardware on our robot. We examine raw low-level control first, then build up to WPILib's pure Command-Based architecture.

## Slide 2
ROBOT HARDWARE
From hardware tests to a complete robot program
First, prove that the hardware works 1. Identify each motor, valve, port, and controller. 2. Run one component at a time with short TimedRobot programs. 3. Read a controller button and stop the output when the button is released.
Then, organize the complete robot 4. Use subsystems, commands, button bindings, and the scheduler. 5. Follow Button A through the real project code. 6. Practice finding common mistakes.
Notes: This slide gives students the route through the presentation. We begin with the physical robot and very small programs. Those programs prove that the ports, wiring, motors, and pneumatic valve work. We then add a controller button so the operator can start and stop a mechanism. After that, we move to command-based code. Command-based programming organizes the same hardware actions into subsystems, commands, button bindings, and scheduler rules. The final part of the presentation follows Button A through the real repository and uses short debugging exercises to check understanding. Students do not need to memorize this list. Its purpose is to show how the early hardware examples connect to the final robot program.

## Slide 3
ROBOT HARDWARE
Physical Hardware Inventory & Actuator Channel Map
Actuator Channel Allocation
• Drivetrain: 4x Talon SRX Motor Controllers
- Left: PWM 0 (Front) & PWM 1 (Back)
- Right: PWM 3 (Front) & PWM 2 (Back)
• Ball Transport Belt: 1x Talon SRX on PWM 5
• Outtake Roller: 1x Talon SRX on PWM 4
• Climber Arms: 1x CTRE PCM (ID 0), Solenoid 0 & 1
• Power Distribution Panel (PDP)
Hardware Inversion & Wiring
• Symmetrical Mechanical Mounting:
Left and right drivetrain gearboxes are mounted facing opposite directions on the chassis.
• Software Sign Inversion:
leftDriveMotors.setInverted(true) aligns forward velocity vectors so positive values drive straight ahead.
• Motor control:
The roboRIO tells each motor controller how fast and which direction to run.
Notes: What is an actuator? An actuator is a device that turns a robot command into physical movement. Motors spin, and pneumatic cylinders push or pull.
Note the exact PWM port mappings: Front Left is PWM 0, Back Left is PWM 1, Front Right is PWM 3, Back Right is PWM 2. Because the gearboxes face opposite directions, inverting leftDriveMotors in software aligns forward motion.

## Slide 4
ROBOT HARDWARE
Direct hardware tests
Five single-component demos
• Belt motor on PWM 5
• Roller motor on PWM 4
• Climber valve on PCM 0
• Drivetrain motors on PWM 0 through 3
Reading controller inputs
Each program contains only the hardware it operates.
How each demo works
• Load one Robot.java file at a time.
• teleopPeriodic() sends one fixed output.
• Driver Station Enable starts the test.
• Disable stops the test.
• No Xbox input for the 1st 4 demos
• No command-based classes yet.
Raise the drivetrain off the floor before enabling.
Notes: We will first use the shortest possible path from Java to the hardware.
Each temporary Robot.java program operates one mechanism directly.
These tests confirm ports, wiring, direction, and basic device control before controller input or command-based structure enters the picture.
Ask students what must happen between a number in Java and physical motion.

## Slide 5
TIMEDROBOT BASICS
TimedRobot runs the robot program
WPILib provides the loop • Starts the robot program. • Calls our robot methods. • Waits for the next cycle. • Repeats about every 20 ms.
We fill in the methods • Robot extends TimedRobot. • Our methods contain the robot code. • Each method finishes and returns to WPILib. • We do not write the repeating loop.
Notes: Before showing the belt program, explain who calls teleopPeriodic(). WPILib does. Robot extends TimedRobot. That gives the program WPILib's repeating robot loop. We provide methods that TimedRobot calls at the correct time. The normal loop period is about 20 milliseconds. That means WPILib gives the program another chance to read inputs and update outputs about 50 times each second. Our methods should do a small amount of work and return. We do not place our own repeating while loop inside teleopPeriodic(). We also avoid Thread.sleep() because it delays the whole robot loop. Ask the class: Who calls teleopPeriodic()? The answer is TimedRobot through WPILib. Our code overrides the method, but our code does not call it directly. Transition: TimedRobot chooses which methods to call based on the robot's current mode. Source: https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj/TimedRobot.html

## Slide 6
TIMEDROBOT BASICS
TimedRobot calls methods for the current mode
Called for the whole robot robotInit() Runs once when the program starts. robotPeriodic() Runs about every 20 ms in every mode.
Based on selected mode run when enabled: teleopPeriodic()
autonomousPeriodic()
disabledPeriodic() testPeriodic()
Runs about every 20 ms
Notes: TimedRobot calls robotInit() once when the robot program starts. We use it to create the objects and perform setup that the program needs before the repeating loop begins. During each normal loop, TimedRobot calls robotPeriodic(). It also calls the periodic method for the current Driver Station mode. If the robot is disabled, disabledPeriodic() runs. During autonomous, autonomousPeriodic() runs. During operator control, teleopPeriodic() runs. Test mode uses testPeriodic(). Mode-specific init methods also exist. For example, teleopInit() runs once when teleoperated mode begins. Keep that detail in the notes for now because the next demonstrations only need teleopPeriodic(). Connect this slide directly to the demonstrations that follow. The belt, roller, climber, and drivetrain examples place one hardware instruction in teleopPeriodic(). When the instructor enables teleoperated mode, TimedRobot calls that method repeatedly. Disabling the robot stops the hardware outputs. Preview the finished program without teaching the scheduler yet. Later, robotPeriodic() will call the command scheduler. TimedRobot will still provide the repeating loop underneath the command-based code. Ask the class: While the robot is in teleoperated mode, which two repeating methods run? The expected answer is robotPeriodic() and teleopPeriodic(). Source: https://github.wpilib.org/allwpilib/docs/release/java/edu/wpi/first/wpilibj/IterativeRobotBase.html

## Slide 7
ROBOT HARDWARE
Running the Belt Motor in TimedRobot
// Direct Belt Test Program
package frc.robot;
import edu.wpi.first.wpilibj.TimedRobot;
import edu.wpi.first.wpilibj.motorcontrol.Talon;
public class Robot extends TimedRobot {
private final Talon beltMotor = new Talon(5);
@Override
public void teleopPeriodic() {
// Direct hardware actuation on PWM Port 5
beltMotor.set(0.25); // Runs belt inward at 25% power
}
}
Direct Control Mechanics
• Direct Hardware Handle:
Instantiates a raw Talon object directly tied to PWM Port 5.
• 50 Hz Synchronous Loop:
teleopPeriodic() executes every 20ms while teleop is active.
• Continuous Voltage Output:
Repeatedly sends +3.0V (25% of 12V bus) to the belt controller.
• Hardware Isolation:
Great for quick bench testing single mechanisms without framework overhead.
Notes: This bare-minimum TimedRobot program proves the belt motor and Talon controller on PWM 5 are wired correctly.
Notice how teleopPeriodic executes continuously every 20 ms. Two main things: 1. create an object to control the motor with the new Talon statement
2. Run the motor with the .set statement

## Slide 8
ROBOT HARDWARE
Running the Roller Motor
// Direct Roller Test Program
package frc.robot;
import edu.wpi.first.wpilibj.TimedRobot;
import edu.wpi.first.wpilibj.motorcontrol.Talon;
public class Robot extends TimedRobot {
private final Talon rollerMotor = new Talon(4);
@Override
public void teleopPeriodic() {
// Identical pattern, targeting PWM Port 4
rollerMotor.set(0.25); // Spins ejection roller at 25%
}
}
What Changes From the Belt?
• Same Architectural Pattern:
Instantiates a Talon motor controller inside TimedRobot.
• Channel Target Change:
Constructed with PWM Port 4 instead of PWM Port 5.
• Independent Actuation Domain:
The outtake roller is a physically separate mechanism from the intake belt.
• Reusable Control Pattern:
Demonstrates how every open-loop PWM motor is initialized.
Notes: The roller program follows the exact same pattern as the belt demo, changing only the PWM port handle from 5 to 4. Flip between this slide and the previous to show the changes. Same idea but 2 different motors/subsystems
Make them look at the roborio and seem the wiring for these 2 motors from thw PWM port to the talon motor controller

## Slide 9
ROBOT HARDWARE
Pneumatic Climber Arms Control
// Direct Pneumatic Test Program
package frc.robot;
import edu.wpi.first.wpilibj.DoubleSolenoid;
import edu.wpi.first.wpilibj.PneumaticsModuleType;
import edu.wpi.first.wpilibj.TimedRobot;
public class Robot extends TimedRobot {
private final DoubleSolenoid climberSolenoid =
new DoubleSolenoid(0, PneumaticsModuleType.CTREPCM, 0, 1);
@Override
public void teleopPeriodic() {
// Extends climber solenoids on CTRE PCM ID 0
climberSolenoid.set(DoubleSolenoid.Value.kForward);
}
}
Pneumatic Control Mechanics
• Single CTRE PCM Valve:
Constructed on CAN PCM ID 0, Forward Channel 0, Reverse Channel 1.
• Split Air Lines:
One double-solenoid valve splits airflow via tee-fittings to both physical climber cylinders.
• Latching State:
Pneumatic solenoids maintain state once shifted until commanded otherwise.
Notes: A single valve controls both left and right climber arms together through split air lines. Pneumatics use a DoubleSolenoid valve connected to a CTRE Pneumatics Control Module (PCM) CAN ID 0. channels 0 and 1.
See the pattern is similar even if the hardware is very different: 1. create the object that controls the hardware
2. Give a command (.set) to change the state of the hardware Look at the robot PCM module to see what the channel numbers mean
How many channels can the PCM handle?
What happens if you need more channels?
Constructor args - PCM CAN ID, module type, forward channel, reverse channel
public DoubleSolenoid(
final int module,
final PneumaticsModuleType moduleType,
final int forwardChannel,
final int reverseChannel)
In our real code that you will see later we won’t use literal numbers like 0, 1, etc. We will use names that make it clear what the numbers are being used for
climberSolenoid = new DoubleSolenoid(
Constants.Hardware.PCM,
PneumaticsModuleType.CTREPCM,
Constants.Hardware.CLIMBER_SOLENOID_FORWARD,
Constants.Hardware.CLIMBER_SOLENOID_REVERSE);

## Slide 10
ROBOT HARDWARE
4-Motor Drivetrain Control & Safety Shutdown
// 4-Motor Drivetrain Test package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; public class Robot extends TimedRobot { private final Talon frontLeft = new Talon(0); private final Talon backLeft = new Talon(1); private final Talon frontRight = new Talon(3); private final Talon backRight = new Talon(2); @Override public void robotInit() { frontLeft.addFollower(backLeft); frontRight.addFollower(backRight); frontLeft.setInverted(true); } @Override public void teleopPeriodic() { frontLeft.set(0.15); frontRight.set(0.15); } }
Safety & Motor Limits
⚠️ SAFETY WARNING:
Elevate chassis on blocks off the floor before enabling test code!
• Correct PWM Mapping:
Front-Right is PWM 3, Back-Right is PWM 2. Left is PWM 0 & 1.
• Positive Voltages Drive Forward:
Because left is setInverted(true), passing +0.15 to both sides drives the robot forward.
• Automatic Safety Shutdown:
Disabling the robot commands the motor outputs to a safe disabled state.
Notes: This is similar to the other motor demos except it show how to use all the motors together to create the drivetrain.
Front-right uses PWM 3 and back-right uses PWM 2.
Note how robotInit() configures the followers and left-side inversion once.
Why do you think the inversion is necessary?
Commanding +0.15 to both leaders then drives both sides forward. Keep the chassis elevated on blocks during this test.

## Slide 11
ROBOT HARDWARE
How the hardware tests connect to the robot
Electrical connections used in the tests • PWM 0: Front-left drive motor • PWM 1: Back-left drive motor • PWM 2: Back-right drive motor • PWM 3: Front-right drive motor • PWM 4: Roller motor • PWM 5: Belt motor The CAN bus connects the roboRIO, PCM 0, and PDP.
Pneumatic connections used in the climber test • PCM 0 controls one double-solenoid valve. • Channel 0 extends the climber arms. • Channel 1 retracts the climber arms. • Tee fittings split each air line between the two cylinders. Both cylinders move from the same valve command.
Notes: This slide brings the four direct hardware tests together on one robot. On the electrical side, each PWM number identifies one roboRIO output. The number used in the Java constructor must match the physical port used by the signal cable. The drivetrain uses ports 0 through 3. The roller uses port 4, and the belt uses port 5. The PCM communicates with the roboRIO over the CAN bus. The PDP stays connected at the far end of the standard CAN wiring because it contains the second CAN termination resistor. This project does not create a PDP object or refer to a PDP CAN ID in Java code. On the pneumatic side, the robot has one double-solenoid valve for the climber. Each valve output splits through a tee fitting, so the two cylinders extend and retract together. This is a summary of the hardware used in the direct tests. The next slides add the two Xbox controllers.

## Slide 12
ROBOT HARDWARE
XboxController Mapping
DRIVER CONTROLLER (USB Port 0)
• Driving Responsibilities:
- Left Stick Y: Left-side tank drive speed
- Right Stick Y: Right-side tank drive speed
- both stick forward to go forward.
- Both backward to go backward
- differ positions between the two to turn - Right Bumper (Held): Precision Slow Drive Mode (scales speed from 40% down to 20%)
• Axis Deadband Tuning:
- 0.08 deadband applied to suppress stick drift
OPERATOR CONTROLLER (USB Port 1)
• Mechanism Manipulation:
- Button A (Held): Runs Ball Transport Belt Inward (+1.0)
- Button B (Held): Runs Ball Transport Belt Outward (-1.0)
- Button X (Held): Runs Outtake Roller (+1.0)
- Button Y (Pressed): Toggles Pneumatic Climber Arms once
Take a break - Drive the robot!!!!
Notes: We use 2 xbox controllers to run this robot. Driver commands chassis movement with the xbox controller on USB Port 0
Operator commands mechanisms with the controller on USB Port 1. Take a break from the presentation and drive/operate the robot but do the next slide first!
Caution - Before enabling teleop during live tests, physically confirm the chassis is on blocks or in a well spaced area to handle robot movement

## Slide 13
ROBOT HARDWARE
Driver Station USB setup and live controller check
Match each controller to its software port • USB port 0: Driver controller • USB port 1: Operator controller Before enabling the robot, confirm that the controllers appear in this order. Swapping them also swaps their controls.
Press a controller button and watch the matching indicator. • Operator A should appear on USB port 1. • Driver right bumper should appear on USB port 0.
Notes: Open the USB tab in Driver Station before enabling the robot. The software creates the driver controller on port 0 and the operator controller on port 1. Driver Station must show the physical controllers in the same positions. If the controllers are reversed, the robot code still runs, but each person receives the other controller's assignments. Use the live indicators to verify the mapping. Press A on the operator controller and confirm that Button 1 changes on USB port 1. Press the right bumper on the driver controller and confirm that the matching indicator changes on USB port 0. This test separates a controller or USB-order problem from a Java-code problem. If Driver Station does not show the button changing, inspect the controller connection and USB order before debugging the command code.

## Slide 14
ROBOT HARDWARE
Reading controller inputs in TimedRobot
// Raw Controller Polling
package frc.robot;
import edu.wpi.first.wpilibj.TimedRobot;
import edu.wpi.first.wpilibj.XboxController;
import edu.wpi.first.wpilibj.motorcontrol.Talon;
public class Robot extends TimedRobot {
private final XboxController operator = new XboxController(1);
private final Talon beltMotor = new Talon(5);
@Override
public void teleopPeriodic() {
if (operator.getAButton()) {
beltMotor.set(0.25); // Button held
} else {
beltMotor.set(0.0); // Mandatory release cutoff
}
}
}
What this code must do • A held: write 0.25 to the belt motor. • A released: write 0.0 so the motor stops. This gets complicated quickly. Each new action adds another condition to manage.
Notes: This is the simplest controller version of the belt demo. The program checks Button A every time teleopPeriodic runs. While the button is held, the code sends 0.25 to the belt motor. When the button is released, the else block sends 0.0. The else block matters because a motor controller keeps its last requested output until the program writes a new value or the robot is disabled. Reading a false button value does not stop the motor by itself. This pattern works for one button. As the robot gains more buttons and mechanisms, teleopPeriodic fills with conditions that start actions, stop actions, and decide which action wins. Command-based programming gives those responsibilities clear places.

## Slide 15
ROBOT HARDWARE
How Button A starts the belt
1. Button A pressed
2. Driver Station sends input
3. Robot code sees input
4. Belt code runs
5. Belt motor turns
Follow the path for now 1. The operator presses Button A. 2. Driver Station sends the button state to the robot. 3. The robot program sees that A is pressed. 4. The program runs the code that moves the belt inward. 5. That code sends output to the belt motor on PWM port 5. Next, we will see how command-based programming organizes these jobs.
Notes: This is the same basic process we saw in the TimedRobot demonstration. The operator presses Button A, and Driver Station sends that information to the robot. The robot program sees that the button is pressed and runs the code that moves the belt inward. That code sends an output through PWM port 5 to the belt motor controller. A more coplex robot needs to repeat this process for many buttons and mechanisms. If we put every button check and motor instruction inside teleopPeriodic(), the method will become difficult to manage. The next slide introduces the way command-based programming divides these jobs into smaller, organized parts.

## Slide 16
COMMAND-BASED ROBOT CODE
Command-based robot code
A command-based robot is a way to organize the robot code • Subsystems control one mechanism, such as the belt. • Commands describe actions, such as running the belt inward or raising the climber. • Button bindings connect controller buttons to commands.
• The scheduler starts, runs, and stops commands. • The scheduler also handles conflicts so that two commands cannot control the same subsystem at once. Each responsibility has a clear place.
Notes: So far, we have controlled each device directly. That is a good way to prove that the wiring, ports, and basic code work. Our finished robot has a drivetrain, a belt, a roller, a climber, and two controllers. Putting all of that behavior into one large teleopPeriodic method would become difficult to read and change. Command-based programming is another way of organizing a robot program. It does not change how a motor or controller works. It gives each part of the program a clear job.
There are a few major concepts to understand command based robot programming
subsystems, commands, buttons bindings, command scheduling, conflict resolution, ???
A subsystem contains the code for one mechanism. BeltSubsystem controls the belt motor.
Subsystems are hardware grouping needed to handle a specific function. It may be a single component like a motor or multiple motors, sensors etc.
It usually has the code in it that directly controls the hardware like in our demo code at the start of this presentation.
A command describes one action. BeltInCommand means run the belt inward.
A button binding connects an operator input to a command. For example, in this project, the A button starts BeltInCommand. The scheduler runs the commands. It starts them, calls them while they are active, and stops them when they end.
The scheduler also handles conflicts. If two commands need the same subsystem, it does not let both control that subsystem at once. This slide is only the big picture. The next slides explain each part before we return to the belt example.

## Slide 17
COMMAND-BASED ROBOT CODE
Subsystems and commands have different jobs
Subsystems control hardware • A subsystem owns one or more of the robot’s motors, valves, or sensors. • It provides methods such as run(speed) and stop(). • Each robot mechanism has its own subsystem.
Commands describe actions • A command tells a subsystem what action to perform. • It declares which subsystem it needs. • The scheduler calls its methods as the action starts, runs, and ends.
Notes: Subsystems and commands have different jobs.
A subsystem controls a part of the robot’s hardware. For example, BeltSubsystem owns the belt motor controller and provides methods to run and stop the belt.
A command uses those methods to perform a specific action. BeltInCommand runs the belt at the intake speed. BeltOutCommand runs it in the opposite direction.
The motor-control code stays in one place. Button controls and autonomous code can both use the same subsystem methods without copying that code.
A subsystem may control more than one hardware device. For example, our ShooterSubsystem controlled two flywheel motors, a feeder motor, and several encoders. The subsystem contained the code for running those devices and measuring flywheel speed. The shoot command controlled the sequence: start the flywheels, wait until they reach the requested speed, and then run the feeder to shoot the ball. The intake was a separate mechanism, so it belonged in its own subsystem.
The simple division is:
Subsystems control the hardware. Commands organize the actions and timing.
We will deal with more complex examples like this in future presentations.

## Slide 18
COMMAND-BASED ROBOT CODE
BeltSubsystem provides methods for controlling the belt
// BeltSubsystem.java
package frc.robot.subsystems;
import edu.wpi.first.wpilibj.motorcontrol.Talon;
import edu.wpi.first.wpilibj2.command.SubsystemBase;
import frc.robot.Constants;
/**
* NAME: BeltSubsystem - owns the ball-transport belt motor.
*/
public class BeltSubsystem extends SubsystemBase {
private final Talon beltMotor;
public BeltSubsystem() {
beltMotor = new Talon(Constants.Hardware.PWM_BELT);
}
public void run(double speed) {
beltMotor.set(speed);
}
public void stop() {
run(0.0); // Safe motor output cutoff
}
}
Notes: This is the first complete subsystem from the project. The private Talon field is the motor controller owned by BeltSubsystem. Keeping it private means commands cannot reach around the subsystem and control the motor directly. The constructor creates the Talon using the PWM port stored in Constants. The run(speed) method sends a requested speed to the motor controller. The stop() method calls run(0), which gives the motor a zero output. The public run() and stop() methods are the small set of controls that the rest of the robot program uses. Programmers often call this set of public methods an API. The next slides show how a button starts a command and how that command uses these subsystem methods.

## Slide 19
COMMAND-BASED ROBOT CODE
Button bindings can start and stop commands
whileTrue(...)
Starts the command when the button is pressed Cancels it when the button is released. Used for held-button controls.
onTrue(...)
Starts the command once when the button is pressed. Used to toggle the climber arms.
Default command
Runs whenever no other command is using that subsystem. Used for normal driving.
Notes: A button binding connects an input to a command. It’s how you tell the system to run commands when a controller button is press or used
This slide shows 3 examples. There are more and they can be more complex.
whileTrue is useful for actions that should last only while the operator holds a button.
For example in our code pressing A starts BeltInCommand.
Releasing A cancels it, which causes the command's end method to stop the belt. onTrue starts a command once when the button changes from released to pressed.
In this robot’s code the climber toggle uses onTrue because one press should cause one change of state. A default command runs whenever its subsystem is available.
On this robot the DriveTeleopCommand is the default for DriveSubsystem,
so normal driving resumes whenever another drive command is not using the drivetrain.
Remember: a default command runs whenever no other command is using its subsystem.

## Slide 20
COMMAND-BASED ROBOT CODE
The scheduler calls four methods as a command runs
initialize()
Runs once when the command starts. Prepares the action.
execute()
Runs repeatedly while the command is active. Keeps the action running.
isFinished()
Returns true when the command is done. False keeps it running.
end(interrupted)
Runs once when the command stops. Stops motors safely.
Notes: WPILib calls these methods for us. initialize runs once when the scheduler starts a command. execute then runs repeatedly while the command remains active. isFinished tells the scheduler whether the command has completed normally. end runs once when the command finishes or is interrupted. BeltInCommand does not need initialize, so it uses the empty default implementation. Its execute method runs the belt. Its isFinished method returns false because the button binding controls how long it runs. Its end method stops the belt. The important safety habit is simple: if execute starts a motor, end should normally stop it.

## Slide 21
COMMAND-BASED ROBOT CODE
BeltInCommand runs from button press to release
// BeltInCommand.java (key methods) public class BeltInCommand extends Command { private final BeltSubsystem beltSubsystem; public BeltInCommand(BeltSubsystem beltSubsystem) { this.beltSubsystem = beltSubsystem; addRequirements(beltSubsystem); } @Override public void execute() { beltSubsystem.run(Constants.Tuning.BELT_SPEED); } @Override public void end(boolean interrupted) { beltSubsystem.stop(); } @Override public boolean isFinished() { return false; } }
Notes: This is the first complete command example from the project. It uses the BeltSubsystem methods from the earlier slide. The constructor receives BeltSubsystem and saves it in a field. The addRequirements line tells the scheduler that this command needs the belt. Point out the line now, but tell students that the later conflict example will explain why it matters. While the command is active, execute() repeatedly calls beltSubsystem.run() with the configured belt speed. isFinished() returns false, so the command does not finish on its own. The whileTrue button binding controls how long it remains active. This command does not override initialize() because it has no work that needs to happen only once when the command starts. WPILib uses the empty default implementation. When the operator releases the button or another command interrupts this one, the scheduler calls end(). The end() method calls beltSubsystem.stop(), which sends zero output to the motor.

## Slide 22
COMMAND-BASED ROBOT CODE
Robot.java calls the scheduler every cycle
/** NAME: robotPeriodic - runs the command scheduler every robot packet. */ @Override public void robotPeriodic() { // Command-based robots run bindings and default commands through the scheduler every cycle. CommandScheduler.getInstance().run(); }
Notes: This slide shows the actual robotPeriodic() method from Robot.java. The comments are part of the project source code. The first comment documents the method's purpose. The comment inside the method reminds future programmers why the scheduler call belongs here. Neither comment runs as code. WPILib calls robotPeriodic() automatically while the robot program is running. It calls this method in disabled, autonomous, teleoperated, and test modes. A normal call happens about every 20 milliseconds. CommandScheduler.getInstance().run() tells the command scheduler to perform one pass through its work. During that pass, the scheduler checks button bindings, runs active commands, stops commands that have ended, and starts default commands when their subsystems are available. The next slide breaks that pass into steps. The scheduler does not need Robot.java to name BeltInCommand directly. RobotContainer created the button binding earlier, so the scheduler already knows what to start when Button A is pressed. Connect this to the earlier TimedRobot demonstrations. Those examples placed hardware-control code directly in teleopPeriodic(). In the finished command-based robot, robotPeriodic() calls the scheduler, and the scheduler calls the correct command methods. Ask the class: What would happen if we removed CommandScheduler.getInstance().run()? The program would stop processing button bindings, active commands, and default commands. Transition: Now that we know where the scheduler is called, the next slide shows what it does during each pass.

## Slide 23
COMMAND-BASED ROBOT CODE
The scheduler checks the robot every 20 ms
During each pass, the scheduler: 1. Calls each subsystem's periodic() method. 2. Checks buttons and other triggers. 3. Calls execute() on the active commands. 4. Ends commands that finish or are interrupted. 5. Starts default commands for available subsystems. The callbacks run one after another on the robot's main thread. Do not use Thread.sleep() inside a command. It delays the rest of the robot program.
Notes: Robot.java calls the scheduler repeatedly. A normal pass occurs about every 20 milliseconds, or 50 times per second. During a pass, the scheduler gives subsystems a chance to update, checks the controller bindings, runs the active commands, ends commands that are done, and starts default commands for unused subsystems. These callbacks run one after another on the main robot thread. Thread.sleep inside a command pauses that thread. While it sleeps, the scheduler cannot run the other commands or complete the rest of its work. Use command timing tools instead of blocking the thread. Students do not need to memorize the exact order today. They should remember that the scheduler repeatedly checks inputs and gives each active command a small amount of time to run.

## Slide 24
COMMAND-BASED ROBOT CODE
What if two commands attempt to control the belt?
Two buttons request opposite action: • Button A starts BeltInCommand. • BeltInCommand tells the belt to run inward. • Button B starts BeltOutCommand. • BeltOutCommand tells the same belt to run outward.
Both commands send instructions to the same motor Without conflict handling, the last instruction sent controls the motor. What should happen if the operator presses both buttons?
Notes: Ask: What should happen if the operator presses A for belt in and B for belt out at the same time? Give students time to answer. They may say that the motor stops, one button wins, or the robot breaks. Java does not automatically know that these two actions control the same motor. Without subsystem requirements, both commands could run during the same scheduler cycle.
BeltInCommand could request a positive belt speed, and
BeltOutCommand could request a negative belt speed. The motor controller keeps the last value written during that cycle. The result depends on which command writes last. The robot may appear to work, but changing the code order can change the result. End with: Command-based programming gives us a way to declare this conflict before the commands run.

## Slide 25
COMMAND-BASED ROBOT CODE
Only one command controls the belt at a time
// Declaring Requirements
public class BeltInCommand extends Command {
private final BeltSubsystem beltSubsystem;
public BeltInCommand(BeltSubsystem beltSubsystem) {
this.beltSubsystem = beltSubsystem;
// Tells the scheduler this command uses the belt
addRequirements(beltSubsystem);
}
}
What the scheduler does 1. Both commands say they need BeltSubsystem. 2. The scheduler stops BeltInCommand. 3. end(true) stops the belt motor. 4. The scheduler starts BeltOutCommand.
Notes: Point to addRequirements(beltSubsystem) in both command constructors. Explain it in plain language: This command tells the scheduler that it needs control of the belt subsystem while it runs. Walk through the project behavior. The operator presses A, and the whileTrue binding schedules BeltInCommand. The scheduler starts that command and records that it is using BeltSubsystem. If the operator then presses B, the B binding asks the scheduler to start BeltOutCommand. The scheduler sees that both commands require BeltSubsystem. These commands use WPILib's default interruption behavior, so the scheduler interrupts BeltInCommand. It calls BeltInCommand.end(true), and this project's end method calls beltSubsystem.stop(). After the first command ends, the scheduler starts BeltOutCommand and the belt runs in the opposite direction. The scheduler does not decide which direction is correct. The command code defines the action. The scheduler enforces the rule that only one command can control the belt subsystem at a time. Ask: Could a belt command and the roller command run at the same time? Yes. They require different subsystems. Instructor note: if you demonstrate the conflict by holding A and then pressing B, release both buttons before repeating it. A whileTrue binding does not restart an interrupted command while its button remains held.

## Slide 26
COMMAND-BASED ROBOT CODE
Releasing Button A stops the belt
1. Button A released
2. Binding becomes false
3. Scheduler cancels command
4. end(true) calls stop()
5. Belt motor receives 0.0
What happens when A is released 1. The whileTrue condition becomes false. 2. The scheduler cancels BeltInCommand. 3. The scheduler calls end(true). 4. end() calls beltSubsystem.stop(). 5. BeltSubsystem writes 0.0 to the motor controller. The belt stops even though execute() no longer runs.
Notes: This is the cleanup half of the Button A story. While A is held, the whileTrue binding keeps BeltInCommand active. When the operator releases A, the binding cancels the command. The scheduler then calls end(true). In this project, the end method calls beltSubsystem.stop(), and the subsystem writes 0.0 to the motor controller. The motor does not stop because execute stopped running. It stops because end explicitly sends the stop request. This is why an empty end method is dangerous for a command that runs a motor.

## Slide 27
PROJECT SOURCE CODE
Project Directory Tree & Repository Structure
// Repository Package Layout
src/main/java/frc/robot/
├── Main.java <- Entry point
├── Robot.java <- 20ms scheduler loop
├── RobotContainer.java <- Wiring hub & button bindings
├── Constants.java <- Hardware channels & tuning
├── DriveSpeedMode.java <- Shared drive state
├── subsystems/
│ ├── DriveSubsystem.java <- 4-motor tank drive
│ ├── BeltSubsystem.java <- Transport belt motor
│ ├── RollerSubsystem.java <- Ejection roller motor
│ └── ClimberSubsystem.java <- Pneumatic climber valve
└── commands/
├── DriveTeleopCommand.java
├── BeltInCommand.java
├── BeltOutCommand.java
├── RollerCommand.java
├── SlowDriveCommand.java
└── ToggleClimberArmsCommand.java
Repository Class Roles
• package frc.robot:
Root package housing all robot source code.
• Constants.java:
Central read-only configuration hub for ports, IDs, and speeds.
• RobotContainer.java:
Master wiring hub; instantiates hardware and binds triggers.
• subsystems/:
Contains SubsystemBase classes encapsulating raw hardware.
• commands/:
Contains Command classes that describe robot actions.
Notes: Here is our actual repository directory tree. Notice how code is organized into root package, subsystems, and commands folders.

## Slide 28
PROJECT SOURCE CODE
Constants.java keeps settings in one place
// Selected Constants.java fields // Hardware public static final int PWM_FRONT_LEFT_DRIVE = 0; public static final int PWM_BACK_LEFT_DRIVE = 1; public static final int PWM_BACK_RIGHT_DRIVE = 2; public static final int PWM_FRONT_RIGHT_DRIVE = 3; public static final int PWM_ROLLER = 4; public static final int PWM_BELT = 5; public static final int PCM = 0; public static final int CLIMBER_SOLENOID_FORWARD = 0; public static final int CLIMBER_SOLENOID_REVERSE = 1; public static final Value CLIMBER_ARMS_OUT = Value.kForward; public static final Value CLIMBER_ARMS_IN = Value.kReverse; // Operator public static final int DRIVER_CONTROLLER = 0; public static final int OPERATOR_CONTROLLER = 1; // Tuning public static final double ROLLER_SPEED = 1.0; public static final double BELT_SPEED = 1.0; public static final double NORMAL_DRIVE_SCALE = 0.40; public static final double SLOW_DRIVE_SCALE = 0.20; public static final double DRIVE_DEADBAND = 0.08; public static final double DRIVE_SLEW_RATE_LIMIT = 0.8;
Notes: This focused excerpt shows the constants used by the hardware, controller, and tuning examples. Open the complete Constants.java file in VS Code to show its documentation and private constructors.

## Slide 29
PROJECT SOURCE CODE
RobotContainer connects controls to commands
// RobotContainer.java (focused excerpt) public RobotContainer() { driverController = new CommandXboxController(Constants.Operator.DRIVER_CONTROLLER); operatorController = new CommandXboxController(Constants.Operator.OPERATOR_CONTROLLER); driveSubsystem = new DriveSubsystem(); climberSubsystem = new ClimberSubsystem(); beltSubsystem = new BeltSubsystem(); rollerSubsystem = new RollerSubsystem(); driveSpeedMode = new DriveSpeedMode(); configureDefaultCommands(); configureBindings(); } private void configureBindings() { operatorController.y().onTrue(new ToggleClimberArmsCommand(climberSubsystem)); operatorController.a().whileTrue(new BeltInCommand(beltSubsystem)); operatorController.b().whileTrue(new BeltOutCommand(beltSubsystem)); operatorController.x().whileTrue(new RollerCommand(rollerSubsystem)); driverController.rightBumper().whileTrue(new SlowDriveCommand(driveSpeedMode)); }
Notes: This focused excerpt matches the repository constructor and configureBindings() method. RobotContainer creates the controllers, subsystems, and drive-speed state before installing defaults and button bindings. Show the complete file in VS Code.

## Slide 30
PROJECT SOURCE CODE
Button A across the Java files
1. Controller (Button A)
2. Driver Station (USB Packet)
3. RobotContainer (Event Binding)
4. BeltInCommand (Command methods)
5. BeltSubsystem (PWM 5 Output)
Java Execution Path — Pass 3 Checkpoint
1. RobotContainer.java: operatorController.a().whileTrue(new BeltInCommand(beltSubsystem));
2. WPILib CommandScheduler: Evaluates the Button A trigger during the 20ms scheduler pass.
3. BeltInCommand.java: Constructor executes addRequirements(beltSubsystem); execute() runs every 20ms.
4. BeltSubsystem.java: run(Constants.Tuning.BELT_SPEED) executes beltMotor.set(1.0);
5. Constants.java: Hardware.PWM_BELT = 5 and Tuning.BELT_SPEED = 1.0 supply static channel & speed parameters.
Notes: This is Checkpoint 3. The path begins in the repository binding, passes through WPILib CommandScheduler, and returns to BeltInCommand, BeltSubsystem, and Constants. CommandScheduler belongs to WPILib, not this repository.

## Slide 31
PRACTICE AND REFERENCE
Spot the Bug: Classroom Debugging Challenges
BUG 1: Missing addRequirements
Code Snippet:
public BeltInCommand(BeltSubsystem belt) {
this.belt = belt;
// addRequirements(belt); OMITTED!
}
Question:
What happens when the operator presses Button A and Button B simultaneously?
BUG 2: Empty end() Method
Code Snippet:
public void end(boolean interrupted) {
// Left empty!
}
Question:
When the operator releases Button A, what happens to the physical belt motor?
BUG 3: Duplicate USB Slots
Code Snippet:
public static final class Operator {
public static final int DRIVER_CONTROLLER = 0;
public static final int OPERATOR_CONTROLLER = 0;
}
Question:
What happens when the robot is enabled on the field?
Notes: Present these three bugs to the class. Have students analyze what goes wrong in each case before advancing to the fix slide!

## Slide 32
PRACTICE AND REFERENCE
Spot the Bug: Solutions & Exact Code Fixes
FIX 1: Add addRequirements
Symptom: Last write wins, causing unsafe motor fighting.
Exact Fix:
public BeltInCommand(BeltSubsystem belt) {
this.belt = belt;
addRequirements(belt); // Solved!
}
FIX 2: Call stop() in end()
Symptom: Motor keeps its last output after release until code writes a new value or the robot is disabled.
Exact Fix:
public void end(boolean interrupted) {
beltSubsystem.stop(); // Solved!
}
FIX 3: Assign Unique USB Ports
Symptom: Driver & Operator controls clash on USB Slot 0.
Exact Fix:
public static final class Operator {
public static final int DRIVER_CONTROLLER = 0;
public static final int OPERATOR_CONTROLLER = 1; // Solved!
}
Notes: Fix 1 gives the scheduler exclusive ownership information. Fix 2 writes zero when the command ends. Fix 3 assigns distinct USB slots to the driver and operator controllers.