## Slide 1
2020 FRC Robot Code Architecture & Implementation Guide
A Technical Guide to Robot Hardware, WPILib Command-Based Architecture, and Java Code Case Study: 4-Talon Drivetrain, Belt/Roller Transport, CTRE PCM Climber, and Dual CommandXboxControllers

## Slide 2
SECTION 1
Robot hardware
Exploring physical mechanisms, PWM motor channels, pneumatics, and direct hardware control.

## Slide 3
ROBOT HARDWARE
Physical Hardware Inventory & Actuator Channel Map
Mechanism | Hardware Device | Bus / Channel | Configuration Notes
Drivetrain (4 Motors) | 4x Talon SRX | PWM 0, 1 (Left) PWM 2, 3 (Right) | Tank Drive. Left-side motors inverted due to mechanical mounting.
Ball Transport Belt | 1x Talon SRX | PWM Port 5 | Feeds balls inward/outward through indexer.
Outtake Roller | 1x Talon SRX | PWM Port 4 | High-speed ball ejection roller.
Climber Arms | 1x Double Solenoid Valve | CTRE PCM ID 0 Channels 0/1 | One valve feeds both cylinders through split air lines.
Hardware Inversion Note:
Because the left and right drive gearboxes are mounted symmetrically facing opposite directions, positive voltage on both sides drives left forward and right backward. The left-side motors must be inverted in software (leftDriveMotors.setInverted(true)) so positive speed drives both sides forward.

## Slide 4
ROBOT HARDWARE
Running the belt motor
Bare-Minimum Belt Control Program:
• Direct Hardware Actuation: Uses WPILib's Talon class on PWM Port 5 directly inside a TimedRobot program.
• Continuous Teleop Execution: teleopPeriodic() runs continuously every 20ms while teleop is enabled.
• Constant Power Output: Calls beltMotor.set(0.25) to run the belt at 25% power.
• Automatic Safety Shutdown: Disabling the robot instantly cuts the roboRIO PWM signal to 0V, stopping the motor.
package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; public class Robot extends TimedRobot { // Talon motor controller on PWM Port 5 private final Talon beltMotor = new Talon(5); @Override public void teleopPeriodic() { // Runs belt at 25% output continuously beltMotor.set(0.25); } }

## Slide 5
ROBOT HARDWARE
Roller Challenge: Running the Roller Motor
What Changes From the Belt Program?
• Identical Pattern, Different Channel: Operating the roller requires only changing the PWM channel and instance name.
• PWM Port 4: The outtake roller is wired to PWM Port 4 (Talon rollerMotor = new Talon(4)).
• Direct Actuation: rollerMotor.set(0.25) runs the outtake roller at 25% speed.
• Key Observation: Every motor controller in WPILib uses the exact same set(double speed) API call.
package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; public class Robot extends TimedRobot { // Roller motor controller on PWM Port 4 private final Talon rollerMotor = new Talon(4); @Override public void teleopPeriodic() { // Runs roller at 25% output continuously rollerMotor.set(0.25); } }

## Slide 6
ROBOT HARDWARE
Pneumatic Climber Arms
One Valve Controls Both Arms • One DoubleSolenoid: A single valve on CTRE PCM ID 0 controls the climber. • PCM Channels 0 and 1: The forward and reverse coils use one channel pair. • Split Air Lines: Each valve output splits to the matching port on both cylinders, so both pistons receive the same command. • Shared Motion: kForward extends both arms. kReverse retracts both arms.
package frc.robot; import edu.wpi.first.wpilibj.DoubleSolenoid; import edu.wpi.first.wpilibj.PneumaticsModuleType; import edu.wpi.first.wpilibj.TimedRobot; /** * NAME * Robot - extends both climber arms through one valve. * * DESCRIPTION * One double-solenoid valve feeds both cylinders. */ public class Robot extends TimedRobot { private final DoubleSolenoid climberSolenoid = new DoubleSolenoid( 0, PneumaticsModuleType.CTREPCM, 0, 1); @Override public void teleopPeriodic() { climberSolenoid.set( DoubleSolenoid.Value.kForward); } }

## Slide 7
ROBOT HARDWARE
4-Motor Drivetrain Control
SAFETY WARNING: Place the robot securely on blocks off the floor before enabling this test program.
• 4 Motors Across PWM 0..3: Front-left (PWM 0), Back-left (PWM 1), Back-right (PWM 2), Front-right (PWM 3).
• Sign Inversion (-0.15 vs +0.15): Drives left side at -0.15 and right side at +0.15 to account for left-side motor inversion.
package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; public class Robot extends TimedRobot { private final Talon frontLeft = new Talon(0); private final Talon backLeft = new Talon(1); private final Talon backRight = new Talon(2); private final Talon frontRight = new Talon(3); @Override public void teleopPeriodic() { // Left side inverted in software frontLeft.set(-0.15); backLeft.set(-0.15); frontRight.set(0.15); backRight.set(0.15); } }

## Slide 8
ROBOT HARDWARE
Controlling several mechanisms
Direct Control Strengths:
• 1-to-1 Hardware Verification: Simple TimedRobot code proves electrical wiring, PWM ports, and PCM channels function.
• Zero Framework Overhead: Directly invokes motor.set() without configuring commands or scheduling rules.
• Isolated Testing: Validates direction and motor response on blocks prior to driving.
System Coordination Bottlenecks:
• Monolithic teleopPeriodic(): Mixing joysticks, buttons, and 4 mechanisms into one huge loop leads to chaotic nested if-else logic.
• Hardware Conflicts: What happens if two buttons try to command the same belt motor at once?
• No Clean State Cleanup: Button releases, interruptions, and automated scoring sequences require complex state tracking flags.

## Slide 9
ROBOT HARDWARE
Human Controls & Dual CommandXboxController Mapping
DRIVER CONTROLLER (USB Port 0)
• Left Stick Y: Commands left-side drivetrain speed (-1.0 to +1.0).
• Right Stick Y: Commands right-side drivetrain speed (-1.0 to +1.0).
• Right Bumper (Held): Activates Precision Slow Drive Mode (scales speed from 40% down to 20%).
• Deadband: Applies 0.08 deadband to eliminate stick drift near center.
OPERATOR CONTROLLER (USB Port 1) • Button A (Held): Runs Ball Transport Belt Inward (+1.0 speed). • Button B (Held): Runs Ball Transport Belt Outward (-1.0 speed). • Button X (Held): Runs Outtake Roller (+1.0 speed). • Button Y (Pressed): Toggles the shared climber valve, extending or retracting both arms.

## Slide 10
ROBOT HARDWARE
Driver Station USB Setup & Live Telemetry Diagnostics
Driver Station USB Slot Rules:
• Index Matching: The Driver Station USB tab assigns numeric port slots (0, 1, 2...). Software constants DRIVER_CONTROLLER = 0 and OPERATOR_CONTROLLER = 1 must match physical USB slots.
• Port Swap Misconfigurations: If controllers are plugged in backwards (Operator in Slot 0, Driver in Slot 1), stick inputs drive the wrong mechanisms.
• Live Diagnostic Grid: Pressing physical buttons on the Xbox controller lights up indicators in the live Driver Station telemetry grid to confirm mapping before enabling.

## Slide 11
ROBOT HARDWARE
Button A reaches PWM port 5
1. Controller
Button A Press
2. Driver Station
USB HID Packet
3. RobotContainer
Trigger Binding
4. BeltInCommand
Lifecycle Hooks
5. BeltSubsystem
PWM 5 Motor Output
PHYSICAL SIGNAL ORIGIN
• 1. Human Press: Thumb depresses Button A on Operator Xbox Controller (USB Port 1).
• 2. USB HID Packet: Controller micro-ASIC encodes button state and sends USB packet to Driver Station laptop.
• 3. UDP Network Packet: Driver Station software packages HID state into a 20ms UDP packet sent over Ethernet/Wi-Fi to roboRIO.
ACTUATOR OUTPUT DESTINATION
• 4. roboRIO HAL/FPGA: DriverStation HAL updates internal button array during 20ms periodic pass.
• 5. PWM 5 Signal: Software commands beltMotor.set(1.0). roboRIO FPGA generates 1.0ms to 2.0ms pulse-width signal on PWM Port 5.
• 6. Motor Motion: Talon SRX reads PWM signal and meters +12V from Power Distribution Panel to drive belt motor inward.

## Slide 12
SECTION 2
Command-based robot code
Managing hardware exclusivity, trigger bindings, lifecycle hooks, and the 20ms execution loop.

## Slide 13
COMMAND-BASED ROBOT CODE
Two commands request the belt
A Concrete Engineering Conflict:
1. Button A Request: Operator holds Button A -> Triggers BeltInCommand -> Commands belt motor +1.0 (Inward).
2. Button B Request: Simultaneously, Operator holds Button B -> Triggers BeltOutCommand -> Commands belt motor -1.0 (Outward).
3. The Conflict: Both commands target the exact same physical hardware (Talon SRX on PWM Port 5).
4. The Core Question: Which command owns the motor? What prevents the code from sending contradictory signals to the motor controller in the same 20ms loop pass?
The Architectural Solution: Subsystem Requirements (addRequirements)
WPILib solves this through subsystem requirements. Commands must declare which hardware resources they require. The CommandScheduler enforces hardware exclusivity, cancelling the older command before starting the new one.

## Slide 14
COMMAND-BASED ROBOT CODE
Subsystem Requirements & Hardware Exclusivity
How addRequirements(subsystem) Works:
• Resource Registration: Inside a Command's constructor, calling addRequirements(beltSubsystem) registers the subsystem as a required resource.
• Scheduler Exclusivity Referee: The CommandScheduler tracks which command currently owns each subsystem.
• Automatic Interrupt & Cleanup: When Button B schedules BeltOutCommand, the scheduler sees that beltSubsystem is currently owned by BeltInCommand. It interrupts BeltInCommand, calls its end(true) method to safely stop the motor, and grants ownership to BeltOutCommand.
• Scheduler Ownership Scope: Enforces ownership within the CommandScheduler list—it is a logical referee, not an OS thread mutex.
public class BeltInCommand extends Command { private final BeltSubsystem beltSubsystem; public BeltInCommand(BeltSubsystem beltSubsystem) { this.beltSubsystem = beltSubsystem; // Declares exclusive hardware ownership addRequirements(beltSubsystem); } @Override public void execute() { beltSubsystem.run(Constants.Tuning.BELT_SPEED); } @Override public void end(boolean interrupted) { // Invoked automatically when cancelled beltSubsystem.stop(); } }

## Slide 15
COMMAND-BASED ROBOT CODE
Architectural Separation: Subsystems (HOW) vs. Commands (WHEN)
SUBSYSTEMS (SubsystemBase)
• Hardware Ownership: Owns raw motor controllers (Talon), sensors, and solenoids in private fields.
• Encapsulation (HOW): Defines public API methods for mechanism actions (run(speed), stop(), extendArms()).
• Passive Capability: Knows HOW to move the hardware, but never decides WHEN to move.
• Examples: DriveSubsystem, BeltSubsystem, RollerSubsystem, ClimberSubsystem.
COMMANDS (Command)
• Execution Logic: Contains state machine rules and lifecycle methods (initialize, execute, end).
• Action Sequencing (WHEN): Dictates WHEN hardware actions occur in response to triggers or autonomous schedules.
• Resource Locks: Declares required subsystems via addRequirements().
• Examples: BeltInCommand, BeltOutCommand, ToggleClimberArmsCommand, DriveTeleopCommand.

## Slide 16
COMMAND-BASED ROBOT CODE
Trigger Bindings: whileTrue, onTrue, and setDefaultCommand
whileTrue(command)
• Momentary Active Control: Schedules command when button is pressed; keeps running while held.
• Release Cancellation: Button release cancels command and invokes end(true) cleanup.
• Used for: BeltInCommand, BeltOutCommand, RollerCommand, SlowDriveCommand.
onTrue(command)
• One-Shot State Trigger: Schedules command once on initial press event.
• Instant Execution: Command runs initialize() once and returns isFinished() = true immediately.
• Used for: ToggleClimberArmsCommand.
setDefaultCommand(...)
• Fallback Subsystem Command: Runs automatically whenever no other command is requiring the subsystem.
• Continuous Active Control: Re-schedules every pass unreserved.
• Used for: DriveTeleopCommand on DriveSubsystem.

## Slide 17
COMMAND-BASED ROBOT CODE
Polymorphic Command Lifecycle Method Hooks
Lifecycle Method | When Invoked by CommandScheduler | Implementation Responsibility
initialize() | Runs ONCE when the command is scheduled. | Set up initial state, reset timers, toggle solenoids.
execute() | Runs REPEATEDLY every 20ms while command is active. | Pass motor speed setpoints to subsystem API methods.
isFinished() | Evaluated REPEATEDLY every 20ms after execute(). | Return true when complete (instant) or false to keep running.
end(boolean interrupted) | Runs ONCE when command finishes or is cancelled. | Safely shut off outputs (beltSubsystem.stop()).

## Slide 18
COMMAND-BASED ROBOT CODE
The Fixed 20ms Single-Threaded CommandScheduler Loop
5-Step Execution Sequence (runs synchronously inside Robot.robotPeriodic()):
Step 1: Poll Triggers — Scans registered CommandXboxController button state arrays for press/release events.
Step 2: Check isFinished() — Evaluates active commands; invokes end(false) for completed commands.
Step 3: Resolve & Schedule — Schedules new commands; cancels conflicting commands claiming required subsystems.
Step 4: Execute Active Commands — Calls execute() sequentially on all active commands on the single main thread.
Step 5: Subsystem Periodic — Invokes periodic() on all registered SubsystemBase objects to update hardware telemetry.
Single-Threaded Execution Rule:
The entire loop runs synchronously on the main thread. Never call Thread.sleep() inside a command's execute()—doing so freezes the entire robot loop, stalling communications, safety watchdogs, and all other mechanisms.

## Slide 19
COMMAND-BASED ROBOT CODE
Releasing Button A stops the belt
1. Controller
Button A Press
2. Driver Station
USB HID Packet
3. RobotContainer
Trigger Binding
4. BeltInCommand
Lifecycle Hooks
5. BeltSubsystem
PWM 5 Motor Output
STATE MACHINE CLEANUP TRACE ON BUTTON RELEASE:
1. Trigger State Transition: Operator releases Button A -> CommandXboxController detects state change from TRUE to FALSE.
2. Command Cancellation: whileTrue() trigger condition becomes false -> CommandScheduler cancels BeltInCommand.
3. end(true) Lifecycle Hook: CommandScheduler invokes BeltInCommand.end(true) with interrupted = true.
4. Subsystem Shutdown Method: BeltInCommand.end() calls beltSubsystem.stop().
5. Motor Voltage Cutoff: BeltSubsystem.stop() executes run(0.0) -> beltMotor.set(0.0), bringing PWM Port 5 output voltage back to zero.

## Slide 20
SECTION 3
Project source code
Examining exact Java repository files: Constants.java, Subsystems, Commands, and RobotContainer.java.

## Slide 21
PROJECT SOURCE CODE
Project Directory Tree & Repository Structure
src/main/java/frc/robot/ ├── Main.java <- Entry point (starts Robot) ├── Robot.java <- 20ms CommandScheduler loop ├── RobotContainer.java <- Wiring hub & button bindings ├── Constants.java <- Hardware ports & tuning ├── subsystems/ │ ├── DriveSubsystem.java <- 4-motor tank drive │ ├── BeltSubsystem.java <- Ball transport belt │ ├── RollerSubsystem.java <- Outtake roller │ └── ClimberSubsystem.java <- One valve, two cylinders └── commands/ ├── DriveTeleopCommand.java ├── BeltInCommand.java ├── BeltOutCommand.java ├── RollerCommand.java ├── SlowDriveCommand.java └── ToggleClimberArmsCommand.java
Repository Class Roles:
• package frc.robot: Root package housing all robot Java source files.
• Constants.java: Central configuration hub containing static inner classes for hardware ports and tuning values.
• RobotContainer.java: Master wiring hub; instantiates hardware subsystems and connects controller triggers to commands.
• subsystems/: Folder containing SubsystemBase classes that encapsulate motor controllers and solenoids.
• commands/: Folder containing Command classes implementing action logic and lifecycle hooks.

## Slide 22
PROJECT SOURCE CODE
Centralized Configuration: Constants.java
Constants.java Structure • Hardware ports: Stores every PWM channel and the PCM module ID. • Climber valve: CLIMBER_SOLENOID_FORWARD and CLIMBER_SOLENOID_REVERSE identify PCM channels 0 and 1. • Climber commands: CLIMBER_ARMS_OUT and CLIMBER_ARMS_IN name the two valve states. • Operator and tuning groups: Store controller ports, motor speeds, drive scaling, and deadband values.
package frc.robot; import edu.wpi.first.wpilibj.DoubleSolenoid.Value; public final class Constants { private Constants() { } public static final class Hardware { public static final int PWM_FRONT_LEFT_DRIVE = 0; public static final int PWM_BACK_LEFT_DRIVE = 1; public static final int PWM_BACK_RIGHT_DRIVE = 2; public static final int PWM_FRONT_RIGHT_DRIVE = 3; public static final int PWM_ROLLER = 4; public static final int PWM_BELT = 5; public static final int PCM = 0; public static final int CLIMBER_SOLENOID_FORWARD = 0; public static final int CLIMBER_SOLENOID_REVERSE = 1; public static final Value CLIMBER_ARMS_OUT = Value.kForward; public static final Value CLIMBER_ARMS_IN = Value.kReverse; } }

## Slide 23
PROJECT SOURCE CODE
Hardware Encapsulation: BeltSubsystem.java
BeltSubsystem Class Anatomy:
• Extends SubsystemBase: Inherits subsystem capabilities and automatic periodic() registration with the scheduler.
• Private Hardware Object: Private final Talon beltMotor hides raw PWM handle from external classes.
• run(double speed) API: Public method allowing commands to set motor output speed.
• stop() Method: Convenience API executing run(0.0) to command zero output.
package frc.robot.subsystems; import edu.wpi.first.wpilibj.motorcontrol.Talon; import edu.wpi.first.wpilibj2.command.SubsystemBase; import frc.robot.Constants; public class BeltSubsystem extends SubsystemBase { private final Talon beltMotor; public BeltSubsystem() { beltMotor = new Talon(Constants.Hardware.PWM_BELT); } public void run(double speed) { beltMotor.set(speed); } public void stop() { run(0.0); } }

## Slide 24
PROJECT SOURCE CODE
Action Execution Logic: BeltInCommand.java
BeltInCommand Class Anatomy:
• Constructor Requirement: Calls addRequirements(beltSubsystem) to declare exclusive hardware ownership.
• execute() Pass: Calls beltSubsystem.run(Constants.Tuning.BELT_SPEED) every 20ms.
• isFinished() = false: Returns false so the command continues running while Button A is held.
• end(boolean interrupted): Calls beltSubsystem.stop() when button is released or command is cancelled.
package frc.robot.commands; import edu.wpi.first.wpilibj2.command.Command; import frc.robot.Constants; import frc.robot.subsystems.BeltSubsystem; public class BeltInCommand extends Command { private final BeltSubsystem beltSubsystem; public BeltInCommand(BeltSubsystem beltSubsystem) { this.beltSubsystem = beltSubsystem; addRequirements(beltSubsystem); } @Override public void execute() { beltSubsystem.run(Constants.Tuning.BELT_SPEED); } @Override public void end(boolean interrupted) { beltSubsystem.stop(); } @Override public boolean isFinished() { return false; } }

## Slide 25
PROJECT SOURCE CODE
Robot Wiring & Event Bindings: RobotContainer.java
Central Event Wiring Hub:
• Instantiates Controllers & Subsystems: Instantiates driverController (Port 0), operatorController (Port 1), and all 4 hardware subsystems.
• configureBindings(): Connects Xbox triggers to commands (a().whileTrue(BeltIn), b().whileTrue(BeltOut), x().whileTrue(Roller), y().onTrue(ToggleClimber)).
• configureDefaultCommands(): Binds DriveTeleopCommand as default command on DriveSubsystem.
• Note: Code simplified for slide display.
// Note: Simplified code example for slide presentation public class RobotContainer { private final CommandXboxController driverController = new CommandXboxController(Constants.Operator.DRIVER_CONTROLLER); private final CommandXboxController operatorController = new CommandXboxController(Constants.Operator.OPERATOR_CONTROLLER); private final DriveSubsystem driveSubsystem = new DriveSubsystem(); private final BeltSubsystem beltSubsystem = new BeltSubsystem(); private void configureBindings() { // Operator Xbox Bindings operatorController.a().whileTrue(new BeltInCommand(beltSubsystem)); operatorController.b().whileTrue(new BeltOutCommand(beltSubsystem)); operatorController.x().whileTrue(new RollerCommand(rollerSubsystem)); operatorController.y().onTrue(new ToggleClimberArmsCommand(climberSubsystem)); // Driver Xbox Binding driverController.rightBumper().whileTrue(new SlowDriveCommand(driveSpeedMode)); } }

## Slide 26
PROJECT SOURCE CODE
Button A across the Java files
1. Controller
Button A Press
2. Driver Station
USB HID Packet
3. RobotContainer
Trigger Binding
4. BeltInCommand
Lifecycle Hooks
5. BeltSubsystem
PWM 5 Motor Output
Repository File | Code Line / Method | Action Execution Responsibility
RobotContainer.java | operatorController.a().whileTrue(...) | Registers whileTrue trigger condition for Operator Button A.
BeltInCommand.java | public BeltInCommand(BeltSubsystem...) addRequirements(beltSubsystem); | Declares exclusive hardware requirement on BeltSubsystem.
BeltInCommand.java | execute() -> beltSubsystem.run(...) end() -> beltSubsystem.stop() | Commands belt speed in execute(); stops belt in end() on button release.
BeltSubsystem.java | run(double speed) -> beltMotor.set(speed) stop() -> run(0.0) | Sends speed setpoint directly to Talon motor controller on PWM Port 5.

## Slide 27
SECTION 4
Practice and reference
Student code-tracing exercises, technical investigation questions, and hardware protocols.

## Slide 28
PRACTICE AND REFERENCE
Trace another control
Student Code-Tracing Exercises EX-01: Signal Path Tracing. Trace Operator Button X (Scoring Roller) from the physical press through RobotContainer.java, RollerCommand.java, and RollerSubsystem.java to PWM Port 4. EX-02: Conflict Protection Analysis. Trace what happens when Button A (Belt In) and Button B (Belt Out) are pressed simultaneously. Identify the addRequirements() call that lets the scheduler enforce belt ownership. EX-03: One-Shot vs. Held Lifecycle Comparison. Compare Button Y (ToggleClimberArmsCommand) with Button A (BeltInCommand). Why does isFinished() return true after initialize() toggles the shared climber valve? EX-04: Driver Slow Drive Mode. Trace the Driver Right Bumper through SlowDriveCommand.java and DriveSpeedMode. Explain how the drive scale changes from 0.40 to 0.20.

## Slide 29
PRACTICE AND REFERENCE
Questions to investigate
Technical Investigation Prompts:
Question 1: Why is thinking of WPILib Command-Based as a 'multithreaded' application a serious mistake, and what happens if you call Thread.sleep() inside execute()?
Question 2: If a programmer forgets to call addRequirements(subsystem) in a command's constructor, what bug occurs when two buttons commanding that subsystem are pressed at the same time?
Question 3: How does the single-threaded 20ms CommandScheduler loop prevent race conditions when reading controller triggers and updating motor setpoints?
Question 4: What is the mechanical and software difference between a momentary command (whileTrue) and a one-shot state toggle (onTrue)?

## Slide 30
PRACTICE AND REFERENCE
Hardware Protocol Appendix: PWM vs. CAN Bus
Feature | PWM Protocol (Current Robot Setup) | CAN Bus Protocol (Advanced Hardware)
Wiring Topology | Point-to-point 3-wire cable from roboRIO PWM port to each Talon SRX. | Daisy-chained 2-wire differential bus (CAN High / CAN Low) linking all motor controllers.
Signal Direction | One-way control signal (roboRIO -> Talon). No telemetry feedback. | Bi-directional data bus allowing real-time motor telemetry.
Telemetry Capabilities | Open-loop voltage control only. Cannot read motor temperature, current draw, or encoder position. | Full closed-loop telemetry (current, voltage, temperature, position, velocity).