## Slide 1
2020 FRC Robot Code Architecture & Implementation Guide From Direct Hardware Control to Command-Based Java

## Slide 2
Robot Mechanisms and Hardware Channels
4-Motor Drivetrain Differential Tank Drive 4x PWM Talon SRX Motor Controllers PWM Ports 0, 1 (Left) & 2, 3 (Right) Left side motors inverted in code
Ball Transport Belt
Internal Indexing Mechanism
1x PWM Talon SRX Motor Controller PWM Port 5 Transports power cells upward to outtake
Scoring Roller
High-Speed Outtake Mechanism
1x PWM Talon SRX Motor Controller PWM Port 4 Ejects power cells into high/low goal
Pneumatic Climber
Dual-Cylinder Endgame Lift
CTRE Pneumatics Control Module (PCM ID 0) Double Solenoids 0/1 (Left) & 2/3 (Right) Pneumatic pressure extends/retracts arms

## Slide 3
Running the Belt Motor
package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; /** * NAME: Robot - runs the belt motor directly. * DESCRIPTION: Enabling teleop runs the belt at 25% output. * Disabling the robot stops the PWM output. */ public class Robot extends TimedRobot { private final Talon beltMotor = new Talon(5); @Override public void teleopPeriodic() { beltMotor.set(0.25); // Runs belt continuously while teleop is enabled } }

## Slide 4
Running the Scoring Roller
package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; /** * NAME: Robot - runs the roller motor directly. * DESCRIPTION: Enabling teleop runs the roller at 25% output. * Disabling the robot stops the PWM output. */ public class Robot extends TimedRobot { private final Talon rollerMotor = new Talon(4); @Override public void teleopPeriodic() { rollerMotor.set(0.25); // Runs outtake roller continuously while teleop is enabled } }

## Slide 5
Extending the Climber Arms
package frc.robot; import edu.wpi.first.wpilibj.DoubleSolenoid; import edu.wpi.first.wpilibj.PneumaticsModuleType; import edu.wpi.first.wpilibj.TimedRobot; /** * NAME: Robot - extends both climber arms directly. * DESCRIPTION: Enabling teleop commands both climber solenoids forward. * Disabling removes electrical command (does not guarantee physical retraction). * To make climber retract, change kForward to kReverse. */ public class Robot extends TimedRobot { private final DoubleSolenoid leftClimber = new DoubleSolenoid(0, PneumaticsModuleType.CTREPCM, 0, 1); private final DoubleSolenoid rightClimber = new DoubleSolenoid(0, PneumaticsModuleType.CTREPCM, 2, 3); @Override public void teleopPeriodic() { leftClimber.set(DoubleSolenoid.Value.kForward); rightClimber.set(DoubleSolenoid.Value.kForward); } }

## Slide 6
Running the Drivetrain
⚠️ SAFETY WARNING: Place the robot securely on blocks off the floor before enabling this demo!
package frc.robot; import edu.wpi.first.wpilibj.TimedRobot; import edu.wpi.first.wpilibj.motorcontrol.Talon; public class Robot extends TimedRobot { private final Talon frontLeftMotor = new Talon(0); private final Talon backLeftMotor = new Talon(1); private final Talon backRightMotor = new Talon(2); private final Talon frontRightMotor = new Talon(3); @Override public void teleopPeriodic() { frontLeftMotor.set(-0.15); // Left side inverted for forward motion backLeftMotor.set(-0.15); frontRightMotor.set(0.15); // Right side forward backRightMotor.set(0.15); } }

## Slide 7
Driver and Operator Controls
DRIVER CONTROLLER (USB PORT 0)
• Primary Focus: Driving
• Left Stick Y: Tank Drive Left Side Output
• Right Stick Y: Tank Drive Right Side Output
• Right Bumper (Held): Slow Drive Mode (20% Speed Scale)
• Code Reference: driverController = new CommandXboxController(0)
OPERATOR CONTROLLER (USB PORT 1)
• Primary Focus: Ball Transport, Scoring & Endgame Lift
• Button A (Held): Belt In Command (Intake Power Cells)
• Button B (Held): Belt Out Command (Eject / Clear Jam)
• Button X (Held): Scoring Roller Command (Power Cell Eject)
• Button Y (Pressed): Toggle Climber Arms (Extend / Retract)
• Code Reference: operatorController = new CommandXboxController(1)

## Slide 8
Driver Station Controller Diagnostics
DRIVER STATION USB VERIFICATION
1. Port Slot Verification: Verify USB Port 0 is Driver Xbox Controller and USB Port 1 is Operator Xbox Controller.
2. Live Indicator Grid: Pressing Button X lights up Button 3 bright green in the USB Setup tab telemetry grid.
3. Port Conflict Diagnosis: If Button X is pressed on Slot 0 instead of Slot 1, Java routes the input to DriverController (which has no Button X binding) -> Motor stays off!
4. Pre-Match Check: Always verify USB port order before loading code to prevent control swaps on the field.

## Slide 9
Button A Reaches PWM Port 5
1. Human Action
Operator presses Button A on Xbox Controller Port 1
2. USB HID Packet
Windows Driver Station encodes button press into 20ms UDP packet
3. roboRIO Ingestion
robot receives network packet & passes to WPILib DriverStation API
4. Java Routing
CommandScheduler evaluates trigger & runs BeltInCommand
5. Hardware Output
roboRIO sends PWM pulse to Port 5 (Talon SRX) -> +12V to Belt Motor

## Slide 10
Two Commands Request the Belt
BUTTON A: BELT IN Holding Button A schedules BeltInCommand. The command requests positive motor output through BeltSubsystem. The belt moves power cells toward the scoring mechanism.
BUTTON B: BELT OUT Holding Button B schedules BeltOutCommand. The command requests negative motor output through the same BeltSubsystem. If both buttons are held, which command owns the belt motor?

## Slide 11
Subsystems and Commands
SUBSYSTEMS (SubsystemBase)
• Definition: Physical mechanisms on the robot.
• Core Role: Encapsulate hardware (motors, solenoids, sensors) in private fields.
• Responsibility: Define HOW actions occur via public API methods.
• Example Methods: run(speed), stop(), toggle()
• Rule: Subsystems NEVER decide when actions happen!
COMMANDS (Command)
• Definition: Action instructions and behavioral logic.
• Core Role: Manage execution state and timing hooks.
• Responsibility: Define WHEN actions occur and reserve hardware.
• Resource Guard: Calls addRequirements(subsystem) in constructor.
• Rule: Commands NEVER access motor controllers directly!

## Slide 12
One Subsystem, One Active Command
HOW addRequirements() CONTROLS OWNERSHIP 1. BeltInCommand and BeltOutCommand both call addRequirements(beltSubsystem). 2. CommandScheduler allows only one scheduled command to require BeltSubsystem at a time. 3. When a conflicting command is scheduled, the scheduler interrupts the current owner. 4. The interrupted command's end(true) method stops the belt before ownership changes. 5. The newly scheduled command then controls the subsystem.

## Slide 13
Controller Bindings
Momentary Commands
whileTrue(command)
Schedules command while button is held. When released, command is cancelled and end(true) stops motor. Example: BeltInCommand, RollerCommand
One-Shot Instant Commands
onTrue(command)
Schedules command once upon button press. Completes instantly (isFinished=true). Example: ToggleClimberArmsCommand
State Modifiers
whileTrue(slowDriveCommand)
Alters subsystem state parameters (e.g., speed scaling) while active. Reverts state on release. Example: SlowDriveCommand
Default Commands
setDefaultCommand(command)
Runs continuously whenever no other command claims the subsystem. Example: DriveTeleopCommand on DriveSubsystem

## Slide 14
Command Lifecycle Methods
initialize()
Run Once on Schedule
Called exactly once when command transitions from inactive to active. Use for setup, timer resets, or solenoid toggles.
execute()
Run Every 20ms
Called repeatedly every 20ms while command is active. Use for continuous motor speed commands or PID updates.
isFinished()
Evaluated Every 20ms
Returns boolean indicating if command has completed. Momentary commands return false; One-shot commands return true.
end(interrupted)
Run Once on Completion
Called once when command finishes or is cancelled. Use to safely stop motors (beltSubsystem.stop())!

## Slide 15
The CommandScheduler Loop
Step 1: Poll Buttons
Check physical status of all registered Xbox triggers & buttons.
Step 2: Check Finished
Call isFinished() on all active commands; schedule end() for completed ones.
Step 3: Resolve Conflicts
Check newly triggered commands, evaluate addRequirements(), interrupt conflicting commands.
Step 4: Execute Commands
Call execute() on all active scheduled commands single-threaded.
Step 5: Subsystem Periodic
Call periodic() on all registered Subsystems for telemetry & sensor updates.
CommandScheduler runs every 20ms (50 Hz)
Called from our code in robotPeriodic in Robot.java

## Slide 16
Releasing Button A Stops the Belt
BUTTON A RELEASE TRACE 1. CommandScheduler detects that operatorController.a() changed from pressed to released. 2. The whileTrue() binding cancels BeltInCommand. 3. CommandScheduler calls BeltInCommand.end(true). 4. end(true) calls beltSubsystem.stop(). 5. BeltSubsystem calls run(0), which commands zero output on PWM Port 5 and releases the subsystem for another command.

## Slide 17
Project Source Files
src/main/java/frc/robot/ ├── Main.java <- Entry point; launches Robot instance ├── Robot.java <- TimedRobot lifecycle; calls CommandScheduler.getInstance().run() ├── RobotContainer.java <- Central wiring hub; instantiates Subsystems & configures bindings ├── Constants.java <- Configuration constants (Hardware PWM/PCM ports, USB slots, Tuning) ├── subsystems/ │ ├── DriveSubsystem.java <- 4-motor differential drive encapsulation │ ├── BeltSubsystem.java <- PWM Port 5 ball transport belt encapsulation │ ├── RollerSubsystem.java <- PWM Port 4 outtake roller encapsulation │ └── ClimberSubsystem.java<- CTRE PCM double solenoid climber encapsulation └── commands/ ├── BeltInCommand.java <- Momentary command for intake ├── BeltOutCommand.java <- Momentary command for ejection ├── RollerCommand.java <- Momentary command for scoring roller ├── SlowDriveCommand.java<- Momentary speed scaler for driver ├── ToggleClimberArmsCommand.java <- One-shot instant command for climber └── DriveTeleopCommand.java <- Default command for tank drive

## Slide 18
Hardware and Tuning Constants
package frc.robot; // Presentation excerpt: open Constants.java in VS Code for the full required // class headers, comments, and hardware configuration. public final class Constants { public static final class Hardware { public static final int PWM_FRONT_LEFT_DRIVE = 0; public static final int PWM_BACK_LEFT_DRIVE = 1; public static final int PWM_BACK_RIGHT_DRIVE = 2; public static final int PWM_FRONT_RIGHT_DRIVE = 3; public static final int PWM_ROLLER = 4; public static final int PWM_BELT = 5; public static final int PCM = 0; } public static final class Operator { public static final int DRIVER_CONTROLLER = 0; public static final int OPERATOR_CONTROLLER = 1; } public static final class Tuning { public static final double BELT_SPEED = 1.0; public static final double DRIVE_DEADBAND = 0.08; public static final double NORMAL_DRIVE_SCALE = 0.40; public static final double SLOW_DRIVE_SCALE = 0.20; } }

## Slide 19
BeltSubsystem Owns the Belt Motor
package frc.robot.subsystems; import edu.wpi.first.wpilibj.motorcontrol.Talon; import edu.wpi.first.wpilibj2.command.SubsystemBase; import frc.robot.Constants; // Presentation excerpt: open BeltSubsystem.java in VS Code for the full // required NAME, DESCRIPTION, and method comments. public class BeltSubsystem extends SubsystemBase { private final Talon beltMotor; public BeltSubsystem() { beltMotor = new Talon(Constants.Hardware.PWM_BELT); } public void run(double speed) { beltMotor.set(speed); } public void stop() { run(0); } }

## Slide 20
BeltInCommand Runs the Belt
package frc.robot.commands; import edu.wpi.first.wpilibj2.command.Command; import frc.robot.Constants; import frc.robot.subsystems.BeltSubsystem; // Presentation excerpt: open BeltInCommand.java in VS Code for the full // required NAME, DESCRIPTION, PARAMETERS, and RETURNS comments. public class BeltInCommand extends Command { private final BeltSubsystem beltSubsystem; public BeltInCommand(BeltSubsystem beltSubsystem) { this.beltSubsystem = beltSubsystem; addRequirements(beltSubsystem); } @Override public void execute() { beltSubsystem.run(Constants.Tuning.BELT_SPEED); } @Override public void end(boolean interrupted) { beltSubsystem.stop(); } @Override public boolean isFinished() { return false; } }

## Slide 21
RobotContainer Connects Buttons to Commands
public class RobotContainer { // Presentation excerpt: controllers and subsystems are created once in // the constructor. Open RobotContainer.java in VS Code for full comments. /** NAME: configureBindings - maps controller buttons to commands. */ private void configureBindings() { operatorController.y() .onTrue(new ToggleClimberArmsCommand(climberSubsystem)); operatorController.a() .whileTrue(new BeltInCommand(beltSubsystem)); operatorController.b() .whileTrue(new BeltOutCommand(beltSubsystem)); operatorController.x() .whileTrue(new RollerCommand(rollerSubsystem)); driverController.rightBumper() .whileTrue(new SlowDriveCommand(driveSpeedMode)); } }

## Slide 22
Button A Across the Java Files
BUTTON A CODE TRACE 1. RobotContainer.java binds operatorController.a().whileTrue(...) to a BeltInCommand. 2. BeltInCommand.java calls addRequirements(beltSubsystem) in its constructor. 3. Robot.java calls CommandScheduler.getInstance().run() from robotPeriodic(). 4. While Button A is held, BeltInCommand.execute() calls beltSubsystem.run(Constants.Tuning.BELT_SPEED). 5. BeltSubsystem.java sends that output to the Talon on Constants.Hardware.PWM_BELT (PWM Port 5).

## Slide 23
Trace Another Control
BUTTON A Trace a press from the physical controller to PWM Port 5, then trace the release back to zero output.
BUTTONS A + B Trace what happens when both belt buttons are held. Identify the scheduled command and subsystem owner.
BUTTON Y Compare onTrue(ToggleClimberArmsCommand) with the belt's whileTrue binding and lifecycle.
BUTTON X Diagnose a roller that does not run by checking Driver Station USB assignment, binding, command, and PWM Port 4.

## Slide 24
PWM and CAN Motor Control
Feature / Dimension | PWM Signal (Standard Talons) | CAN Bus (Talon SRX / CANSparkMax) | Robot Application
Wiring Topology | Point-to-point 3-pin cable from roboRIO | Daisy-chained 2-wire bus across entire robot | CAN reduces roboRIO wiring clutter
Feedback & Telemetry | One-way command signal (0V to 5V pulse) | Bi-directional (Current, Voltage, RPM, Encoder) | CAN enables closed-loop PID control
WPILib Class | edu.wpi.first.wpilibj.motorcontrol.Talon | com.ctre.phoenix.motorcontrol.can.WPI_TalonSRX | 2020 codebase uses PWM Talons for simplicity
Configuration | PWM channel number (0..5) | CAN Device ID (0..63) | Constants.java stores port mapping