## Slide 1
NEW PROGRAMMER ONBOARDING
2020 Robot Code
Learn the main robot concepts, using one operator action to connect them.
DRIVE
BELT
ROLLER
CLIMBER
The goal is understanding the current implementation—not memorizing Java.
V2 • shared core + two experience tracks
Notes: Talk track Start with the physical robot, not the codebase. Ask students to name anything the robot can make move. Accept informal answers. Set the expectation: newcomers only need to recognize the path; experienced students should watch for design decisions and failure modes. Nobody needs to understand every Java symbol on first sight. Presenter choice If a current robot photo is available, replace the abstract mechanism labels with that photo and label the four mechanisms. Do not use a historical robot photo.

## Slide 2
SHARED CORE
Four parts of the robot system
02
HARDWARE
motors, solenoids, sensors
SUBSYSTEMS
software that owns hardware
COMMANDS
software that describes actions
SCHEDULER
software that runs commands
An operator action travels through the scheduler, command, subsystem, and hardware.
LOOK FOR
The rest of the deck builds this path one part at a time.
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track: This course follows four parts of one robot system. Hardware is the physical robot. Subsystems own and operate hardware. Commands describe robot actions. The scheduler starts, runs, and ends commands.
Transition: First, identify the robot's physical mechanisms. Then trace how software reaches them.

## Slide 3
SHARED CORE
What this robot does
03
DRIVETRAIN
Move + steer
BELT
Move game pieces
ROLLER
Eject game pieces
CLIMBER
Change arm position
Each independently controlled mechanism becomes a software boundary.
LOOK FOR
By the end of presentation, match every physical mechanism to one subsystem.
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Point to the real mechanisms if the robot is present. A subsystem is not just a folder or class name; it represents an independently controlled mechanism. Depth option The drivetrain owns four motors but is one subsystem because all four cooperate to create one independently scheduled behavior. The belt and roller are separate because each can run without the other.

## Slide 4
SHARED CORE
Controls are the starting point
04
DRIVER • USB 0
Sticks
drive + steer
Right bumper
slow mode
OPERATOR • USB 1
A held
belt in
B held
belt out
X held
roller
Y pressed
toggle climber
KEY IDEA
Every software path begins with a physical action we want the robot to perform.
Source: RobotContainer.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Keep this physical. Ask students to mime or point to the input and describe the expected motion. Do not yet explain commands, suppliers, or trigger objects. Those names arrive only after students understand the behavior. Experienced extension Ask why the climber uses a press event while the motors use held events. Listen for “one change” versus “continuous output.”

## Slide 5
SHARED CORE
Trace a Button Press
05
1 Operator holds A
2 Belt starts
3 Belt keeps moving
4 Release stops it
operatorController.a()
.whileTrue(new BeltInCommand(beltSubsystem));
While button A is held, run the belt-in action using the belt mechanism.
CHECK
Which controller button starts this behavior?
Source: RobotContainer.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Reveal the behavior sequence first. Then reveal the two lines of code. Read the code as a sentence; do not decode punctuation yet. Beginner answer The operator controller A button. Experienced extension whileTrue matches a behavior that must continue only while the operator holds the button. onTrue would schedule only on the rising edge; whether it kept running would then depend on command completion/cancellation behavior.

## Slide 6
SHARED CORE
The triggered command runs this code
06
beltSubsystem.run(Constants.Tuning.BELT_SPEED);
beltSubsystem
the belt object
.run
the requested action
(BELT_SPEED)
the supplied value
;
statement ends
You can recognize structure before you can write it.
READ IT
Ask the belt subsystem to run at the configured belt speed.
Source: BeltInCommand.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Point left to right. Say object, action, value, stop. Avoid teaching Java grammar beyond what is needed to read this line. Depth option Constants.Tuning.BELT_SPEED is a static named value. Defer the full Constants organization discussion until students see a hardware ID in context later.

## Slide 7
SHARED CORE
How does all this get run?
07
@Override
public void robotPeriodic() {
CommandScheduler.getInstance().run();
}
CHECK
controller triggers
START
new commands
RUN
active commands
END
finished / interrupted
PREDICT
What stops working if CommandScheduler.run() is never called?
Source: Robot.java
CURRENT ROBOT IMPLEMENTATION • V2
robotPeriodic is run every 20 ms
the scheduler is run from robotPeriodic
The scheduler is the robot's traffic controller
Notes: Talk track This is the central runtime loop. WPILib calls robotPeriodic repeatedly, and the scheduler uses each pass to update the command-based system. Beginner answer Bindings are not checked and scheduled commands do not receive lifecycle calls, so command-based robot actions do not run normally. Experienced extension The scheduler also enforces subsystem requirements. That conflict resolution is the reason requirements appear early in this deck.

## Slide 8
SHARED CORE
Mechanisms become subsystems
08
DriveSubsystem
DRIVETRAIN
BeltSubsystem
BELT
RollerSubsystem
ROLLER
ClimberSubsystem
CLIMBER
A subsystem is the software class responsible for one independently controlled mechanism.
PREDICT
Which subsystem should own the belt motor and call beltMotor.set(...)?
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track
The physical mechanisms on slide 2 become these four software classes. The word Subsystem is a naming convention. The boundary matters because each class has one mechanism to own and operate.
Transition
Now zoom in on BeltSubsystem. We will see the motor-controller object it owns and the hardware call it makes.
Depth option
Subsystem requirements also help the scheduler prevent conflicting commands. That idea comes after commands and subsystem responsibilities are clear.

## Slide 9
SHARED CORE
Subsystem Example - BeltSubsystem
09
public BeltSubsystem() {
beltMotor = new Talon(Constants.Hardware.PWM_BELT);
}
public void run(double speed) {
beltMotor.set(speed);
}
OWNS
the Talon motor-controller object
NAMES
a mechanism action: run(speed)
TOUCHES HARDWARE
beltMotor.set(speed)
CHECK
Which line actually changes motor output?
Source: BeltSubsystem.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Yes: the subsystem is where this program directly interacts with mechanism hardware. It creates the motor object and calls its API. Clarification Not every subsystem must own physical hardware; some designs use logical subsystems. In this robot, the useful beginner model is: subsystem owns one independently controlled mechanism and contains its direct hardware calls. Beginner answer beltMotor.set(speed). Experienced extension If commands created their own Talon objects, ownership would be duplicated and port changes, safety behavior, simulation, and testing would become harder to control.

## Slide 10
SHARED CORE
Commands decide what happens—and when
10
public void execute() {
beltSubsystem.run(Constants.Tuning.BELT_SPEED);
}
public void end(boolean interrupted) {
beltSubsystem.stop();
}
execute()
request motion
end(...)
request safe stop
The command never knows the PWM port.
KEY IDEA
Command = intent + timing. Subsystem = mechanism operation.
Source: BeltInCommand.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Remember back to slide - Trace a Button Press – that shows a command being run when a button was pressed
Contrast this with the prior slide. The command says “run inward now” and “stop when I end.” The subsystem knows how to achieve those requests. Depth option end runs on both normal completion and interruption. This while-held command is normally canceled when the trigger becomes false, so the safe-stop path matters every time the operator releases A.

## Slide 11
SHARED CORE
Requirements prevent two owners at once
11
public BeltInCommand(BeltSubsystem beltSubsystem) {
this.beltSubsystem = beltSubsystem;
addRequirements(beltSubsystem);
}
BELT IN
requires BeltSubsystem
BELT SUBSYSTEM
one scheduled owner
BELT OUT
requires BeltSubsystem
scheduler resolves the conflict
RULE
Add every subsystem whose controlled hardware/state the command acts on.
Source: BeltInCommand.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Requirements are scheduler ownership claims. When a new interruptible command with the same requirement starts, the scheduler interrupts the old command and schedules the new one. Do all commands need addRequirements? No. Hardware-owning commands normally require each subsystem they control. A command that changes only coordination state may have no subsystem requirement. Current example DriveTeleop, BeltIn, BeltOut, Roller, and ToggleClimberArms declare their subsystems. SlowDriveCommand intentionally does not require DriveSubsystem because it only changes DriveSpeedMode. If it required the drivetrain, it would interrupt the default drive command, so the robot could not actually drive slowly while held.

## Slide 12
SHARED CORE
Bindings connect an input to an action
12
operatorController.a()
.whileTrue(new BeltInCommand(beltSubsystem));
operatorController.b()
.whileTrue(new BeltOutCommand(beltSubsystem));
WHEN
WHAT
WHO
button trigger
command
subsystem
TRACE
Release makes whileTrue cancel the command; end() stops the motor.
Source: RobotContainer.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Use the three questions: When should something happen? What action should run? Which mechanism will it use? Depth option The trigger is polled by the scheduler. whileTrue maintains scheduling while true and cancels when false. The command’s requirement makes that scheduling safe.

## Slide 13
SHARED CORE
The complete belt path
13
1
A HELD
binding
2
SCHEDULER
starts command
3
EXECUTE
run(speed)
4
SUBSYSTEM
motor.set
5
PWM
belt moves
6
RELEASE
end → stop
framework
team-written code
ACTIVITY
Tell the story left to right without reading the code.
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Have students narrate the six stages. If they use informal language, translate it back to the role vocabulary after they finish. Framework vs team code WPILib owns trigger polling, scheduling, lifecycle calls, requirement conflict handling, and PWM communication. The team wrote the binding, command behavior, subsystem method, constants, and stop logic. Optional activity Print the six stages, cut them apart, and have small groups arrange them.

## Slide 14
SHARED CORE
Subsystems separate—and sometimes cooperate
14
DRIVE
4 motors
BELT
1 motor
ROLLER
1 motor
CLIMBER
2 solenoids
different requirements → can run together
DESIGN
A combined scoring command would require both BeltSubsystem and RollerSubsystem.
Source: RobotContainer.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track The program is broken into separate subsystems according to independently controlled mechanisms. Commands link that decomposition to behavior: a command requires and operates one or more subsystem objects. Cooperation Separate commands with different requirements may run concurrently. One coordinated command or command group may require multiple subsystems and sequence or parallelize their actions. Why belt and roller are separate Either can run by itself. Keeping them separate preserves independent scheduling and reuse.

## Slide 15
SHARED CORE
Shared-core checkpoint
15
1 Who directly calls beltMotor.set()?
2 Who decides the belt runs inward?
3 What connects A to that action?
4 What repeatedly runs command lifecycles?
5 Why can drive and belt run together?
BEGINNER
trace the five roles
EXPERIENCED
predict conflicts
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Suggested answers 1. BeltSubsystem. 2. BeltInCommand. 3. The RobotContainer trigger binding. 4. CommandScheduler, called by robotPeriodic. 5. Their commands require different subsystems. Facilitation Use answers to select tracks. A beginner does not need perfect terminology if they can tell the direction of flow. An experienced student should explain interruption and concurrency, not merely name classes.

## Slide 16
BEGINNER TRACK
Project map: where each role lives
16
frc.robot
Robot.java
RobotContainer.java
Constants.java
commands/
subsystems/
@Override
public void robotInit() {
robotContainer = new RobotContainer();
autonomousMode = new AutonomousMode(robotContainer);
}
Robot
lifecycle + scheduler
RobotContainer
objects + bindings
folders
actions vs hardware
FIND IT
Open RobotContainer.java and locate subsystem construction.
Source: Robot.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Treat the map as navigation, not architecture to memorize. Show students how file names repeat the vocabulary they already know. Depth option RobotContainer is the composition root for this program: it constructs shared objects and connects triggers to commands. Robot owns the WPILib lifecycle entry points.

## Slide 17
BEGINNER TRACK
Constants make sense when hardware needs one
17
public static final int PWM_FRONT_LEFT_DRIVE = 0;
leftDriveLeader = new Talon(Constants.Hardware.PWM_FRONT_LEFT_DRIVE);
HARDWARE
PWM_FRONT_LEFT_DRIVE = 0
OPERATOR
DRIVER_CONTROLLER = 0
TUNING
DRIVE_DEADBAND = 0.08
WHY HERE?
The name records meaning; the subsystem no longer repeats a mystery number.
Sources: Constants.java; DriveSubsystem.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track This is the right moment for Constants: students have already followed behavior, and now they see a real hardware constructor that needs a port number. Avoid teaching Constants as a junk drawer. The nested groups distinguish hardware connections, operator ports, and tunable behavior values. Important hardware fact These Talon objects use roboRIO PWM port numbers. The pneumatic module is the CAN device; the drive Talons are not vendor CAN motor controllers.

## Slide 18
BEGINNER TRACK
The drivetrain owns four motors
18
leftDriveLeader = new Talon(PWM_FRONT_LEFT_DRIVE);
Talon leftDriveFollower = new Talon(PWM_BACK_LEFT_DRIVE);
rightDriveLeader = new Talon(PWM_FRONT_RIGHT_DRIVE);
Talon rightDriveFollower = new Talon(PWM_BACK_RIGHT_DRIVE);
leftDriveLeader.addFollower(leftDriveFollower);
rightDriveLeader.addFollower(rightDriveFollower);
rightDriveLeader.setInverted(true);
LEFT LEADER
LEFT FOLLOWER
RIGHT LEADER
RIGHT FOLLOWER
right side inverted
NOTICE
Follower support is standard WPILib for these PWM Talons.
Source: DriveSubsystem.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track The subsystem creates four PWM Talon objects. Each rear motor follows the leader on its side, so later code sends only left and right values. Why not the old two-motor wrapper? The local DualMotorController was a compatibility expedient after WPILib removed the older SpeedControllerGroup API. It was never removed and later brought back; it was introduced once. The current implementation instead uses WPILib’s standard PWM follower support, which better communicates the intent to students. Clarify follower modes This is WPILib software follower behavior for PWM controllers, not vendor CAN follower configuration.

## Slide 19
BEGINNER TRACK
The subsystem exposes a drivetrain action
19
public void drive(double leftSpeed, double rightSpeed) {
leftDriveLeader.set(leftSpeed);
rightDriveLeader.set(rightSpeed);
}
LEFT SPEED
RIGHT SPEED
drive(left, right)
LEFT LEADER
RIGHT LEADER
LEFT FOLLOWER
RIGHT FOLLOWER
Each request controls one side; each follower mirrors its leader.
PREDICT
Which class should call drive() during teleoperated control?
Source: DriveSubsystem.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Beginner answer DriveTeleopCommand. Talk track The method receives two independent inputs at the same time: one requested speed for the left side and one for the right. It sends each value to the matching leader. WPILib then sends each leader value to its registered follower. The caller does not know ports or individual rear motors. Depth option Keeping inversion in the subsystem means every caller sees the same logical direction convention.

## Slide 20
BEGINNER TRACK
A default command runs when no other command requires the subsystem
20
driveSubsystem.setDefaultCommand(
new DriveTeleopCommand(
driveSubsystem,
this::getLeftDriveValue,
this::getRightDriveValue,
driveSpeedMode));
DRIVETRAIN FREE
scheduler selects default
DRIVE TELEOP
reads current stick values
OTHER DRIVE COMMAND
interrupts the default
KEY IDEA
Default does not mean “runs once”; it fills otherwise unused subsystem time.
Source: RobotContainer.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track The scheduler automatically schedules the default when no other command requires DriveSubsystem. Suppliers let DriveTeleop read fresh stick values each scheduler cycle. Depth option When another drive command ends, the scheduler can restore the default command automatically. For example if we had a command to drive to a specific spot that would supersede the default command and then when it finished the default command would resume

## Slide 21
BEGINNER TRACK
Drive input follows the same five-role path
21
private double getLeftDriveValue() {
return -MathUtil.applyDeadband(
driverController.getLeftY(),
Constants.Tuning.DRIVE_DEADBAND);
}
driveSubsystem.drive(
scale(leftDriveSupplier.getAsDouble()),
scale(rightDriveSupplier.getAsDouble()));
STICK
DEADBAND
SCALE
DRIVE
MOTORS
TRY IT
Find the matching right-stick method; predict a NORMAL_DRIVE_SCALE change.
Sources: RobotContainer.java; DriveTeleopCommand.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Guided activity Have students circle the controller read, the deadband constant, the scale call, and the subsystem call. Then locate getRightDriveValue. Before changing code Ask for a physical prediction. Lowering NORMAL_DRIVE_SCALE reduces requested output in normal mode. Make the edit only with instructor supervision and test with the robot safely raised or in simulation.

## Slide 22
EXPERIENCED TRACK
Slow mode changes state, not drivetrain ownership
22
NORMAL_DRIVE_SCALE = 0.8
SLOW_DRIVE_SCALE = 0.4
DRIVE_DEADBAND = 0.08
public void initialize() {
driveSpeedMode.setSlow(true);
}
public void end(boolean interrupted) {
driveSpeedMode.setSlow(false);
}
DriveTeleopCommand
keeps DriveSubsystem requirement
SlowDriveCommand
changes shared mode; no requirement
DESIGN REVIEW
Why would requiring DriveSubsystem make slow driving fail?
Sources: Constants.java; SlowDriveCommand.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Answer If SlowDriveCommand required DriveSubsystem, pressing the bumper would interrupt the default DriveTeleopCommand and reserve the drivetrain while producing no motor output. DriveTeleop could not read the slow flag while held. On release, SlowDrive would restore normal mode before the default resumed—so slow driving would never occur. Tradeoff discussion The shared DriveSpeedMode object keeps input binding separate from drive execution. Reading the bumper directly in DriveTeleop would reduce indirection but couple the command to that operator choice.

## Slide 23
EXPERIENCED TRACK
Simple motor mechanisms reuse one pattern
23
public RollerSubsystem() {
rollerMotor = new Talon(Constants.Hardware.PWM_ROLLER);
}
public void run(double speed) {
rollerMotor.set(speed);
}
public void stop() {
run(0);
}
CONSTRUCT
own hardware
RUN
set output
STOP
return to zero
Belt + roller stay separate, so they can run together.
CHALLENGE
Use requirements alone to list which drive, belt, and roller commands can coexist.
Source: RollerSubsystem.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track This repeated pattern is a useful template for a similar robot: construct owned hardware, expose mechanism actions, and provide an explicit safe stop. Concurrency answer DriveTeleop can run alongside a belt command and RollerCommand because they require different subsystems. BeltIn and BeltOut conflict with each other. Multiple commands requiring RollerSubsystem would conflict with RollerCommand.

## Slide 24
EXPERIENCED TRACK
Pneumatics use the same boundary, different hardware
24
public void extendArms() {
leftClimberSolenoid.set(SOLENOID_LEFT_OUT);
rightClimberSolenoid.set(SOLENOID_RIGHT_OUT);
armsExtended = true;
}
public void initialize() {
climberSubsystem.toggleArms();
}
ONE MECHANISM
two solenoids cooperate
ONE-SHOT COMMAND
initialize → toggle → finish
ASSUMED STATE
armsExtended starts false
SAFETY REVIEW
How could software learn the real arm position?
Sources: ClimberSubsystem.java; ToggleClimberArmsCommand.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track The command-based split is unchanged even though the hardware API is pneumatic. The subsystem owns both solenoids because they act together as one mechanism. Safety discussion The boolean is a software belief, not a measurement. Possible feedback includes limit switches, reed sensors, pressure/position sensing, or a known homing procedure. The correct choice depends on the actual mechanism and safety analysis.

## Slide 25
EXPERIENCED TRACK
Coordination means declaring every participant
25
operatorController.a()
.whileTrue(new BeltInCommand(beltSubsystem));
operatorController.x()
.whileTrue(new RollerCommand(rollerSubsystem));
CURRENT
two independent controls
PROPOSED SCORE
one coordinated lifecycle
REQUIRES BOTH
belt + roller ownership
DESIGN TASK
Define start, finish, stop, interruption, and requirements before writing code.
Source: RobotContainer.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track The present design lets operators compose behavior manually. A combined scoring command could run both mechanisms in parallel or sequence them. Questions to settle first Does the roller start immediately or after the belt? Does the action run while held, for a duration, or until a sensor changes? On interruption, both mechanisms must stop. The command or group must require BeltSubsystem and RollerSubsystem so independent commands cannot take either mechanism during the action.

## Slide 26
EXPERIENCED TRACK
Tests verify requests without robot hardware
26
command.execute();
command.end(false);
Mockito.verify(beltSubsystem)
.run(Constants.Tuning.BELT_SPEED);
Mockito.verify(beltSubsystem).stop();
ARRANGE
create command + mock
ACT
execute + end
ASSERT
run + safe stop requested
EXTEND IT
A combined-score test should verify both mechanisms start and stop.
Source: TeleopCommandsTest.java
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track The test checks the command-to-subsystem contract. Mockito stands in for the subsystem, so no roboRIO or motor controller is needed. Experienced extension Test normal completion and interruption. Verify both run requests and both stop requests. Then reason about scheduler-level conflicts separately or add a scheduler integration test if the command composition warrants it.

## Slide 27
SHARED CORE
Build a similar robot in this order
27
1 List mechanisms + operator actions
2 Make one subsystem per independent mechanism
3 Put direct hardware calls in the subsystem
4 Add small actions: run, stop, drive
5 Create commands + requirements
6 Bind controls in RobotContainer
7 Run the scheduler in robotPeriodic
8 Name ports + tuning values in Constants
9 Test command requests
10 Verify direction, stops, and real starting state
REJOIN
Beginner traces one action; experienced student explains one design choice plainly.
CURRENT ROBOT IMPLEMENTATION • V2
Notes: Talk track Use this as the team’s implementation checklist. It starts with behavior and ownership, then introduces framework wiring, organization, tests, and physical verification. Rejoin activity Pair students across tracks. The beginner traces one existing action through binding, scheduler, command, subsystem, and hardware. The experienced student explains one scheduler or design decision without assuming Java knowledge. Each pair proposes one safe, testable modification. Final caution Simulation and unit tests reduce risk but do not prove motor direction, pneumatic plumbing, mechanism interference, or real starting position. Perform controlled hardware verification with the team’s safety process.